## Slide 1: 5G NR Advanced Training

## Slide 2: Contents
Module 1: 4G-5G RAN System Description
• 1.1 Overview of 4G LTE and 5G NR
o Evolution from 4G to 5G technologies
o System architecture and components of 4G-5G RAN
• Interworking of 4G and 5G RAN
o Coexistence and interoperation strategies
o Dual-connectivity solutions

## Slide 3: Overview of 4G LTE and 5G NR

## Slide 4
4G LTE-Advanced
Designed for People & Mobile Broadband
Monolithic Architecture
Enhanced Mobile Broadband
Single Service Category
• High-speed mobile internet
• Smartphones & tablets focus
• Up to 1 Gbps peak speeds
Primary Use Cases
Phone
Tablet
Video
Technical Specifications
• Latency: 10-50ms
• Peak Speed: 1 Gbps
• Frequency: Sub-6 GHz
• Device Density: 100,000/km²
• Energy Efficiency: Baseline
• Network Slicing: Limited
5G New Radio (NR)
Designed for Everything (People, Machines, Industry)
Flexible Service-Based Architecture
eMBB
Enhanced Mobile
Broadband
4K/8K Video, AR/VR
URLLC
Ultra-Reliable
Low-Latency
Autonomous, Surgery
mMTC
Massive Machine
Type Communications
IoT, Smart Cities
Network Slicing Architecture
eMBB Slice
URLLC Slice
mMTC Slice
Diverse Use Cases
VR/AR
Auto Car
Industry
IoT
Smart City
Advanced Technical Specifications
• Latency: <1ms (URLLC)
• Peak Speed: 20 Gbps
• Frequency: Sub-6 GHz + mmWave
• Beamforming: Advanced MIMO
• Device Density: 1M/km²
• Energy Efficiency: 100x better
• Network Slicing: Full support
• Edge Computing: Native
Paradigm Shift
Fundamental Transformation
From single-purpose mobile broadband
to multi-service connectivity platform
enabling Society 5.0 and Industry 4.0
Key Technical Differences: 4G (LTE-Advanced) vs. 5G (NR)

## Slide 5
4G EPC (Evolved Packet Core)
Hardware-Based • Rigid Architecture • Dedicated Appliances
Physical Hardware Infrastructure
MME
Mobility Management
Entity
Dedicated Hardware
S-GW
Serving Gateway
Dedicated Hardware
P-GW
PDN Gateway
Dedicated Hardware
HSS
Home Subscriber
Server
Dedicated Hardware
PCRF
Policy Control &
Charging Rules
Dedicated Hardware
OCS
Online Charging
System
Dedicated Hardware
EPC Limitations
• Fixed hardware-based network functions
• Limited scalability and flexibility
• Single service type optimization
• No network slicing capability
• Monolithic architecture
• Vendor lock-in issues
• Difficult to upgrade/modify
• High CAPEX/OPEX costs
5G Core (5GC)
Cloud-Native • Service-Based Architecture • Network Slicing
Cloud-Native Infrastructure (VNFs/CNFs)
Service-Based Architecture (SBA)
AMF
Access & Mobility
Software VNF
SMF
Session Management
Software VNF
UPF
User Plane
Software VNF
UDM
Unified Data Mgmt
Software VNF
PCF
Policy Control
Software VNF
AUSF
Authentication
Software VNF
NRF
NF Repository
Software VNF
API-Based Communication
Network Slicing - Multiple Virtual Networks
eMBB Slice
High Bandwidth | Medium Latency
URLLC Slice
Ultra-Low Latency | High Reliability
mMTC Slice
Low Power | Massive Connectivity
Isolated Virtual Network
Isolated Virtual Network
Isolated Virtual Network
5GC Advantages
• Cloud-native virtualized functions (VNFs/CNFs)
• Service-based architecture with APIs
• Dynamic scaling and programmability
• Multiple service support via network slicing
• Vendor-agnostic and interoperable
• Reduced CAPEX/OPEX costs
• Edge computing integration
• Rapid innovation and deployment
Core Network Architecture: 4G EPC vs 5G Core

## Slide 6
Latency Revolution: 4G vs 5G Technical Architecture
Latency Performance Comparison
4G: 30-50ms
4G
<1ms
5G
50x Improvement
Impact: Enables real-time control, autonomous vehicles, remote surgery, industrial automation
Three Key Technical Innovations
Flexible Numerology
Mini-slots & Dynamic TTI
Ultra-fast transmission
Edge Computing
MEC Integration
Reduced round-trip time
Streamlined Protocol
Optimized Stack
Reduced processing
Innovation 1: Flexible Numerology
4G LTE: Fixed 1ms TTI
1ms slots (fixed)
5G NR: Variable TTI + Mini-slots
Mini-slots (0.125-0.5ms)
Standard slots
URLLC: Ultra-fast mini-slots enable <1ms latency
Innovation 2: Edge Computing Integration (MEC)
4G: Centralized Cloud Processing
UE
Long Round-trip: 30-50ms
Cloud
5G: Multi-access Edge Computing (MEC)
UE
<1ms
MEC
Cloud
Optional
Innovation 3: Streamlined Protocol Stack
4G LTE Stack
Application
IP
PDCP
RLC
MAC
PHY
Multiple processing steps
Complex header handling
Legacy overhead
5G NR Stack
Application
IP
PDCP/RLC
MAC
PHY
Optimized processing
Reduced overhead
Streamlined headers
Hardware acceleration
Real-World Impact: Applications Enabled by Ultra-Low Latency
Autonomous Vehicles
Split-second decisions
Remote Surgery
Haptic feedback
Industrial Robots
Real-time control
AR/VR
Immersive experience
Smart Grid
Instant response
Cloud Gaming
Zero lag experience
5G's sub-millisecond latency transforms networks from human-centric to machine-centric infrastructure
Enabling real-time applications that were impossible with previous generations

## Slide 7
Spectrum Revolution: 4G vs 5G Frequency Usage & Bandwidth
Electromagnetic Spectrum Utilization
600 MHz
2.6 GHz
6 GHz
24 GHz
52 GHz
4G Range
5G FR1 (Sub-6 GHz)
5G FR2 (mmWave)
4G LTE Spectrum (Sub-6 GHz Only)
Frequency Range: 600 MHz - 2.6 GHz
Band 12
700 MHz
Band 2
1900 MHz
Band 7
2600 MHz
Band 41
2500 MHz
Bandwidth Limitations:
Maximum: 20 MHz per carrier
Carrier Aggregation: Up to 5 carriers = 100 MHz total
Peak Theoretical Speed: ~1 Gbps (with carrier aggregation)
Typical Real-world: 50-150 Mbps
5G NR Spectrum (Multi-band Approach)
FR1 (Sub-6 GHz): 450 MHz - 6 GHz
n71: 600MHz
n41: 2.5GHz
n78: 3.5GHz
Coverage: Wide area | Speed: 100 Mbps - 4 Gbps
Bandwidth: Up to 100 MHz per carrier
FR2 (mmWave): 24 GHz - 71 GHz
n257: 28GHz
n260: 39GHz
n261: 28GHz
Coverage: Short range | Speed: 1-20 Gbps
Bandwidth: 100-400 MHz per carrier
5G Peak Theoretical Speeds
FR1: Up to 4 Gbps
FR2: Up to 20 Gbps
Combined theoretical maximum: 20+ Gbps (100x faster than 4G)
Coverage vs Speed Trade-off Analysis
4G Coverage
Range: 5-30 km | Speed: 50-150 Mbps
5G FR1 Coverage
Range: 1-10 km | Speed: 100 Mbps - 4 Gbps
5G FR2 Coverage
Range: 200-500m | Speed: 1-20 Gbps
Wall
Tree
Blocked
Optimal Use Cases by Frequency Band
4G Sub-6 GHz
• Wide area mobile broadband
• Voice calls and messaging
• Video streaming (HD)
5G FR1 Sub-6 GHz
• Enhanced mobile broadband
• 4K/8K video streaming
• IoT and smart cities
5G FR2 mmWave
• Ultra-high-speed hotspots
• Stadium/venue connectivity
• Industrial automation
5G Hybrid Deployment
• Seamless handover
• Coverage + Capacity
• Future-ready networks
Spectrum Evolution: From Limited Sub-6 GHz to Comprehensive Multi-band Architecture

## Slide 8
Radio Access & Antenna Technology Evolution: 4G MIMO vs 5G Massive MIMO
4G LTE Radio Access & MIMO Technology
Fixed OFDMA • Limited Antennas • Omnidirectional Coverage
4G Radio Access: Fixed OFDMA
Subcarrier Spacing: Fixed 15 kHz
15 kHz spacing (rigid structure)
Limitations:
• Single numerology (15 kHz only)
• Not optimized for diverse services
• Limited flexibility
• Higher latency for URLLC
4G MIMO: 2x2, 4x4, or 8x8 Antenna Configuration
Base Station
8 Antennas (Maximum)
Omnidirectional Coverage
User 1
User 2
User 3
Signal Characteristics:
• Broadcasting in all directions
• Signal interference between users
• Limited spatial multiplexing
• Energy waste in unused directions
• Reduced spectral efficiency
5G NR Radio Access & Massive MIMO Technology
Flexible OFDMA • Massive Arrays • Precision Beamforming
5G Radio Access: Flexible OFDMA with Multiple Numerologies
Variable Subcarrier Spacing: 15 kHz - 120 kHz
15 kHz (Coverage)
30 kHz (Balanced)
120 kHz (URLLC)
Advantages:
• Service-specific optimization
• Dynamic adaptation
• Ultra-low latency support
• Improved spectral efficiency
5G Massive MIMO: 32, 64, 128+ Antenna Arrays with Beamforming
Base Station
128+ Antenna Array
User 1
Beam 1
User 2
Beam 2
User 3
Beam 3
Beamforming Benefits:
• Focused signal energy
• Reduced interference
• Higher signal quality
• Increased capacity
• Energy efficiency
• Spatial multiplexing
Technical Comparison: MIMO vs Massive MIMO
Aspect
4G MIMO
5G Massive MIMO
Improvement Factor
Antenna Count
2-8 antennas
32-128+ antennas
16x-64x more
Signal Precision
Omnidirectional
Precision beamforming
10x better targeting
Spectral Efficiency
30 bps/Hz
100+ bps/Hz
3-5x improvement
Energy Efficiency
Baseline
100x better per bit
100x improvement
Concurrent Users
Tens per cell
Hundreds per cell
10x more users
Key Enabling Technologies
Advanced DSP
• Real-time beamforming
• Channel estimation
• Interference cancellation
AI/ML Optimization
• Predictive beamforming
• Dynamic optimization
• User behavior prediction
Hardware Innovation
• Miniaturized antennas
• Low-power RF chains
• Massive arrays
Network Intelligence
• Self-organizing networks
• Adaptive algorithms
• Resource optimization
Cloud RAN
• Centralized processing
• Flexible deployment
• Cost optimization
The Antenna Revolution: From Broadcasting to Precision Targeting
Massive MIMO transforms wireless from "spray and pray" to surgical precision, enabling unprecedented capacity and efficiency

## Slide 9: System architecture and components of 4G-5G RAN

## Slide 10
5G Core Network: Key Design Principles & Paradigm Shifts
1. Service-Based Architecture (SBA)
4G EPC (Legacy)
MME
SGW
PGW
S1
S11
Point-to-Point Interfaces
Rigid • Protocol-Specific
Hard to Add New Services
Evolution
5G Core - Service-Based Architecture
Network Functions (NFs):
AMF
SMF
UDM
PCF
Service Bus (HTTP/2 + REST APIs)
Key Benefits:
• Microservices Architecture
• Standardized APIs (HTTP/2 + JSON)
• Modular & Scalable
• Easy to Add New Services
💡 Analogy: Web Services
NFs communicate like web services - they don't need to
know each other's internal workings, just how to call
the right API for the service they need.
2. Control & User Plane Separation (CUPS)
Control Plane (CP)
"THE BRAIN"
AMF
SMF
PCF
Signaling • Management
Decision Making • Authentication
Centralized Location
SEPARATED
User Plane (UP)
"THE WORKHORSE"
UPF
User Data Traffic
Video • Web • Streaming
Distributed • Edge Deployment
🎯 CUPS Benefits
✓ Reduced Latency:
UPF can be placed at network edge (factories, city centers)
✓ Flexible Scaling:
Scale CP and UP independently based on traffic demands
✓ Cost Optimization:
Deploy UP functions only where needed
✓ Service Innovation:
Enable edge computing and ultra-low latency services
🏭 Use Case:
Factory automation, AR/VR, autonomous vehicles
3. Cloud-Native Design
Virtualized/Containerized
Docker
K8s
VM
• Run on Cloud Infrastructure
• Private/Public/Hybrid Cloud
• Kubernetes Orchestration
• Dynamic Scaling
• Resource Optimization
Stateless Design
NF
Instance
state
UDR
Central Store
NF
Instance
state
Session state stored centrally
Any instance can handle any request
🚀 Cloud-Native Benefits & Capabilities
🔄 High Resilience:
• NF instance fails → Another takes over instantly
• No session data lost (stored in UDR)
📈 Dynamic Scaling:
• Auto-scale based on traffic demand
• Spin up/down NF instances as needed
💰 Cost Efficiency:
• Pay-as-you-use cloud resources
• Resource sharing across multiple services
🔧 DevOps Integration:
• CI/CD pipelines for rapid deployment
• Infrastructure as Code (IaC)
⚡ Result: Dramatic improvement in resilience, scalability, and operational efficiency

## Slide 11
5G NSA Core Network Architecture
Non-Standalone Architecture with Separated Control/User Planes
UE
User Equipment
Dual Connectivity
Radio Access Network (RAN)
LTE eNodeB
eNB
Master Node (MN)
RRC
PDCP
5G gNodeB
gNB
Secondary Node (SN)
PDCP
RLC/MAC
X2 Interface
EPC (Evolved Packet Core)
Control Plane
MME
Mobility
Management
HSS
Home
Subscriber Server
PCRF
Policy and
Charging
QoS Control
SGW-C
Serving Gateway
Control Plane
PGW-C
PDN Gateway
Control Plane
User Plane
SGW-U
Serving Gateway
User Plane
PGW-U
PDN Gateway
User Plane
IMS
Core
VoLTE
Support
Internet
LTE
EN-DC
S1-MME
S1-U
S6a
S11
S5/S8-C
Sxa
Sxb
S5/S8-U
SGi
Gx
5G NSA Key Characteristics
Dual Connectivity (EN-DC): UE connects to both LTE eNB (master) and 5G gNB (secondary)
Control/User Plane Separation (CUPS): SGW-C/SGW-U and PGW-C/PGW-U interfaces
X2 Interface: Signaling and user-plane coordination between eNB and gNB
VoLTE for Voice: Voice services use VoLTE through IMS core (not VoNR)

## Slide 12
5G Core Service-Based Architecture (SBA)
(3GPP TS 23.501, TS 23.502)
Service-Based Interface (SBI) Bus
HTTP/2 - REST - JSON
AMF
Access and Mobility
Management Function
SMF
Session Management
Function
PCF
Policy Control
Function
NEF
Network Exposure
Function
NRF
Network Repository
Function
UDM
Unified Data
Management
AUSF
Authentication
Server Function
UDR
Unified Data
Repository
NSSF
Network Slice
Selection Function
SMSF
SMS
Function
UPF
User Plane Function
AF
Application Function
gNB
(5G NR)
N2
N3
DN
(Data Network)
N6
External
Application
N4
Reference Point Architecture
Outside the bus: N1, N2, N3, N4, N6
Inside the bus: Namf, Nsmf, Npcf, etc. service-based
Network Slicing Support
• NSSF manages slice selection
• Multiple instances of NFs can be deployed
UE
N1
3GPP References:
• TS 23.501: System Architecture for 5G System
• TS 23.502: Procedures for 5G System
• TS 29.500: Technical Realization of SBI
• TS 29.501: Principles and Guidelines for SBI
Service-Based Interface (SBI) Naming:
• Each NF exposes services with its name prefix (e.g., Namf, Nsmf)
• RESTful APIs with HTTP/2 as transport protocol
• JSON is used for information encoding
• OpenAPI 3.0.0 specifications available in TS 29.5xx series
Items in red indicate key components and interfaces in 5G Service-Based Architecture

## Slide 13
5G CORE NETWORK ARCHITECTURE
Service-Based Architecture (SBA) | ETSI TS 123 501 Standard
Control and User Plane Separation (CUPS) • Stateless Network Functions • Microservices Architecture
UE
User Equipment
• Mobile Devices
• IoT Devices
• Connected Vehicles
(R)AN
Radio Access Network
• 5G gNB (3GPP)
• WiFi AP (Non-3GPP)
• Fixed Access
5G CORE NETWORK (5GC) - SERVICE-BASED ARCHITECTURE
CONTROL PLANE (CP) - STATELESS NETWORK FUNCTIONS
Microservices Architecture • RESTful APIs over HTTP/2 • Cloud-Native Design
AMF
Access & Mobility
Management Function
• UE Registration
• Mobility Control
• N1/N2 Termination
SMF
Session Management
Function
• PDU Session Mgmt
• UE IP Allocation
• UPF Selection
PCF
Policy Control
Function
• Policy Rules
• QoS Control
• Charging Control
NEF
Network Exposure
Function
• API Gateway
• External Access
• 3rd Party Services
AUSF
Authentication
Server Function
• UE Authentication
• Security Context
• Credential Verification
NSSF
Network Slice Selection
Function
• Slice Selection
• NSSAI Management
• Network Slicing
NRF
Network Repository
Function
• Service Discovery
• NF Registry
• Service Directory
UDM
Unified Data
Management
• Subscriber Data
• Authentication Data
• Subscription Info
UDR
Unified Data
Repository
• Database Backend
• Stateful Storage
• Persistent Data
USER PLANE (UP) - STATEFUL FUNCTIONS
High-Performance Packet Processing • Real-Time Data Forwarding
UPF - User Plane Function (Stateful Data Anchor)
Packet Routing • QoS Enforcement • Traffic Steering • Data Network Interconnection
DN
Data Network
• Internet
• Enterprise Networks
• IMS Services
• Local Services
N1
NAS Signalling
N2
CP Signalling
N3
User Plane Traffic
N4
CUPS Critical
N6
Data Network Exit
N11
N8
N10
N12
N22
SBA
Service Bus
REFERENCE POINTS
Control Plane
User Plane
Support Functions
Service Registration
Key Interfaces:
N1: UE ↔ AMF
N2: RAN ↔ AMF
N3: RAN ↔ UPF
N4: SMF ↔ UPF
N6: UPF ↔ DN

## Slide 14
AMF (Access and Mobility Management Function) - Network Interactions
AMF
Access & Mobility
Management Function
• Registration Management
• Connection Management
• Security Anchor (SEAF)
• Mobility Control
UE
User Equipment
• NAS Protocol
• Registration Req
gNodeB
5G Base Station
• RAN Functions
• UE Context Mgmt
SMF
Session Management
• PDU Sessions
• UPF Selection
AUSF
Authentication Server
• UE Authentication
• Security Keys
UDM
Unified Data Mgmt
• Subscription Data
• UE Registration
NSSF
Network Slice Selection
• Slice Selection
• AMF Selection
PCF
Policy Control
• AM Policy
• UE Policy
N1
NAS Protocol
N2
NGAP Protocol
N11
Communication
N12
Authentication
N8
UECM/SDM
N22
NS Selection
N15
AM Policy
Key AMF Functions:
• Registration & Connection Management • Security Anchor (SEAF)
• Mobility Control • NAS Termination • SM Proxy

## Slide 15
SMF (Session Management Function) Overview
Core Control Plane Function for PDU Session Management
SMF
Session Management Function
• PDU Session Lifecycle Management
• Policy Enforcement Point
• UPF Control via N4 Interface
• IP Address Management
Session Management
✓ PDU Session Establishment
✓ Session Modification
✓ Session Release
UE IP Management
✓ IPv4/IPv6 Allocation
✓ Static IP Management
✓ DHCP/DN-AAA Integration
UPF Selection and Control
✓ UPF Selection Logic
✓ N4 Rules Installation
✓ Dynamic UPF Re-selection
Policy and QoS
✓ PCC Rules Translation
✓ QoS Enforcement
✓ Traffic Steering
Downlink Data Management
✓ Data Notification Trigger
✓ UE Paging Coordination
✓ Idle Mode Handling
Charging Support
✓ CHF Integration
✓ Usage Data Collection
✓ Billing Information
SSC Management
✓ SSC Mode 1, 2, 3
✓ Session Continuity
✓ PDU Session Anchor
AMF
Access and Mobility
Management
UPF
User Plane
Function
PCF
Policy Control
Function
CHF
Charging
Function
N11
N4
N7
N40
As per Section 6.2.2
Core SMF Functionalities Specification

## Slide 16
UPF (User Plane Function) Overview
The "Workhorse" of 5G Networks - User Plane Data Processing Engine
Control and User Plane Separation (CUPS) Architecture | Section 6.2.3
UPF
User Plane Function
🔧 Data Processing Workhorse
📊 Packet Routing and Forwarding
🛡️ Policy Enforcement Engine
⚡ QoS and Traffic Management
PDU Session Anchor
✓ Gateway to Data Network
✓ Mobility Anchor Point
✓ IP Address Preservation
Packet Routing
✓ RAN ↔ Data Network
✓ Advanced Forwarding
✓ UL CL / Branching Point
Packet Inspection
✓ Deep Packet Inspection
✓ Application Detection
✓ Traffic Classification
Policy Enforcement
✓ Gating and Blocking
✓ Traffic Redirection
✓ Traffic Steering
QoS Handling
✓ Rate Enforcement
✓ Packet Marking (QFI)
✓ Session-AMBR/MBR
Usage Reporting
✓ Data Volume Collection
✓ Time-based Statistics
✓ Charging and Billing
Downlink Buffering
✓ CM-IDLE State Handling
✓ Data Notification
✓ Paging Trigger
N4 Transport
✓ SMF-UPF Signaling
✓ I-SMF Scenarios
✓ Tunnel Transport
SMF
Control Interface
Master-Slave
RAN
gNodeB
GTP-U Tunnel
Other UPFs
I-UPF / PSA
UPF Chaining
Data Network
Internet / IMS
Corporate Network
N4
N3
N9
N6
CUPS Architecture
🧠 Control Plane: AMF/SMF (Brains)
💪 User Plane: UPF (Muscle)
⚡ Flexible Edge Deployment
Key UPF Rules
📋 PDR (Packet Detection)
🔄 FAR (Forwarding Action)
⚡ QER (QoS Enforcement)
📊 URR (Usage Reporting)
All rules provisioned
by SMF via N4
Master-Slave relationship

## Slide 17: 5G Radio Access Network (RAN) Architecture: The NG-RAN
5G NG-RAN Architecture: The RAN Split
Radio Unit (RU)
• RF Processing
• Low-PHY Functions
• Antenna Interface
• Digital Beamforming
Distributed Unit (DU)
• High-PHY Processing
• MAC (Medium Access Control)
• RLC (Radio Link Control)
• Real-time Processing
• Low-latency Functions
Cell Site / Near Cell Site
Centralized Unit (CU)
• RRC (Radio Resource Control)
• PDCP (Packet Data Convergence)
• Non-real-time Processing
• Higher-layer Protocols
• Centralized Intelligence
Edge Cloud / Data Center
Fronthaul
eCPRI/Ethernet
Midhaul
F1 Interface
Backhaul
NG Interface
5G Core
Network
Key Benefits of RAN Split Architecture
Flexibility & Scalability
• Independent scaling of components
• Vendor-agnostic deployments
• Cloud-native architectures
• Network slicing support
Cost Optimization
• Reduced CAPEX through centralization
• Lower OPEX with automation
• Shared infrastructure resources
• Energy efficiency improvements
Performance Enhancement
• Ultra-low latency applications
• Enhanced mobile broadband
• Massive IoT connectivity
• Advanced interference management
Technical Notes:
• Fronthaul: High-bandwidth, low-latency connection using eCPRI over Ethernet or fiber
• Midhaul: F1 interface enabling flexible placement of CU functions
• This architecture enables Open RAN implementations and multi-vendor ecosystems

## Slide 18
CU-DU Split in 5G Architecture
Key Benefits for Network Deployment and Performance
Edge Data Center / Regional Hub
Cell Site
Centralized Unit (CU)
RRC, PDCP
Control Plane Functions
CU-CP
CU-UP
Distributed Unit (DU)
RLC, MAC, High-PHY
Real-time Processing
Scheduling, HARQ
Radio Unit (RU)
Low-PHY, RF
F1 Interface
Benefits of CU-DU Split
Flexibility
Deploy functions where they
make the most sense
(centralized CU, distributed DU)
Scalability
CU and DU resources can be
scaled independently based
on specific requirements
Edge Computing
Place DU and UPF close to users
Significantly reduces latency
for URLLC applications
Resource Pooling
Centralized CU allows efficient
coordination across multiple
DUs/cells
Virtualization (vRAN/Open RAN)
Standardized F1 interface enables multi-vendor environments
CUs and DUs from different suppliers can potentially interoperate
Facilitates vRAN and O-RAN deployments
To 5G Core Network
To UE

## Slide 19: What is Dual Connectivity?
MeNB
SeNB
MCG PCell [Carrier 1]
MCG SCell [Carrier 2]
SCG PSCell [Carrier 3]
SCG Scell [Carrier 4]
MCG Master
Cell
Group
SCG Secondary
Cell
Group
Notes: Dual Connectivity includes:
Bearer Split - in dual connectivity, this term refers to the ability to split a bearer over multiple RAN Nodes.
Split bearer: in MR-DC, a radio bearer with RLC bearers both in MCG and SCG.
Dual Connectivity - is the operation where a device consumes radio resources provided by at least two different network points (Master and Secondary) connected while in the RRC (Radio Resource Control) Connected state.
MCG (Master Cell Group) - in MR-DC, a group of serving cells associated with the Master Node, comprising of the SpCell (PCell) and optionally one or more SCells
Master RAN Node - in dual connectivity mode, this is the gNB/ng- eNB/eNB which terminates the core network connectivity and therefore acts as the mobility anchor towards the core network.
SCG (Secondary Cell Group) - is the group of serving cells associated with the Secondary RAN Node.
Secondary RAN Node - in MR-DC, the radio access node, with no control plane connection to the core network, providing additional resources to the UE. It may be an en-gNB (in EN-DC), a Secondary ng-eNB (in NE-DC) or a Secondary gNB (in NR-DC and NGEN-DC)

## Slide 20
5G Core Deployment Options
NR
f2
5GC | 
N2 | N3
Option 2
5GC
NR
f1
f
2
Option 4
LTE
f1
EPC
LTE
Option 1 (Legacy Networks)
f1
f
2
EPC
NR
LTE
S1-U
S1-MME
X2
Option 3
5GC
eLTE
f1
f2
Option 7
NR
f1
eLTE
5GC
Option 5
Deployed options depend on Use Cases/Spectrum

## Slide 21
5G Network Architecture: NSA and SA
(3GPP TS 38.300, TS 37.340, TS 23.501)
Non-Standalone (NSA)
(Option 3/3a/3x - TS 37.340)
Standalone (SA)
(TS 38.300)
UE
Dual connectivity
eNB
(4G LTE)
Master Node
gNB (NSA)
gNB-CU
gNB-DU
RRC/PDCP
RLC/MAC/PHY
F1
EPC (4G Core)
MME
S-GW
P-GW
LTE-Uu
NR-Uu
(PDCP/RLC/MAC)
X2
(X2-C, X2-U)
S1
(S1-MME, S1-U)
UE
SA capable
gNB (SA)
gNB-CU-CP
(Control Plane)
RRC/PDCP-C
gNB-CU-UP
(User Plane)
SDAP/PDCP-U
gNB-DU
RLC/MAC/PHY
F1-C
F1-U
E1
5GC (5G Core)
AMF
SMF
PCF
UDM
AUSF
UPF
NRF
Network Exposure (NEF)
NR-Uu
(RRC/PDCP/RLC)
NG-C
(NGAP)
NG-U
(GTP-U)
SA Only:
• SDAP protocol
• CU-CP/CU-UP split
• PDCP-C/PDCP-U split
3GPP References:
• TS 38.300: NR and NG-RAN Overall Description
• TS 37.340: Multi-RAT Dual Connectivity (EN-DC)
• TS 23.501: System Architecture for 5G System
Protocol Stack Abbreviations:
• RRC: Radio Resource Control • PDCP: Packet Data Convergence Protocol
• RLC: Radio Link Control • MAC: Medium Access Control
• SDAP: Service Data Adaptation Protocol (SA only) • GTP-U: GPRS Tunneling Protocol

## Slide 22
5G NR Standalone (SA) Architecture (Option 2)
Full 5G Core + 5G RAN Implementation
UE
User Equipment
NG-RAN
gNB
Next Generation NodeB
gNB-CU
Centralized Unit
gNB-DU
Distributed Unit
F1
5G Core (5GC)
Service-Based Architecture (SBA)
AMF
Access and Mobility
Management Function
SMF
Session Management
Function
UPF
User Plane
Function
Other Network Functions
UDM, AUSF, PCF, NRF, NSSF, NEF
DN
Data Network
Internet, IMS, etc.
NR Uu
N1
N2
N3
N4
N6
SBI
SBI
Xn
Control Plane
User Plane

## Slide 23
5G Non-Standalone Architecture 3x
SgNB
Split bearer – Control Plane
Split bearer – User Plane
The Dual Connectivity and the split bearer work together in the 5G-LTE interworking.
The Control Plane will always go over the LTE layer.
The data bearers to the DC-enabled UE can go over LTE or over 5G.
MeNB
SgNB
X2
S1-U
S1-U
S1-C
EPC
PDCP layer splitting point
DC UE

## Slide 24
LTE - 5G Non-Standalone (NSA) Architecture Option 3x interworking
The Non-Standalone Architecture uses (reuses) the concept of split bearer.
The split bearer is a data bearer that is set up between two nodes (here: between LTE S-GW and 5G SgNB), but at the PDCP level the actual data can be split and sent over two different channels (here: 5G radio and LTE radio via X2 relay).
The PDCP layer at the UE will take care of reordering the received packets.
SgNB
UE
EPC
MME
S1-C
S1-U
X2-C
X2-U
S1-U
S11
S5
Uu
S-GW
P-GW
MeNB
NR PDCP
RLC
RLC
NR PDCP
NR RLC
NR RLC
NR MAC
NR MAC
NR PDCP
MAC
MeNB
SgNB
SCG Bearer Split
MCG Bearer
The data bearer that goes over 5G radio can be split and sent partially over 5G radio and partially over LTE radio (with data packets relayed over X2 connection).

## Slide 25
PDCP
PDCP
RLC
RLC
MAC
RLC
MAC
EPC
LTE eNB
gNB
X2-C
X2-U
S1-C
S1-U
Core Network is EPC, LTE act as a MN, gNB act as SN.
Bearer split at master Node
RLC
MAC
LTE eNB
NR RLC
NR MAC
gNB
PDCP
NR PDCP
EPC
S1-C
S1-U
S1-U
X2-C
Independent bearer at second Node
Option 3
Option 3A
PDCP
RLC
RLC
MAC
EPC
LTE eNB
S1-C
S1-U
NR PDCP
NR RLC
NR RLC
NR MAC
gNB
NR PDCP
S1-U
Bearer split at Secondary Node
Option 3X
Option 3 EN-DC
X2-C
X2-U
Notes: In MR-DC, the UE has a single RRC state, based on the MN RRC and a single C-plane connection towards the Core
Each radio node has its own RRC entity (E-UTRA version if the node is an eNB or NR version if the node is a gNB) which can generate RRC PDUs to be sent to the UE.
RRC PDUs generated by the SN can be transported via the MN to the UE.
The MN always sends the initial SN RRC configuration via MCG SRB (SRB1), but subsequent reconfigurations may be transported via MN or SN.
When transporting RRC PDU from the SN, the MN does not modify the UE configuration provided by the SN.
Option 3X
In E-UTRA connected to EPC, at initial connection establishment SRB1 uses E-UTRA PDCP. If the UE supports ENDC, regardless whether EN-DC is configured or not, after initial connection establishment, MCG SRBs (SRB1 and SRB2) can be configured by the network to use either E-UTRA PDCP or NR PDCP (either SRB1 and SRB2 are both configured with E-UTRA PDCP, or they are both configured with NR PDCP)
Change from E-UTRA PDCP to NR PDCP (or vice-versa) is supported via a handover procedure (reconfiguration with mobility) or, for the initial change of SRB1 from E-UTRA PDCP to NR PDCP, with a reconfiguration without mobility before the initial security activation
If the SN is a gNB (i.e. for EN-DC, NGEN-DC and NR-DC), the UE can be configured to establish a SRB with the SN (SRB3) to enable RRC PDUs for the SN to be sent directly between the UE and the SN. RRC PDUs for the SN can only be transported directly to the UE for SN RRC reconfiguration not requiring any coordination with the MN. Measurement reporting for mobility within the SN can be done directly from the UE to the SN if SRB3 is configured.
  In EN-DC, the SCG configuration is kept in the UE during suspension. The UE releases the SCG configuration (but not the radio bearer configuration) during resumption initiation.
  In MR-DC with 5GC, the UE stores the PDCP/SDAP configuration when moving to RRC Inactive but it releases the SCG configuration.

## Slide 26: X2 Setup
S1U
SGW
RAC: Radio Access Cloud; CU
RAU: Radio Access Unit ; DU
RU: Radio Unit
5G RAC
5G RAU
F1
MME
LTE NodeB
S1C
(legacy)
X2-C X2-U
S1U
(legacy)
5G RU
The feature introduces the S1-U, X2-U, X2-C interfaces over IPv4/IPv6 for the 5G gNB
The S1-U interface is used for the user data transport between the S-GW and the 5G Node B. It is based on GTP-U over UDP/IP (see TS 36.414). The GTPv1-U is supported (see TS 29.281).
The X2-U interface is used for the user data transport between the eNode B and at the 5G Node B. It is based on GTP-U over UDP/IP (see TS 36.414). The GTPv1-U is supported (see TS 29.281).
The X2-C interface is used for the control plane message transfer between the eNode B and the 5G Node B. The X2-C is based on the SCTP (Stream Control Transmission Protocol, see 3GPP TS 36.422).

## Slide 27
EN-DC (LTE-NR Dual Connectivity) Network Parameters & KPIs
eNodeB (MN)
• endcSupportSwitch: ENABLED
• featureStateEndc: ENABLED
• X2/Xn Interface Config
• sctpPortX2/Xn
• LTE RSRP > -105 dBm
• lteQualityThresholdForNrMeas
• scgInactivityTimer: 10-30s
• Release Threshold: -120 to -128 dBm
• Hysteresis: 5-10 dB
gNodeB (SN)
• SSB Configuration
• PCI, ARFCN, SCS
• RACH Parameters
• p0-NominalPUSCH: -70 to -90 dBm
• p0-NominalPUCCH
• PDCP SN Size Support
• pdsch-HARQ-ACK-Codebook
• pucch-Config/pusch-Config
• UL Power Control
MME/Core Network
• DCNR Support: ENABLED
• UE 5G NSA Subscription
• HandoverRestrictionList
• UE Capabilities Check
UE Device
• EN-DC Capable
• NR Band Support
• PDCP SN 12/18 bits
• Measurement Reports
S1
RRC
NR
X2/Xn Interface
NR Measurement Configuration (B1 Event)
MeasObjectNR-r15:
• carrierFreq-r15 (ARFCN): NR frequency
• rs-ConfigSSB-r15: SSB config
• ssb-ToMeasure: bitmap mask
• ss-RSSI-Measurement: boolean
ReportConfigInterRAT (B1-NR):
• b1-ThresholdNR RSRP: -110 to -120 dBm
• b1-ThresholdNR RSRQ: -16 to -20 dB
• hysteresis-r15: 1-3 dB (2x in IE)
• timeToTrigger-r15: 320-640 ms
• maxReportCells-r15: 1-4
SCG Addition Configuration
nr-SecondaryCellGroupConfig-r15:
• cellGroupId-r15: 1-maxSCG
• rlc-BearerToAddModListSCG-r15
• pdcp-SN-Size: len12bits/len18bits
DRX Configuration:
• onDurationTimerSCG: 10-20 ms
• drx-InactivityTimerSCG: 100-200 ms
• longDRX-CycleSCG: 320-640 ms
RLF Timers:
• t310-r15: 500-1000 ms
• n310-r15: n4-n6, n311-r15: n1
Bearer Configuration
Split Bearers (PDCP at MN):
• moreThanOneRLC-r15: true
• primaryPath-r15: eUTRA/nR/both
• ul-DataSplitThreshold-r15
• t-Reordering-r15: 40-150 ms
SCG Bearers (PDCP at SN):
• High data rate non-GBR QCIs
• GBR QCIs (if NR reliable)
MCG Bearers (LTE only):
• QCI 9 (Internet) initially
• Standard LTE DRB config
Key Performance Indicators (KPIs) for Monitoring
Setup & Connection KPIs:
• EN-DC Setup Success Rate (target: >95%)
• SCG Addition Success Rate
• X2/Xn Interface Availability
• Time to SCG Setup (<200ms target)
Performance & Failure KPIs:
• SCG Drop Rate (<2% target)
• User Throughput (with/without EN-DC)
• Session Time on NR
• SCG Failure Types Analysis
• RLF (t310-Expiry, RACH problems)
• Inactivity Timer Expiry Rate
SCG Failure Analysis & Release Triggers
UE Initiated Failures (SCGFailureInformationNR):
• t310-Expiry: RLF timer expiration
• randomAccessProblemSCG: RACH failure
• rlc-MaxNumRetxSCG: RLC max retx
• synchReconfigFailureSCG: Reconfig fail
eNB Initiated Release Triggers:
• scgInactivityTimer: 10-30s
• Poor NR Quality (<-125 dBm)
• LTE quality degradation
• Load balancing decisions
• Handover preparations
Optimization Guidelines & Best Practices
Coverage Optimization:
• B1 threshold tuning: Lower (-120 dBm) for limited NR coverage, Higher (-110 dBm) for good coverage
• Hysteresis: 1-3 dB to prevent ping-pong, Time-to-trigger: 320-640ms for stability
Performance Tuning:
• DRX timers: Balance battery life vs latency (onDuration: 10-20ms, inactivity: 100-200ms)
• Bearer mapping: QCI 9 start MCG→Split, High data QCIs to Split/SCG, GBR to SCG if reliable
Reliability & Stability:
• RLF timers: t310 500-1000ms, n310 n4-n6, n311 n1 for balanced detection
• Release hysteresis: 5-10 dB between addition and release thresholds
• PDCP reordering: 40-150ms for split bearers based on path delay difference
• Monitor KPIs continuously: Setup success >95%, SCG drop <2%, failure type analysis
• Vendor-specific: Consult RAN vendor documentation for exact parameter paths and ranges
• Environment-dependent: Tune based on urban/rural, indoor/outdoor, UE capabilities, traffic models

## Slide 29: EN-DC Enablement and UE Capability
eNodeB Side (Master Node - MN):
  Vendor-specific feature license/switch: E.g., endcSupportSwitch, featureStateEndc.
    Check: Must be enabled per eNB or per cell.
    Default: Often DISABLED initially.
    Recommended: ENABLED on LTE cells intended as EN-DC anchors.
  X2/Xn Interface Configuration:
    Parameter (Conceptual): x2IpAddressListToGnb, xnIpAddressListToGnb, sctpPortX2, sctpPortXn.
    3GPP IE (for X2AP/XnAP messages): Not directly a UE RRC param, but essential. ServedCellsToAdd, ServedCellsToModify in ENB CONFIGURATION UPDATE / GNODEB CONFIGURATION UPDATE.
    Check: Correct IP addresses, SCTP ports, and link status to neighboring gNBs.
    Default: Empty, requires manual configuration.
    Recommended: All potential neighbor gNBs correctly configured and X2/Xn links operational.
MME Side (Core Network):
  UE Subscription & MME Support: MME must indicate "DCNR (Dual Connectivity with NR) supported" to eNB for the UE (part of HandoverRestrictionList or UE capabilities).
    Check: MME configured to allow DCNR, UE subscription includes 5G NSA service.
    Default: Operator/vendor dependent.
    Recommended: Enabled for 5G subscribers.

## Slide 30: NR Measurement Configuration by eNB (for SCG Addition)
The eNB configures the UE to perform measurements on NR frequencies. This is typically done via an RRCConnectionReconfiguration message.
MeasConfig IE (within RRCConnectionReconfiguration):
  measObjectToAddModList -> MeasObjectNR-r15: Defines what to measure.
    carrierFreq-r15 (ARFCN): The NR Absolute Radio Frequency Channel Number.
      Check: Correct ARFCNs of deployed NR carriers.
      Default: None. Must be configured.
      Recommended: List all deployed neighbor NR ARFCNs.
    rs-ConfigSSB-r15 or ssb-ConfigMobilityNR-r15: SSB configuration.
      ssb-ToMeasure: Bitmask indicating which SSBs to measure (can be shortBitmap, mediumBitmap, longBitmap).
      ss-RSSI-Measurement: Boolean, enable/disable SSB RSSI measurement.
      Check: Aligned with gNB's SSB transmission pattern (periodicity, subcarrier spacing if different from LTE).
      Default: Vendor specific, often a conservative set.
      Recommended: Match actual gNB SSB configuration. Use ssb-ToMeasure if specific SSBs are known to be strong/weak.
    blackCellsToAddModList-r15 / whiteCellsToAddModList-r15: PCI lists for blacklisting/whitelisting specific NR cells.
      Check: Useful for specific optimization or barring problematic cells.
      Default: Empty.
      Recommended: Use sparingly, only when necessary.
  reportConfigToAddModList -> ReportConfigInterRAT: Defines how and when to report.
    triggerType -> event:
      eventId -> eventB1-NR-r15: Inter-RAT neighbor becomes better than a threshold.
        b1-ThresholdNR-r15: Choice of nr-RSRP-r15 or nr-RSRQ-r15.
          Value: Integer (-156 to -31 for RSRP, -43 to 20 for RSRQ in 3GPP units). Vendor OSS shows dBm/dB.
          Check: Is the threshold appropriate for NR coverage?
          Default Example (Vendor OSS): RSRP: -115 dBm; RSRQ: -18 dB.
          Recommended:
            RSRP: -110 to -120 dBm. Lower (e.g., -120 dBm) for more aggressive SCG addition if NR coverage is limited. Higher (e.g., -110 dBm) if NR coverage is good, to ensure a quality NR leg.
            RSRQ: -16 to -20 dB.
        reportOnLeave-r15: Boolean. If true, report when condition is no longer met.
        hysteresis-r15: (0..30 in 0.5 dB steps).
          Check: Prevents ping-pong reporting.
          Default Example (Vendor OSS): 2 dB (which is hysteresis = 4 in 3GPP IE).
          Recommended: 1-3 dB.
        timeToTrigger-r15: (0, 40, 64, 80, 100, 128, 160, 256, 320, 480, 512, 640, 1024, 1280, 2560, 5120 ms).
          Check: Balances responsiveness and stability.
          Default Example (Vendor OSS): 320ms or 640ms.
          Recommended: 320ms - 640ms. Shorter for faster SCG addition.
    maxReportCells-r15: Max NR cells to include in one measurement report.
      Default: 1 or 2.
      Recommended: 1 to 4, depending on how many strong NR cells are typically found.
  measIdToAddModList: Links a measObjectId with a reportConfigId.

## Slide 31: NR Measurement Configuration by eNB (for SCG Addition)
The eNB configures the UE to perform measurements on NR frequencies. This is typically done via an RRCConnectionReconfiguration message.
LTE Serving Cell Condition (eNB internal logic, can be influenced by A-event thresholds):
  Often, B1 measurements for NR are only triggered if the serving LTE cell quality is above a certain threshold (e.g., using Event A3/A5 logic: a3-Offset, a5-Threshold1/2). This ensures the LTE leg is stable enough to support EN-DC.
  Parameter (Vendor conceptual): lteQualityThresholdForNrMeas, lteRsrpMinForEnDcAttempt.
  Check: Ensure LTE conditions are reasonable and don't unnecessarily prevent NR measurements.
  Recommended: LTE RSRP > -105 dBm or -100 dBm before attempting SCG addition.

## Slide 32: SCG Addition Configuration (in RRCConnectionReconfiguration)
When the eNB decides to add an NR SCG based on measurement reports:
secondaryCellGroup -> nr-SecondaryCellGroupConfig-r15 IE: This is the main container.
  cellGroupId-r15: (1..maxSCG-r15). Identifies the SCG.
  rlc-BearerToAddModListSCG-r15 / rlc-BearerToReleaseListSCG-r15: For configuring RLC bearers on SCG (SN-terminated bearers).
    For each bearer: logicalChannelIdentitySCG-r15, servedRadioBearer, rlc-ConfigSCG-r15 (AM/UM, timers), pdcp-ConfigSCG-r15.
    pdcp-ConfigSCG-r15 -> pdcp-SN-SizeUL-r15 / pdcp-SN-SizeDL-r15: (len12bits or len18bits).
      Check: UE and gNB support for 18-bit SN.
      Default: Often len12bits.
      Recommended: len18bits for high throughput bearers to avoid SN wrap-around, if supported.
  mac-CellGroupConfigSCG-r15:
    drx-ConfigSCG-r15: Configures DRX for the SCG.
      onDurationTimerSCG: (1..60, 80, 100, 200, 300, 400, 500, 600, 800, 1000, 1200, 1600 psf) in subframes/slots.
      drx-InactivityTimerSCG: (0, 1..60, 80, 100, 200, 300, 400, 500, 600, 800, 1000, 1200, 1600, 1920, 2560 ms).
      drx-RetransmissionTimerDL-SCG / drx-RetransmissionTimerUL-SCG.
      longDRX-CycleSCG-r15: (sf80, sf128, sf160, sf256 ... sf2560).
      Check: DRX enabled and timers appropriate for battery saving vs. latency.
      Default: May be vendor profile, or OFF.
      Recommended: Enable DRX. Example: onDurationTimerSCG 10-20ms, drx-InactivityTimerSCG 100-200ms, longDRX-CycleSCG 320-640ms. Tune based on traffic patterns.
    tag-ToReleaseListSCG-r15 / tag-ToAddModListSCG-r15: For Timing Advance Group configuration.
  spCellConfigSCG-r15: Configuration for the PSCell (Primary SCell) in the NR SCG.
    servCellIndex-r15: PCI and frequency of the target NR PSCell.
    reconfigurationWithSyncSCG-r15: Includes RACH configuration for initial access to NR SCG.
    rlf-TimersAndConstantsSCG-r15:
      t310-r15: SCG Radio Link Failure detection timer. (ms0, ms50, ms100, ms200, ms500, ms1000, ms2000).
      n310-r15: Max "out-of-sync" indications from PHY for SCG. (n1, n2, n3, n4, n6, n8, n10, n20).
      n311-r15: Max "in-sync" indications to declare SCG RLF recovery. (n1, n2, n3, n4, n5, n6, n8, n10).
      Check: Timers are not too aggressive (premature drops) or too relaxed (hanging on bad link).
      Default Example (Vendor OSS): t310 200-1000ms, n310 n4-n6, n311 n1.
      Recommended: t310 500-1000ms, n310 n4-n6, n311 n1. Values depend on expected radio conditions.

## Slide 33: SCG Addition Configuration (in RRCConnectionReconfiguration)
When the eNB decides to add an NR SCG based on measurement reports:
Bearer Type Configuration (within RadioBearerConfig in RRCConnectionReconfiguration):
  For Split Bearers (PDCP at MN-eNB):
    pdcp-Config -> moreThanOneRLC-r15: (ENUMERATED {true}) Indicates split bearer for this DRB.
    pdcp-Config -> primaryPath-r15: (ENUMERATED {eUTRA, nR, eUTRA-AndNR}) Suggests initial path for UL data. Not always strictly followed by UE.
    pdcp-Config -> ul-DataSplitThreshold-r15: (b0, b100, b200 ... infinity) Threshold for UL data split.
    pdcp-Config -> t-Reordering-r15: (ms0, ms20, ms40 ... ms1000, ...) Reordering timer at PDCP.
      Check: Essential for split bearers to handle differential delay.
      Default: ms40 - ms100.
      Recommended: ms40 to ms150. Longer if significant LTE-NR path delay difference is expected.
  For SCG Bearers (PDCP at SN-gNB):
    The DRB is configured with rlc-BearerToAddModListSCG-r15 (as above) and cellGroupId pointing to SCG.
  For MCG Bearers (PDCP at MN-eNB, LTE only):
    Standard LTE DRB configuration without moreThanOneRLC or SCG mapping.
  Operator Policy for Bearer Mapping:
    Check: How are QCI bearers mapped (default bearer QCI 9, GBR bearers, IMS QCI 1/5)?
    Default: QCI 9 often starts as MCG, then potentially moved to SCG/Split. High throughput bearers to Split or SCG.
    Recommended:
      QCI 9 (Internet): Start as MCG, or Split with ul-DataSplitThreshold = infinity (effectively MCG UL initially) or a high value.
      High data rate non-GBR QCIs: Split bearer or SCG bearer (if NR link is robust).
      GBR QCIs: Often SCG bearer if reliable NR, or MCG if NR reliability is a concern.

## Slide 34: SCG Release
UE Initiated (SCG Failure): UE sends SCGFailureInformationNR-r15 to eNB.
  failureType-r15: e.g., t310-Expiry, randomAccessProblemSCG, rlc-MaxNumRetxSCG, synchReconfigFailureSCG.
  Check (via KPIs): Monitor frequency and types of SCG failures.
eNB Initiated: eNB sends RRCConnectionReconfiguration releasing the nr-SecondaryCellGroupConfig-r15.
  Triggers (Vendor Specific Timers/Logic):
    scgInactivityTimer: If no data on SCG bearers for X seconds.
      Default (Vendor): 5-20 seconds.
      Recommended: 10-30 seconds. Balance battery vs. re-setup latency.
    Poor NR Quality: B1 event with reportOnLeave set to true, or a separate "NR bad quality" threshold (e.g., NR RSRP < -125 dBm).
      Recommended Release Threshold: NR RSRP -120 to -128 dBm. Ensure sufficient hysteresis (e.g., 5-10 dB) from addition threshold.
    LTE quality drops below a certain level where EN-DC is no longer beneficial.

## Slide 35: gNB Side Parameters (Secondary Node - SN)
Xn/X2 Interface Configuration: (As above, but from gNB perspective).
Cell Configuration:
  SSB: PCI, ARFCN, Subcarrier Spacing, Periodicity.
  RACH parameters for SCG initial access.
PhysicalCellGroupConfig (part of what gNB would send in SA, but relevant for its capabilities):
  pdsch-HARQ-ACK-Codebook: (dynamic, semi-static).
  pucch-Config / pusch-Config (for SCG bearers).
  UL Power Control: p0-NominalPUSCH, alpha, p0-NominalPUCCH.
    Check: Aligned with link budget and interference goals.
    Default: Generic values for the band.
    Recommended: Tuned based on drive tests and performance monitoring. E.g., p0-NominalPUSCH might be around -70 to -90 dBm depending on band and cell range.
Supported PDCP SN Sizes: Must support what eNB requests.

## Slide 36: Basic LTE-NR Dual connectivity
GTP:Modify Bearer Request (DL S1 TEID)
Dual Connectivity NSA mode 3x operation – call flow (1/2)
UE
MeNB
RRC Connection Establishment
Random Access over LTE
SgNB
MME
P-GW
S-GW
S1AP:Initial UE Message
GTP:Create Session Request
GTP:Create Session Request (DL S5 TEID)
GTP:Create Session Response (UL S5 TEID)
GTP:Create Session Response (UL S1 TEID)
S1AP:Initial Context Setup Request (UL S1 TEID)
S1AP:Initial Context Setup Response (DL S1 TEID)
GTP:Modify Bearer Request
GTP:Modify Bearer Response
GTP:Modify Bearer Response
X2 connection existing
Update Location
HSS
LTE Cell detection (PSS and SSS) and
LTE System Information decoding
AS Security Setup
UE Capability Transfer
RRC Connection Reconfiguration
UL S1 TEID / DL S1 TEID
UL S5 TEID / DL S5 TEID

## Slide 37: Basic LTE-NR Dual connectivity
Dual Connectivity NSA mode 3x operation – call flow (2/2)
UE
MeNB
SgNB
MME
P-GW
S-GW
X2AP:SgNB Addition Request
X2AP:SgNB Addition Request Acknowledge
RRC Connection Reconfiguration
RRC Connection Reconfiguration Complete
X2AP:SgNB Reconfiguration Complete
X2AP:SN Status Transfer
5G Cell detection (PSS and SSS) and 5G System Information decoding
Random Access over 5G
S1AP:E-RAB Modification Indication
S1AP:E-RAB Modification Confirm
GTP:Modify Bearer Request
GTP:Modify Bearer Response
DL data Forwarding (opt.)
UL data only
Two channels over air interface
U-Plane
U-Plane, C-Plane
S1-U bearer switch
from S-GW <-> MeNB
towards S-GW <-> SgNB
UL S1 TEID / DL S1 TEID
UL S5 TEID / DL S5 TEID
UL X2 TEID / DL X2 TEID

## Slide 38: Contents
Module 2: Massive MIMO and Beamforming Essentials
• 2.1 Massive MIMO Technology
o Principles and benefits of Massive MIMO
o Antenna array configurations and beamforming gains
• 2.2 Beamforming Techniques in 5G NR
o Digital and analog beamforming
o Beamforming for mmWave frequencies
• 2.3 Integration of Massive MIMO and Beamforming
o Practical applications and use cases
o Challenges and solutions in implementation

## Slide 39
5G MIMO (Multiple-Input Multiple-Output) Technology
5G Base Station (gNB)
Massive MIMO Array
32-128 Antenna Elements
Baseband Processing Unit
Channel Estimation, Precoding
Beamforming Controller
3D Beamforming (Azimuth/Elevation)
User Equipment (UE)
MIMO Receiver
4-8 Antenna Elements
Signal Processing Unit
Channel Estimation, Decoding
Baseband Processing
3GPP Rel-15/16 Compliant
MIMO Principles
Spatial Multiplexing
Multiple data streams on same channel
Increases throughput (up to 20 Gbps)
Transmit/Receive Diversity
Same data via multiple paths
Improves reliability and robustness
Beamforming
Focused energy toward specific UEs
Reduces interference, extends range
5G MIMO Benefits
Higher Data Rates
Peak: 20 Gbps (DL), 10 Gbps (UL)
Increased Capacity
1M devices/km² (3GPP Rel-15)
Improved Reliability
99.999% for URLLC applications
Spectrum Efficiency
30 bps/Hz (vs 15 bps/Hz in 4G)
Diversity/Beamforming
Spatial Multiplexing

## Slide 40
gNB MAC
CRC Calculation + attachment
LDPC Graph Selection
Code Block Segmentation
Channel Coding (LDPC Encoding)
Rate Matching + HARQ
Interleaving + Scrambling +
Modulation
Layer Mapping
Antenna Port Mapping
Precoding
Virtual/Physical Resource Element Mapping
OFDM Modulation + CP Insertion
DAC TX Beamforming
IQ Modulation/RF Up-conversion/ PA and TX Filter
Information Element
Multiplexing
CRC Calculation + Attachment
Channel Coding (Polar Encoding)
Rate Matching
CCE-to-REG Mapping
Scrambling
QPSK Modulation
Reference Signal Generation
DM-RS/CSI-RS/PT-RS/TRS
Payload Generation +
Scrambling
CRC Calculation + Attachment
Channel Coding (Polar Encoding)
Rate Matching
Scrambling
QPSK Modulation
SS Block Generation
SSS
PSS
Reference Signal
Configuration
HARQ
HARQ ACK/NACK
MAC Scheduler
CSI Reports estimation
SS block configuration
Overall downlink physical layer processing
DL-SCH
DCI
BCH

## Slide 41
Physical layer processing of PBCH and mapping to time-frequency resources
1st scrambling stage with cell ID
M= SFN/2 mod4
Polar Coding
2nd scrambling stage with cell ID
N=(SSB time index) mod4
N=(SSB time index) mod8
frequency
symbols
PBCH
PBCH
SSS
PSS
PBCH
PBCH
12 PRB
20 PRB
Scramble bit
Scrambled bits + CRC
Coded Bits
PBCH payload generation
Scrambling
CRC attachment
Channel Coding
Rate matching
scrambling
Modulation
RE Mapping
BCH Data
Payload size
32 bits
PBCH Transport Process
Antenna Port 4000
Notes: BCH Payload Generation and other processing information
- Layer-1, after receiving the BCH data (24-bits), appends Eight additional timing related bits to generate PBCH payload bits (32-bits).
- A 24-bit CRC is appended to the PBCH payload which yields 56-bits in total.
- These 56-bits would result in 512-bits after channel coding (Polar coding) which then becomes 864-bits after rate matching. Since QPSK is used, just 432 REs are needed to transmit 432 QPSK symbols (864-bits).
- As discussed already, there are 576 REs dedicated for PBCH, remaining 144 REs (576-432) are used for PBCH DM-RS (see Table 7.4.3.1-1 from 38.211).
The PBCH payload size is 56 bits including 24-bit CRC. In NR, PBCH uses a single antenna port transmission scheme, using the same antenna port as PSS and SSS within the same SS block. The periodicity of PBCH is 80 ms.
The MIB data arrive at the PBCH processing unit in the form of one transport block (TB) every 80 ms and goes through the following steps as shown in Fig. 4.9: payload generation, scrambling, TB CRC calculation and attachment, channel coding, and rate matching.
The coded and modulated bits of PBCH are mapped onto the resource elements allocated for PBCH .
the PBCH content is encoded using the polar code.
Two scrambling operations are performed on PBCH which include one before CRC attachment and another one after the polar coding and rate matching.
In the first scrambling stage, initialization based on Cell ID, the sequence is partitioned into four non-overlapping portions.
The portion for transmission is selected based on the second and third least significant bits of the SFN.
In the second scrambling stage, initialization based on Cell ID, the sequence is partitioned into four or eight non-overlapping portions.
The portion for transmission is selected based on the second or third least significant bits of the SS block time index.

## Slide 42
Physical layer processing of NR PDCCH
Information element
multiplexing
TS 38.212 Section 7.3.1
CRC attachment
TS 38.212 Section 7.3.2
Channel coding
TS 38.212 Section 7.3.3
Rate matching
TS 38.212 Section 7.3.4
Scrambling
TS 38.211 Section 7.3.2.3
Modulation
TS 38.211 Section 7.3.2.4
Resource element mapping
TS 38.211 Section 7.3.2.5
Scheduling information (DCI data)
To
,

## Slide 43
Transport block (TB)
TB CRC
LDPC base graph
Code Block
LDPC coding
Rate Matching
Code Block Concatenation
Scrambling
Modulation
Layer Mapping
Antenna Port
Antenna Port
VRB Mapping
VRB to PRB Mapping
Rel 15 supports up to 2 TBS
TBS>3824 has 24 bits CRC
Else 16 bits CRS
Max CB size( Kcb) based LDPC base graph selection type1= 8448 Type 2: 3840
CB segmentation and CRC attachment 24 bits
LDPC based channel coding
Code bit to resource mapping
Data is scrambled with 31 length gold sequence
Modulation table selection 64 QAM and 256 QAM
Modulation symbols are mapped to multiple layers
Virtual resource block are mapped to physical RBS interleaved or non interleaved
CRC
CRC
Physical downlink Shared channel (PDSCH)

## Slide 44
5G NR Physical Layer Standards & Massive MIMO Integration
TS 38.211: NR Physical Channels and Modulation
Antenna Ports
• Physical channel mapping
• Spatial multiplexing foundation
Reference Signals
• CSI-RS (Channel State Info)
• SRS (Sounding Reference)
• SSB (Sync Signal Block)
• NZP/ZP CSI-RS configs
Layer Mapping
• Data to layers
• Precoding interface
TS 38.213: NR Physical Layer Procedures for Control
CSI Reporting
• CQI, PMI, RI
• L1-RSRP
• Codebook/Non-CB
• Beam measurement
Beam Management
• Beam Measurement
• Beam Reporting
• Beam Indication
• Failure Recovery
TCI States
• Beam indication
• PDSCH/PDCCH
• Dynamic config
• Multi-beam support
MU-MIMO
• Multi-user spatial
• Interference mgmt
• Resource allocation
• Spatial separation
TS 38.214: NR Physical Layer Procedures for Data
PDSCH/PUSCH
• Data transmission
• Layer-to-antenna mapping
• TCI state utilization
• Spatial multiplexing
Dynamic Beaming
• Real-time beam selection
• Adaptive beamforming
• Link adaptation
• Performance optimization
Resource Allocation
• Time-frequency resources
• Spatial domain
• Multi-layer support
• MIMO rank adaptation
TS 38.212: NR Channel Coding
Coding Impact on MIMO
• Per-layer coding schemes
• Error correction across streams
• Rate matching for spatial layers
• HARQ for MIMO streams
Coding Schemes
• LDPC for data channels
• Polar codes for control
• Turbo codes (legacy)
• CRC attachment
Massive MIMO Key Benefits & Implementation
Spatial Multiplexing
Multiple data streams
Higher spectral efficiency
128+ antenna elements
Up to 16 layers DL
Up to 4 layers UL
Precoding optimization
Advanced Beamforming
3D beamforming
Digital precoding
Multi-user beamforming
Null-steering
Reciprocity-based BF
CSI-RS beam sweeping
Channel Estimation
High-resolution CSI
Massive CSI-RS configs
Beam-specific measurement
L1-RSRP reporting
SRS uplink sounding
TDD reciprocity
Interference Mgmt
Spatial interference rejection
Zero-forcing precoding
Inter-cell coordination
ZP CSI-RS muting
Co-channel sharing
Multi-user orthogonality
Performance Gains
10x capacity increase
Energy efficiency gain
Coverage enhancement
Latency reduction
99.999% reliability
Massive connectivity
Implementation
Active antenna systems
Digital baseband processing
Real-time adaptation
Machine learning opt.
Sub-6GHz & mmWave
Cloud-RAN integration
Key Frequency Bands & Deployment Scenarios
Sub-6 GHz (FR1)
mmWave (FR2)
TDD Reciprocity
FDD Challenges
Urban Deployment
Rural Coverage
Massive MIMO Performance Metrics
Capacity:
10-20x increase vs 4G
Spectral Efficiency:
30+ bps/Hz/cell
Energy Efficiency:
100x improvement
Latency:
Sub-1ms URLLC
Reliability:
99.999% availability
Connections:
1M devices/km²
Concurrent Beams:
64+ simultaneous
Coverage:
Cell edge +10dB

## Slide 45
SU-MIMO & MU-MIMO
Notes: 1. What is MIMO?
At its core, MIMO (Multiple-Input Multiple-Output) is a wireless communication technology that uses multiple antennas at both the transmitter (e.g., the 5G base station, called gNB) and the receiver (e.g., the smartphone or user equipment, called UE). This allows for exploiting the spatial dimension of the radio channel to improve communication performance.
2. What is SU-MIMO (Single-User MIMO)?
SU-MIMO specifically refers to the scenario where the multiple antennas and associated processing at the gNB are used to communicate with only one UE within a specific time and frequency resource block. The primary goal of SU-MIMO in 5G is typically spatial multiplexing to increase the data rate for that single user.
3. Core Principle: Spatial Multiplexing
Concept: Imagine you have multiple separate paths (spatial streams or layers) between the gNB's transmit antennas and the UE's receive antennas. Spatial multiplexing allows the gNB to send different data streams simultaneously over these spatial paths using the same time and frequency resources.
Analogy: Think of it like having multiple parallel pipes between the gNB and UE, each carrying a portion of the total data concurrently.
Result: If the gNB can successfully transmit 'N' independent spatial layers, the peak data rate for that single UE can ideally be multiplied by 'N' compared to a single-antenna (SISO - Single-Input Single-Output) system, without requiring additional bandwidth.
4. Key Mechanisms and 3GPP Concepts for SU-MIMO in 5G NR:
Multiple Antennas: Both the gNB and the UE need multiple physical antennas. The number of antennas dictates the potential maximum number of spatial layers.
Layers (Spatial Streams): These are the independent data streams transmitted in parallel. The number of layers actually transmitted is called the Rank of the MIMO transmission. The rank is limited by the minimum of the number of transmit antennas and receive antennas (Rank ≤ min(N_Tx, N_Rx)), and also heavily dependent on channel conditions.
Channel State Information (CSI): For SU-MIMO spatial multiplexing to work effectively, the gNB needs to know the characteristics of the radio channel between each of its transmit antennas and each of the UE's receive antennas. This is CSI.
  CSI Acquisition: The gNB transmits known reference signals, specifically CSI-RS (Channel State Information Reference Signals). The UE measures these CSI-RS to estimate the channel.
  CSI Feedback: The UE processes the channel estimate and reports relevant information back to the gNB. This feedback is crucial for the gNB to adapt its transmission. The 5G NR CSI framework includes reporting:
    RI (Rank Indicator): The UE recommends the number of spatial layers (rank) it believes the channel can reliably support. This is fundamental for SU-MIMO. If RI=1, it's not spatial multiplexing SU-MIMO (might be diversity or single-layer beamforming). If RI > 1, the UE is requesting spatial multiplexing.
    PMI (Precoding Matrix Indicator): The UE recommends a specific precoding matrix from a predefined set (codebook) that the gNB should use to prepare the data streams for transmission. The precoder helps to spatially separate the layers and align them with the channel's characteristics.
    CQI (Channel Quality Indicator): The UE indicates the highest data rate (Modulation and Coding Scheme - MCS) it estimates it can successfully decode per layer, assuming the gNB uses the recommended RI and PMI.
Precoding: This is the signal processing done at the gNB before transmission, based on the received CSI feedback (or sometimes based on gNB's own channel estimation in TDD).
  Purpose: To manipulate the signals transmitted from each antenna such that the different spatial layers interfere minimally with each other at the UE's receiver antennas and are received with maximum possible power.
  Codebook-Based Precoding: The most common type, where the gNB uses the PMI reported by the UE to select a precoding matrix from a standardized codebook (defined in 3GPP TS 38.214). This simplifies feedback but might not be perfectly optimal. 5G NR supports various codebooks, including more advanced Type II CSI reporting for potentially better performance (non-codebook or more detailed feedback).
  How it works (simplified): The gNB takes the multiple data layers, multiplies them by the chosen precoding matrix, and the result determines the complex signal values to be sent from each physical (or virtualized) antenna port.
UE Receiver Processing: The UE receives the superimposed signals on its multiple antennas. Since the signals traveled through the wireless channel and were precoded, they are mixed up. The UE needs sophisticated receiver algorithms (like MMSE - Minimum Mean Square Error, or SIC - Successive Interference Cancellation) to:
  Estimate the effective channel for each layer (using DMRS).
  Separate the different spatial layers from the received mixture.
  Decode the data from each layer individually.
Demodulation Reference Signals (DMRS): These reference signals are transmitted along with the data and are subjected to the same precoding as the data layers. The UE uses DMRS to estimate the effective channel experienced by each layer after precoding, which is essential for demodulating the data correctly. The configuration of DMRS (e.g., number of DMRS ports) is linked to the number of layers being transmitted.
5. Factors Influencing SU-MIMO Performance:
Channel Rank: The actual number of independent spatial paths the channel can support. This depends heavily on the richness of the multipath environment (scattering). A Line-of-Sight (LOS) channel often has a low rank (Rank=1), making spatial multiplexing difficult. Rich scattering environments are better for higher ranks.
Antenna Correlation: If the signals received at different UE antennas (or transmitted from different gNB antennas) are too similar (highly correlated), it's hard to separate the layers. Good antenna separation and design, along with a scattering environment, reduce correlation.
Signal-to-Noise Ratio (SNR): Higher SNR is generally required to support higher ranks and higher-order modulation schemes on each layer.
CSI Quality: The accuracy and timeliness of the CSI feedback are critical. Outdated or inaccurate CSI leads to imperfect precoding, resulting in Inter-Layer Interference (ILI), which degrades performance.
UE Processing Capability: Separating multiple high-data-rate streams requires significant processing power at the UE.
6. SU-MIMO vs. MU-MIMO:
SU-MIMO: Focuses on boosting the peak data rate for a single user at a given time/frequency resource. Improves user experience for demanding applications.
MU-MIMO (Multi-User MIMO): Serves multiple users simultaneously using the same time/frequency resource by spatially separating their signals. Improves overall cell capacity and spectral efficiency but may not necessarily maximize the peak rate for any single user involved compared to SU-MIMO.

## Slide 46
MU-MIMO (Multi-User MIMO)
gNB
5G
Tx1
Tx2
Tx3
Tx4
Data Streams (Layers)
User 1
R1
User 2
R1
User 3
Rx2
User 4
Rx2
CSI Feedback (RI, PMI, CQI)

## Slide 47
From 4G LTE to 5G NR Massive MIMO
4G LTE MIMO
Traditional Multi-Antenna Technology
Antenna Panel
8
Antennas
Broad Coverage Area
📱
📱
📱
4G LTE MIMO Specifications
🔹 Antenna Configuration: 2x2, 4x4, up to 8x8 MIMO
🔹 Antenna Elements: 2-8 antenna elements typical
🔹 Beamforming: Basic digital beamforming
🔹 Coverage Strategy: Wide area, sector-based
🔹 Frequency Range: Sub-6 GHz (700 MHz - 2.6 GHz)
🔹 Peak Data Rate: Up to 1 Gbps theoretical
🔹 User Capacity: Limited simultaneous users
5G NR Massive MIMO
Revolutionary Massive Antenna Arrays
Massive MIMO Array
64+
Antennas
📱
📱
📱
📱
📱
📱
Targeted Beamforming
5G NR Massive MIMO Specifications
🔸 Antenna Configuration: 32x32, 64x64, up to 256x256 MIMO
🔸 Antenna Elements: 32-256+ elements in dense arrays
🔸 Beamforming: Advanced 3D beamforming with beam steering
🔸 Coverage Strategy: Precise user-specific targeting
🔸 Frequency Range: Sub-6 GHz + mmWave (24-100 GHz)
🔸 Peak Data Rate: Up to 20 Gbps theoretical
🔸 User Capacity: Massive simultaneous connections
Key Innovation: 10x-100x More Antennas = Revolutionary Performance

## Slide 48
Course Title / Slide Title
5G Beamforming: Controlled Interference Principle
4G Style: Omnidirectional (Floodlight)
gNB
UE1
UE2
UE3
⚠️ High Interference
⚡ Energy Waste
5G Style: Beamforming (Spotlight Array)
gNB
UE1
UE2
UE3
NULL
NULL
✅ Minimal Interference
⚡ Energy Efficient
📶 Higher Data Rates
Wave Interference Principle
Constructive Interference (BEAM)
Wave 1
Wave 2
Combined
STRONGER!
Destructive Interference (NULL)
Wave 1
Wave 2
Combined
CANCELLED!
Beamforming Control Parameters
Phase Control (Timing)
• Adjust signal timing from each antenna
• Creates constructive/destructive interference
• Steers beam direction precisely
φ₁
φ₂
Amplitude Control (Power)
• Adjust signal power from each antenna
• Controls beam shape and width
• Optimizes energy distribution
A₁
A₂
Result: Precise spatial control → Higher capacity, Better coverage, Reduced interference
Each user gets a dedicated "spotlight" of RF energy, while others experience "darkness" (nulls)

## Slide 49
Beam management in 5G NR
(P-4): Beam Failure Recovery (BFR)

## Slide 50
Why Beamforming is ESSENTIAL for 5G: Solving Critical Challenges
Challenge 1: Overcoming High-Frequency Physics
Frequency Band Comparison
4G Low Band (700MHz-2GHz)
Good Coverage
Penetrates Obstacles
5G mmWave (28GHz+) - WITHOUT Beamforming
Wall
BLOCKED
High Path Loss
Easily Blocked
Path Loss Physics
Path Loss proportional to (frequency)squared
• 700 MHz to 28 GHz = 40x frequency increase
• Path Loss increases by 40squared = 1,600x
• Signal becomes 32 dB weaker!
Communication nearly impossible
SOLUTION: Massive MIMO + Beamforming
• Array Gain = 10 x log10(N) where N = antennas
• 64 antennas gives 18 dB gain = 63x power boost!
Compensates for high path loss
Array Gain Mathematics
Problem: mmWave path loss = 32 dB higher than 4G
Solution: Massive MIMO Array Gain = 18 dB + Beamforming Gain = 15 dB = 33 dB total gain
Result: 33 dB gain greater than 32 dB loss makes mmWave viable!
For mmWave: Communication is PRACTICALLY IMPOSSIBLE without beamforming
Beamforming transforms 5G from impossible to practical
by concentrating scattered energy into focused, penetrating beams
Challenge 2: Enabling Massive Capacity (Thousands of Devices)
Traditional Approach: Time Division
UE1
t=1ms
UE2
waiting...
UE3
waiting...
UE4
waiting...
Users take turns leads to Low capacity
Congestion in dense areas
SOLUTION: Multi-User MIMO (MU-MIMO) with Beamforming
UE1
Stream 1
UE2
Stream 2
UE3
Stream 3
UE4
Stream 4
NULL
NULL
All users served simultaneously
Same frequency, same time gives Massive capacity
Capacity Multiplication Through Spatial Division
Traditional: 1 frequency x 1 time slot = 1 data stream
MU-MIMO: 1 frequency x 1 time slot x N spatial streams = N data streams
Example: 64-antenna array supports up to 8-16 simultaneous users = 8-16x capacity increase!
Critical: Null steering prevents interference between simultaneous beams
Real-World Impact: Stadium with 50,000 Users
Without MU-MIMO: Network congestion
Users get less than 1 Mbps each
With MU-MIMO: Spatial multiplexing
Users get 100+ Mbps each

## Slide 51
Types of Beamforming in 5G NR: Implementation Trade-offs
Performance vs Complexity vs Cost
A. Analog Beamforming
"Single Garden Hose + Adjustable Sprinkler"
Architecture
Baseband Processor
(Single Data Stream)
Single RF Chain
Analog Phase Shifters
φ₁
φ₂
φ₃
φ₄
φ₅
φ₆
Antenna Array
Single Steerable Beam
UE1
Garden Hose Analogy
Single Hose
Same water (data) direction adjustable
but only ONE stream possible
Characteristics
PROS:
• Simple implementation
• Low cost
• Low power consumption
• Fast beam steering
CONS:
• Only ONE beam at a time
• No true MU-MIMO
• Cannot send different data
simultaneously
USE CASE: mmWave Beam Sweeping
Initial signal discovery and coarse beam alignment
B. Digital Beamforming
"Separate Faucet for Every Nozzle"
Architecture
Baseband Processor
(Multiple Data Streams)
RF₁
RF₂
RF₃
RF₄
RF₅
RF₆
Each Antenna = Dedicated RF Chain
Antenna Array
Multiple Independent Beams
UE1
Stream 1
UE2
Stream 2
UE3
Stream 3
Multiple Faucets Analogy
Separate Computer-Controlled Faucets
Different colored water (data) to different directions
Characteristics
PROS:
• Multiple independent beams
• True MU-MIMO capability
• Highest precision and performance
• Perfect interference nulling
CONS:
• Extremely expensive
• Massive power consumption
• Computationally intensive
• Complex implementation
USE CASE: Theoretical Ideal
Foundation principle but not practical for large arrays
C. Hybrid Beamforming
"8 Colored Faucets + Adjustable Sprinklers"
The PRACTICAL Solution!
Two-Stage Architecture
Baseband Processor
(Digital Precoding)
Stage 1: Digital (Fewer RF Chains)
RF₁
RF₂
RF₃
RF₄
RF₅
RF₆
Stage 2: Analog Phase Shifters
Large Antenna Array (64+ elements)
Multiple Steered Beams (Best of Both Worlds)
UE1
Stream 1
UE2
Stream 2
Smart Compromise Analogy
8 Colored Faucets
Each feeds sprinkler head
Different data + analog steering = efficient precision
Characteristics
PROS:
• Enables MU-MIMO
• Much lower cost than digital
• Reduced power consumption
• Practical for large arrays
• Best performance/cost trade-off
CONS:
• More complex than analog
• Limited by number of RF chains
• Some performance compromise
USE CASE: 5G Mid-band and mmWave Deployments
The workhorse of practical 5G Massive MIMO systems
Implementation Trade-off Summary
Analog: Simple + Cheap = One beam only
Digital: Perfect + Powerful = Too expensive
Hybrid: Smart compromise = 5G reality
Hybrid beamforming enables practical 5G by balancing performance, cost, and complexity

## Slide 52
Analog Beamforming (RF Beamforming) Architecture
Baseband
Processing
(Digital)
DAC
Digital to
Analog
RF Front-end
Up-converter
Power Amp
Power
Splitter
Phase Shifter
φ₁
Phase Shifter
φ₂
Phase Shifter
φ₃
Phase Shifter
φ₄
Ant 1
Ant 2
Ant 3
Ant 4
Main Beam
θ = 30°
UE
1
Key Characteristics
Cost-effective:
Requires fewer RF chains (one per beam/panel)
Power efficient:
Less power consumption due to fewer RF chains
Limited Flexibility:
Can only form one beam per RF chain at a time
Cannot simultaneously serve multiple users
Spatial Multiplexing:
Difficult to achieve true spatial multiplexing
Typical Use Cases
Initial Access (SSB Sweeping):
Broadcasting Synchronization Signal Block in mmWave bands
gNB sweeps different pre-defined analog beams for coverage
Broad Coverage:
For sectors where a wide, fixed beam is sufficient
Lower Frequency Bands:
Where Massive MIMO capabilities are not strictly required
Simpler analog beamforming deployment
Single RF Chain
Analog Phase Control
Beam Steering
• Entire array steers together
• One beam direction at a time
• Fixed beam width
Frequency Band Applications
• mmWave (24-100 GHz): Primary use for initial access and beam sweeping in 5G NR
• Sub-6 GHz: Cost-effective solution for basic beamforming
Signal Flow:
RF Signal Path
Wireless Link
Phase Control
Limitation

## Slide 55
PDCP Split Bearer Function - Downlink (DL) and Uplink (UL) Data Flow
DOWNLINK (DL) Data Flow
Core Network
(Data Packets/SDUs)
MN PDCP Entity
• Sequence Numbering
• Header Compression (RoHC)
• Ciphering
• Splitting Decision
MCG Leg
MN RLC/MAC/PHY
Direct to UE
SCG Leg
Via Xn-U/X2-U
to SN
SN (gNB/eNB)
RLC/MAC/PHY
UE PDCP Entity
• Receives from MCG & SCG
• Reordering (handles out-of-order)
• Deciphering & Header Decompression
• Delivery to Upper Layers
UPLINK (UL) Data Flow
UE PDCP Entity
• Sequence Numbering
• Header Compression
• Ciphering
• Splitting Decision (ul-DataSplitThreshold)
MCG Leg
UE RLC/MAC/PHY
Direct to MN
SCG Leg
UE RLC/MAC/PHY
to SN
SN (gNB/eNB)
Forwards via Xn-U/X2-U
MN PDCP Entity
• Receives from MCG & SCG
• Reordering
• Deciphering & Header Decompression
• Delivery to Core Network
Core Network
(Processed SDUs)
Xn-U/X2-U Interface
Xn-U/X2-U Interface
MCG Air Interface
SCG Air Interface
Key PDCP Functions in Split Bearer Operation
• Sequence Numbering:
Essential for reordering at receiving PDCP entity
• Routing/Splitting Logic:
Decision algorithm for MCG vs SCG path selection
• Reordering:
Handles PDUs from two paths with different delays
• Ciphering/Header Compression:
Performed once by single PDCP entity
• Status Reporting:
Complex reporting across both legs for retransmissions
• UL Threshold Control:
ul-DataSplitThreshold determines routing decision
3GPP Specification References
• TS 38.323 (NR) / TS 36.323 (LTE):
PDCP specification - Section 5.1.2 (PDCP PDU routing)
• TS 38.331 (NR) / TS 36.331 (LTE):
RRC specification - PDCP-Config IE, ul-DataSplitThreshold
• TS 38.300 (NR) / TS 36.300 (LTE):
Architecture - Section 16 Dual Connectivity overview
Legend
Core Network
Master Node (MN)
Secondary Node (SN)
User Equipment (UE)
MCG Path
SCG Path

## Slide 56: Module 3: Configuration Parameters, KPIs, and Troubleshooting

## Slide 57
5G NR Numerology & Radio Frame Structure
Numerology Parameters
μ
SCS
Slot Duration
Use Cases
0
15 kHz
1 ms
Wide coverage, LTE interworking
1
30 kHz
0.5 ms
Standard eMBB
2
60 kHz
0.25 ms
URLLC, Industrial IoT
3
120 kHz
0.125 ms
URLLC, mmWave
Key Formula
SCS = 2^μ × 15 kHz
Slot Duration = 1ms / 2^μ
Radio Frame Structure (10ms)
Radio Frame (10 ms) = 10 Subframes
1ms
1ms
... Subframes (1ms each) ...
Slot Structure for Different Numerologies
μ=0 (15kHz):
1 Slot (1ms)
14 OFDM Symbols
μ=1 (30kHz):
0.5ms
0.5ms
2 Slots per 1ms
μ=2 (60kHz):
0.25ms
0.25ms
0.25ms
0.25ms
4 Slots per 1ms
μ=3 (120kHz):
0.125ms
8 Slots per 1ms
Key 5G NR Features
Dynamic TDD: Flexible UL/DL allocation
Mini-slots: Sub-slot scheduling for URLLC
Mixed Numerology: Multiple SCS in same cell
Self-contained: All signals within slot
Symbols: D (DL), U (UL), F (Flexible)
Latency Impact
μ=0: Higher Latency (1ms slots)
μ=1: Medium Latency (0.5ms slots)
μ=2: Lower Latency (0.25ms slots)
μ=3: Ultra-low Latency (0.125ms slots)
Trade-off Visualization
Higher SCS →
Better Coverage ↑
15kHz
30kHz
60kHz
120kHz

## Slide 58
Accessibility KPI

## Slide 59
5G NR Accessibility KPIs
1. Registration Success Rate (RSR)
Formula:
RSR = (∑ AMF.5GSRegisSucc.Type / ∑ AMF.5GSRegisAtt.Type) × 100%
• AMF.5GSRegisSucc.Type: Successfully performed registrations
• AMF.5GSRegisAtt.Type: Attempted registrations
• Type: initial, mobility update, periodic update, emergency
2. Partial DRB Accessibility
Per 5QI:
Partial DRBAccessibility_5QI =
(∑RRC.ConnEstabSucc.Cause / ∑RRC.ConnEstabAtt.Cause) ×
(∑UECNTXT.ConnEstabSucc.Cause / ∑UECNTXT.ConnEstabAtt.Cause) ×
(DRB.EstabSucc.5QI / DRB.EstabAtt.5QI) × 100
Per S-NSSAI:
Replace 5QI with SNSSAI in above formula
Note: Excludes mo-Signalling establishment cause
3. Total DRB Accessibility
Formula (per 5QI):
DRBAccessibility_5QI = 100 ×
[DRB.InitialEstabSucc.5QI + (DRB.EstabSucc.5QI - DRB.InitialEstabSucc.5QI) + DRB.ResumeSucc.5QI]
[DRB.InitialEstabAtt.5QI × (RRC connection setup success rate/100) ×
(UE-associated logical NG-connection success rate/100)] +
[(DRB.EstabAtt.5QI - DRB.InitialEstabAtt.5QI)] +
[DRB.ResumeAtt.5QI × (RRC Resume success rate/100)]
• RRC connection setup success rate = ∑RRC.ConnEstabSucc.Cause / ∑RRC.ConnEstabAtt.Cause
• UE-associated NG-connection success rate = ∑UECNTXT.ConnEstabSucc.Cause / ∑UECNTXT.ConnEstabAtt.Cause
• RRC Resume success rate = RRC.ResumeSucc.cause / RRC.ResumeAtt.cause (excludes RNA update)
Key Terms & Abbreviations
• 5QI: 5G QoS Identifier - Quality of Service Class Identifier
• S-NSSAI: Single Network Slice Selection Assistance Information
• DRB: Data Radio Bearer - Radio bearer for user data transmission
• RRC: Radio Resource Control - Layer 3 signaling protocol
• AMF: Access and Mobility Management Function
• UECNTXT: UE Context - User Equipment Context establishment
• mo-Signalling: Mobile Originated Signalling (excluded from calculations)

## Slide 60
RACH Success Rate KPI Analysis
RACH Success Rate Formula:
RACH Success Rate = (Number of Successfully Completed RACH Procedures) / (Total Number of RACH Attempts) × 100%
RACH Procedure Flow
UE
(User Equipment)
gNB
(Base Station)
Msg1: Preamble
(Random Access)
Msg2: RA Response
(RAR)
Msg3: Contention
(if contention-based)
Msg4: Resolution
(Contention Resolution)
Success Criteria:
✓ UE successfully transmits Preamble (Msg1)
✓ gNB receives and processes Preamble
✓ gNB sends RA Response (Msg2) successfully
✓ Contention resolution completed (if applicable)
Root Causes for Low RACH Success Rate
1
Poor Radio Coverage/Quality
Weak signal strength, high path loss
2
Excessive Interference
Co-channel/adjacent-channel interference
3
Incorrect Power Control
UE transmit power too low/high
4
Insufficient RACH Resources
Not enough PRACH occasions/preambles
5
Timing Advance Issues
Preambles arrive outside reception window
6
gNB Load/Capacity
gNB overloaded, delayed processing
7
Misconfigured Parameters
Incorrect 3GPP parameter settings
Key Performance Indicators:
Excellent
≥95%
Target Range
Good
90-95%
Acceptable
Poor
<90%
Needs Action
Typical Measurement Period: 15 minutes to 1 hour
• Measured per cell or per gNB
• Focus on Msg1-Msg2 handshake success

## Slide 61
Preamble Transmission Power & Ramping - KPI Impact Analysis
gNB
Base Station
UE1
Close
Low PL
UE2
Medium
Med PL
UE3
Far
High PL
Low Tx Power
Medium Tx Power
High Tx Power
PreambleInitialReceivedTargetPower
• 3GPP: rach-ConfigCommon → rach-ConfigGeneric
• Target power at gNB receiver (dBm)
• UE calculates: P_tx = TargetPower + PathLoss
• Typical Range: -120 to -90 dBm
• Recommended: -100 to -110 dBm
Power Calculation Formula
P_tx_preamble = PreambleInitialReceivedTargetPower + PathLoss
(PathLoss derived from RSRP measurements)
Too Low Setting Impact
• Weak preamble detection
• Increased retransmissions
• Higher RACH failure rate
• Poor connection success rate
Optimal Setting Benefits
• First-attempt preamble detection
• Minimized retransmissions
• Reduced access delay
• Optimized power consumption
Too High Setting Impact
• Excessive interference
• UE battery drain
• Receiver saturation
• Reduced cell capacity
Key Performance Indicators (KPIs) Improved
RACH Success Rate ↑
Connection Setup Time ↓
Preamble Retransmissions ↓
UE Power Efficiency ↑
Inter-cell Interference ↓
Legend
Low Power (Close UE)
Medium Power
High Power (Far UE)
PL = Path Loss

## Slide 62
5G RACH powerRampingStep Parameter Optimization
Transmit Power (dBm)
Transmission Attempts
-10
0
+10
+20
+30
1
2
3
4
5
6
7
8
Optimal Detection Zone (+5 to +15 dBm)
SUCCESS
OVERSHOOT
Power Ramping Scenarios:
1 dB Step (Too Small): Many attempts needed, high latency, may reach PreambleTransMax
4 dB Step (Optimal): Quick convergence to detection zone, balanced efficiency
8 dB Step (Too Large): Quick overshoot, excessive interference, resource waste
KPI Impact Analysis:
Latency Impact
• Small steps → High latency
• Large steps → Quick but inefficient
• Optimal: 4dB = Low latency
Resource Efficiency
• Fewer retransmissions
• Reduced PRACH congestion
• Better success rate
Interference Control
• Prevents power overshoot
• Minimizes uplink interference
• Optimal: 2-4 dB range
3GPP TS 38.331: rach-ConfigCommon → rach-ConfigGeneric → powerRampingStep

## Slide 63
5G NR PreambleTransMax Parameter Impact Analysis
UE Device
(Smartphone)
gNB
(5G Base Station)
RACH Preamble Transmission Timeline
1
Attempt 1
-120 dBm
2
Attempt 2
-117 dBm
3
Attempt 3
-114 dBm
4
SUCCESS!
-111 dBm
Avoided
Waste
Power Ramping Process:
Initial Power (-120 dBm)
+3 dB Step (-117 dBm)
+3 dB Step (-114 dBm)
+3 dB Step (-111 dBm) ✓
PreambleTransMax Settings Impact
Too Low (n3)
Gives up early
Poor success rate
Optimal (n8-10)
Balanced approach
Best performance
Too High (n200)
Wastes resources
Long delays
KPI Performance Comparison
RACH Success Rate:
75% (Too Low)
95% (Optimal)
90% (Too High)
Average Access Delay:
15ms (Too Low)
25ms (Optimal)
80mas (Too High)
Battery Impact:
Low
Moderate
High
Key Insights:
Optimal Range: n8-n10 provides best balance between success rate and resource efficiency
Power Ramping: Each retry increases transmission power by ~3dB until detected
Trade-off: Too low = poor coverage, Too high = resource waste + delays
3GPP Path: rach-ConfigCommon → rach-ConfigGeneric → PreambleTransMax

## Slide 64
Cell Selection & Contention

## Slide 65
5G RACH Contention Resolution Timer (ra-ContentionResolutionTimer)
UE
gNB
Msg1: RACH Preamble
Msg2: Random Access Response (RAR)
Msg3: Scheduled Transmission
Timer Starts
Contention Resolution
Timer Period
sl32 or sl64
(32 or 64 slots)
UE Monitors
for Msg4
Msg4: Contention Resolution Message
Timer Stops
Timer Configuration
3GPP Reference:
rach-ConfigCommon →
rach-ConfigGeneric →
ra-ContentionResolutionTimer
Recommended Setting:
sl32 or sl64 (32 or 64 slots)
Default/Typical:
Often sl64
Impact on KPIs:
• Too Short: UE aborts RACH early
• Too Long: Increases latency
• Optimal: Balances success rate
and latency performance
Timer Expiry Scenario
If timer expires before Msg4:
1. RACH procedure fails
2. UE may retry RACH
3. Increased access delay
4. Potential call setup failure
Optimization Strategy:
Set timer considering:
• gNB processing time
• Network load conditions
Time →
Timer Start
Msg4 Received

## Slide 66
RACH Success Rate Optimization Strategy
1. MONITOR & BASELINE
• Monitor RACH Success Rate KPI
• Identify problematic cells
• Establish baseline metrics
• Identify problematic areas
2. ANALYZE ROOT CAUSES
• Drive tests & counters analysis
• Msg1/Msg2 failure analysis
• Resource limitation check
• Coverage issue identification
3. ITERATIVE ADJUSTMENT
• Parameter optimization
• Power control tuning
• Resource configuration
• Coverage optimization
4. VERIFY &
RE-EVALUATE
• Monitor KPI changes
• Validate improvements
• Check trade-offs
POWER CONTROL PARAMETERS
PreambleInitialReceivedTargetPower
PowerRampingStep
PreambleTransMax
RSRP-ThresholdSSB
Purpose: Optimal initial power
and efficient ramping control
Balance success vs latency
Coverage edge optimization
RESOURCE CONFIGURATION
PRACH-ConfigIndex
msg1-FDM
ra-ResponseWindow
restrictedSetConfig
Purpose: Capacity optimization
Resource allocation tuning
Msg2 reception improvement
Interference mitigation
ANALYSIS TOOLS & METHODS
Drive Test Analysis
Counter Monitoring
Trace Analysis
PCI Planning
Purpose: Root cause identification
Performance validation
Issue troubleshooting
Network optimization
KEY OPTIMIZATION CONSIDERATIONS
Trade-offs to Monitor:
• Increasing PreambleTransMax improves success rate but increases latency
• Higher PowerRampingStep reduces attempts but may cause interference
• More PRACH resources improve capacity but consume spectrum
Success Metrics:
• RACH Success Rate improvement (target: >95%)
• Reduced average RACH attempts per success
• Improved cell edge performance
Continuous Process:
Monitor → Analyze → Adjust → Verify → Repeat
Legend:
Process Steps
Analysis Phase
Feedback Loop

## Slide 67
RRC Connection Setup Success Rate Analysis
KPI DEFINITION
Success Rate = (Successful RRC Setup Procedures) / (Total RRC Setup Attempts)
Target: >98% | Typical Range: 95-99%
RRC CONNECTION SETUP PROCEDURE FLOW
UE
gNB
1. RRCSetupRequest (Msg3)
PUSCH
2. RRCSetup (PDSCH)
PDCCH+PDSCH
3. RRCSetupComplete
PDCCH+PUSCH
✓
SUCCESS
✗
FAILURE
ROOT CAUSES FOR LOW SUCCESS RATE
PRECEDING RACH
FAILURE
Msg1/Msg2 Issues
PRACH Detection
Power Control
Resource Conflicts
MOST COMMON
~60-70% of failures
RADIO CONDITIONS
Poor RSRP/SINR
UL Interference
DL Coverage Issues
Mobility Issues
Channel Quality
COVERAGE RELATED
~20-25% of failures
RESOURCE
AVAILABILITY
C-RNTI Shortage
PUSCH/PDSCH
Processing Load
Memory Issues
CAPACITY RELATED
~5-10% of failures
TIMER EXPIRATION
T300 Timer (UE)
T302 Timer (UE)
gNB RRC Timer
Scheduling Delays
Processing Delays
TIMING RELATED
~3-5% of failures
CONFIGURATION
ISSUES
Wrong Parameters
SIB Errors
RRC IE Issues
Security Config
PARAMETER RELATED
~2-3% of failures
NETWORK & UE
ISSUES
Backhaul Delays
Core Network
UE Implementation
UE Capability
EXTERNAL FACTORS
~1-2% of failures
OPTIMIZATION STRATEGY & KEY PARAMETERS
1. RACH OPTIMIZATION
• Fix underlying RACH
• Power control tuning
• Resource optimization
Primary Impact: 60-70%
2. COVERAGE ANALYSIS
• RF optimization
• Interference mitigation
• Cell planning review
Primary Impact: 20-25%
3. RESOURCE TUNING
• C-RNTI pool sizing
• PUSCH/PDSCH allocation
• Processing capacity
Primary Impact: 5-10%
4. TIMER OPTIMIZATION
• T300/T302 tuning
• Scheduling efficiency
• Processing delays
Primary Impact: 3-5%
5. CONFIG REVIEW
• Parameter validation
• SIB consistency
• RRC IE correctness
Primary Impact: 2-3%
6. MONITORING
• Continuous KPI tracking
• Root cause analysis
• Performance validation
Ongoing Process
KEY PARAMETERS TO MONITOR & OPTIMIZE
RRC Timers:
• T300 (RRC Setup Timer) • T302 (RRC Reject Timer)
Resource Parameters:
• C-RNTI Pool Size • PUSCH/PDSCH Allocation
Coverage Parameters:
• Reference Signal Power • Coverage Thresholds
Processing Parameters:
• Scheduling Efficiency • Load Balancing
OPTIMIZATION PRIORITY: Start with RACH (highest impact) → Coverage → Resources → Timers → Configuration

## Slide 68
5G RRC Connection Setup Timers - Technical Architecture
3GPP TS 38.331 | Critical Parameters for Latency & Success Rate Optimization
UE (User Equipment)
T300 Timer
Started: RRCSetupRequest
Stopped: RRCSetup received
Expire: Connection Failed
Recommended: 200-300ms
Balance: Speed vs Reliability
Default: 300ms typical
UE Process Flow
1. Send RRCSetupRequest
2. Start T300 Timer
gNB (Base Station)
Internal Timers
RRCSetupRequest Processing
RRCSetup Transmission
RRCSetupComplete Wait
Performance Factors
• CPU Load & Processing
• C-RNTI Pool Availability
• Backhaul Latency
• Scheduling Efficiency
Vendor Tunable
Internal Algorithm Optimization
1. RRCSetupRequest
T300 Timer Started
gNB Processing Time (Critical Window)
Resource Allocation | Authentication | Bearer Setup
2. RRCSetup
Must arrive before T300
3. RRCSetupComplete
Connection Established
Timeout/Failure → Restart RACH
KPI Impact Analysis
RRC Setup Success Rate
Too Short T300
• Premature timeout during load spikes
• Higher failure rate in edge coverage
Too Long T300
• Resource waste on bad connections
Connection Setup Latency
High Load Impact: 50% increase
Optimized: 40% improvement
Optimal T300 + gNB tuning = Best UX
Optimization Strategy (3GPP TS 38.331)
UE Side:
• T300 = 200-300ms (balance reliability vs speed)
• Monitor coverage conditions for adaptive timeout
gNB Side:
• Adequate CPU/memory provisioning
• C-RNTI pool sizing, efficient scheduling algorithms
3GPP TS 38.331 - MeasAndMobParametersMRDC
Target: >95% Success Rate, <100ms Setup Time

## Slide 69
RACH Parameters - Prerequisites for RRC Setup
UE
gNB
MSG1: PRACH Preamble
MSG1 Parameters
• PreambleInitialReceivedTargetPower
• powerRampingStep
• PRACH-ConfigIndex
Configuration
• msg1-FDM
• PreambleTransMax
(Max attempts)
MSG2: RAR (Random Access Response)
MSG2 Timing
• ra-ResponseWindow
(Window to receive RAR)
MSG3: RRC Setup Request
RRC Connection Starts
MSG4: Contention Resolution
Contention Resolution
• ra-ContentionResolutionTimer
(Critical for contention-based RACH)
Power Ramping Process
P1
P2
P3
P4
Initial Power + (Attempt × powerRampingStep)
Max attempts = PreambleTransMax
Each step increases transmission power
Critical Timer Windows
ra-ResponseWindow (MSG2 timeout)
ra-ContentionResolutionTimer (MSG4)
Timers ensure proper procedure completion
Failure triggers retransmission or abort
Parameter Relationships
🔗 PRACH-ConfigIndex defines time/frequency
🔗 msg1-FDM affects preamble multiplexing
🔗 Power ramping prevents interference
🔗 Timer windows ensure reliability
🔗 All parameters must be optimized together
RRC Connected

## Slide 70
3GPP Parameters for RRC Connection Setup Success Rate Improvement
Parameter Name | 3GPP Reference (IE Path in SIB1) | Explanation | Default/Typical Setting | Recommended Setting | How it Helps Improve RRC KPI
I. RRC Connection Setup Timers (Critical for Latency & Success) |  |  |  |  | 
T300 (ms) | servingCellConfigCommon -> rrc-SetupCommon -> T300 (implicitly derived from rrc-config in some structures, or similar) | The UE starts this timer when it sends RRCSetupRequest. If no RRCSetup message is received before T300 expires, the UE aborts the RRC connection attempt. | ms300 (300ms) | ms200 or ms300 (200-300ms) | Crucial. If too short, UE aborts prematurely, even if gNB is slightly delayed, leading to RRC failures. If too long, increases latency. Ensures UE waits long enough for gNB response.
ra-ContentionResolutionTimer (slots) | rach-ConfigCommon -> rach-ConfigGeneric -> ra-ContentionResolutionTimer | In contention-based RACH, this timer is started by the UE after transmitting Msg3 (RRCSetupRequest). If Msg4 (Contention Resolution) is not received before this timer expires, the RACH (and thus RRC) procedure fails. | sl64 (64 slots) | sl32 or sl64 (32-64 slots) | Indirect but Critical. For contention-based RRC setup, a too-short timer can cause failure even if the gNB is processing Msg3. Ensures UE waits sufficiently for Msg4, completing the prerequisite RACH before RRCSetup.
II. Physical Layer and Resource Configuration for RRC Messages |  |  |  |  | 
msg3-DeltaPreamble (dB) | rach-ConfigCommon -> msg3-DeltaPreamble | Power offset between the last transmitted preamble (Msg1) and the first uplink transmission on UL-SCH (Msg3, which carries RRCSetupRequest). | 0 dB | 0 dB or 1 dB | Direct. Optimizes the transmit power for RRCSetupRequest. If too low, RRCSetupRequest might not be detected. If too high, causes excessive UL interference. A balanced value ensures reliable reception.
msg3-TransformPrecoding | rach-ConfigCommon -> msg3-TransformPrecoding | Enables or disables transform precoding for Msg3 transmission. Transform precoding improves UL coverage and power efficiency. | Enabled for FR1 typically | Enabled | Direct. Enhances the reliability of RRCSetupRequest transmission, especially at cell edge, by providing better SINR at the gNB, reducing Msg3 detection failures.
PDCCH-ConfigCommon (via controlResourceSetZero and searchSpaceZero) | sib1 -> controlResourceSetZero, searchSpaceZero | These configure the common CORESET and search space where the UE monitors PDCCH for initial access, including the scheduling of RRCSetup and the UL grant for RRCSetupComplete. | Varies by SIB1 and pdcch-ConfigSIB1 settings. | Ensure optimal power allocation for PDCCH and robust MCS (e.g., QPSK) for common search space. | Direct. If PDCCH is not reliably received, the UE cannot get the scheduling information for RRCSetup (DL) or the UL grant for RRCSetupComplete (UL), leading to RRC failures.
pdsch-ConfigCommon (relevant for RRCSetup message) | sib1 -> pdsch-ConfigCommon | Defines common PDSCH configurations, including MCS tables, resource allocation types, and rate matching. Affects how RRCSetup is transmitted on PDSCH. | Varies (e.g., MCS table, R-match pattern) | Ensure robust MCS (e.g., lower order modulation like QPSK) and proper rate matching for common channels. | Direct. The RRCSetup message is critical. Using robust physical layer settings for its transmission ensures it can be reliably decoded by the UE, even in challenging radio conditions.
pusch-ConfigCommon (relevant for RRCSetupComplete message) | sib1 -> pusch-ConfigCommon | Defines common PUSCH configurations, including MCS tables and transform precoding for common channels. Affects how RRCSetupComplete is transmitted on PUSCH. | Varies | Similar to pdsch-ConfigCommon, ensure robust MCS and optimal transform precoding for UL common channels. | Direct. RRCSetupComplete confirms the RRC connection. Robust UL settings ensure this final critical message is reliably received by the gNB, preventing RRC setup failures.

## Slide 71
3GPP Parameters for RRC Connection Setup Success Rate Improvement
Parameter Name | 3GPP Reference (IE Path in SIB1) | Explanation | Default/Typical Setting | Recommended Setting | How it Helps Improve RRC KPI
III. RACH Resource & Signaling (Prerequisites for RRC) |  |  |  |  | 
PreambleInitialReceivedTargetPower (dBm) | rach-ConfigCommon -> rach-ConfigGeneric -> PreambleInitialReceivedTargetPower | The target power level at which the gNB expects to receive the first preamble transmission from the UE. UE calculates its initial preamble TX power based on this. | -100 dBm to -110 dBm | Adjust between -120 dBm and -90 dBm. Lower for larger cells/poor coverage, higher for good coverage. | Indirect but foundational. Successful RACH is a prerequisite for RRC setup. Optimal preamble power ensures the first step of initial access is robust, allowing the UE to proceed to RRCSetupRequest.
powerRampingStep (dB) | rach-ConfigCommon -> rach-ConfigGeneric -> powerRampingStep | Step size by which the UE increases its preamble transmit power for subsequent retransmissions if the previous attempt fails. | 4 dB | 2 dB or 3 dB | Indirect but foundational. Efficient power ramping helps the UE quickly find the optimal power for preamble detection, reducing RACH retransmissions and improving the chance of reaching the RRC setup phase.
PreambleTransMax | rach-ConfigCommon -> rach-ConfigGeneric -> PreambleTransMax | Maximum number of preamble retransmissions allowed before the RACH procedure is considered a failure by the UE. | n10 or n20 (10 or 20) | n8 or n10 (8 or 10) | Indirect but foundational. A balanced value allows sufficient attempts for preamble detection without excessive delay, ensuring the UE doesn't give up too early on RACH.
ra-ResponseWindow (slots) | rach-ConfigCommon -> rach-ConfigGeneric -> ra-ResponseWindow | The time window during which the UE monitors PDCCH for the Random Access Response (RAR/Msg2) after transmitting a preamble. | sl20 (20 slots) | sl20 or sl40 (20-40 slots) | Indirect but foundational. A sufficiently long window ensures the UE receives Msg2 from the gNB, allowing the RACH procedure to complete and the UE to send RRCSetupRequest.

## Slide 72
3GPP Parameters for RRC Connection Setup Success Rate Improvement
Parameter Name | 3GPP Reference (IE Path in SIB1) | Explanation | Default/Typical Setting | Recommended Setting | How it Helps Improve RRC KPI
III. RACH Resource & Signaling (Prerequisites for RRC) |  |  |  |  | 
PRACH-ConfigIndex | rach-ConfigCommon -> prach-Config -> prach-ConfigIndex | Points to a 3GPP table specifying PRACH configuration (preamble format, SCS, periodicity, slots, etc.). | Varies by deployment | Select an index providing sufficient PRACH capacity/frequency for expected RACH load. | Indirect but foundational. Determines the availability and type of PRACH resources. Insufficient or misaligned PRACH resources can lead to preamble collisions or inability to find resources, failing RACH before RRC setup.
msg1-FDM (Frequency Division Multiplexing) | rach-ConfigCommon -> rach-ConfigGeneric -> msg1-FDM | Specifies the number of frequency-multiplexed PRACH occasions within a given time resource. | 1 or 2 | 2, 4, or 8 (increase for higher load) | Indirect but foundational. Increases the number of available RACH resources per PRACH occasion, enhancing the capacity for simultaneous random accesses. This reduces preamble collisions and congestion, boosting RACH success.
restrictedSetConfig | rach-ConfigCommon -> prach-Config -> restrictedSetConfig | Restricts the set of Zadoff-Chu sequences (preambles) that can be used. | unrestrictedSet | unrestrictedSet as default. Use restrictedSetTypeA or restrictedSetTypeB in interference-limited scenarios. | Indirect but foundational. Helps reduce inter-cell preamble interference and false detections, leading to more reliable Msg1 reception and hence more successful RACH procedures.
IV. Cell Selection/System Information (Foundational for Initial Access) |  |  |  |  | 
q-RxLevMin / ssb-RSRP (dBm) | cellReselectionInfoCommon -> q-RxLevMin (for LTE/NR inter-RAT); servingCellConfigCommon -> ssb-RSRP (for NR cell selection) | Minimum RSRP level required for a UE to select a cell for initial access and RRC setup. | -128 dBm (often) | Between -120 dBm and -130 dBm. | Indirect but essential. If set too low, UEs might attempt RRC setup on cells with very poor radio conditions where success is unlikely, artificially lowering the KPI. Ensures attempts are made on cells with a reasonable chance of success.
pdcch-ConfigSIB1 / pdsch-ConfigSIB1 | sib1 -> pdcch-ConfigSIB1, pdsch-ConfigSIB1 (implicit) | These common configurations define how SIB1 is scheduled and transmitted (e.g., CORESET, search space, MCS for SIB1). | Varies by vendor/deployment | Ensure robust MCS (e.g., QPSK) and adequate power for SIB1 transmission. | Foundational. SIB1 carries all the essential parameters (including many above) for initial access and RRC setup. If SIB1 is not reliably received, the UE cannot even attempt RACH or RRC.

## Slide 73
Retainbility KPI

## Slide 74
Call Drop Rate Analysis - Radio Link Failure (RLF) Root Causes
Call Drop Rate Formula:
CDR = (Number of abnormal call/session terminations)
÷ (Total number of successfully established calls/sessions)
Primary Root Cause: Radio Link Failure (RLF)
Key Definition:
Abnormal terminations are those NOT initiated by:
• User actions (e.g., end call button)
• Network legitimate reasons (e.g., session timeout)
7 Primary Causes of Call Drops Leading to RLF
1
Poor Radio Conditions
• Persistent weak signal (RSRP)
• Low SINR in UL/DL
• Signal degradation
2
Mobility Issues
• Failed handovers (inter/intra-gNB)
• Inter-RAT handover failures
• Beam mobility failures (FR2)
3
Interference
• High UL/DL interference
• Corrupted data signals
• Control signal corruption
4
Resource Limitations
• Insufficient PDCCH capacity
• PUSCH/PDSCH RB shortage
• Scheduling failures
5
gNB/Core Network Issues
• Network overload conditions
• Hardware/software faults
• Backhaul congestion
6
UE Issues
• Faulty UE hardware
• Software bugs/issues
• Abnormal UE behavior
7
Protocol/Timer Mismatches
• Incorrect timer configurations at RLC, PDCP, or RRC layers
• Premature RLF declaration due to timer mismatches
• Protocol stack synchronization issues
RLF
CALL DROP
5G Network Optimization: Understanding and Mitigating Call Drop Scenarios
Comprehensive analysis of RLF root causes for improved network performance and user experience

## Slide 75
Call Drop Rate Improvement Plan
Parameter Name | 3GPP Reference (Relevant Context) | Explanation | Default/Typical Setting | Recommended Setting | How it Helps Improve Call Drop KPI
maxRetxThreshold | RLC-Config -> am-Config -> maxRetxThreshold | Defines the maximum number of retransmissions for an RLC PDU (Protocol Data Unit) or SDU (Service Data Unit) before the RLC entity indicates a failure to the higher layer (PDCP). | t8 (8 retransmissions), t16 (16 retransmissions), t32 (32 retransmissions) | t16 or t32 (Higher value for robustness, especially in cells with fluctuating radio conditions) | Direct. A higher maxRetxThreshold allows the RLC layer more attempts to successfully deliver data over the air interface, increasing robustness against transient radio issues and delaying the declaration of RLF. This directly reduces call drops caused by temporary data loss.
pollPDU | RLC-Config -> am-Config -> pollPDU | Specifies that a POLL (request for RLC Status Report) is triggered every pollPDU number of RLC SDUs transmitted. | p4, p8, p16, p32, p64, p128, p256, pInfinity (often p8 or p16) | p4 or p8 (Lower value to detect errors faster) | Direct. A lower pollPDU value means the UE/gNB requests status reports more frequently. This allows faster detection of missing RLC PDUs and quicker retransmission initiation, reducing overall data loss and preventing RLF from prolonged data stalls.
pollByte | RLC-Config -> am-Config -> pollByte | Specifies that a POLL is triggered every pollByte number of bytes transmitted. | kB1, kB2, kB4, etc. (often kB2 or kB4) | kB1 or kB2 (Lower value to detect errors faster) | Direct. Similar to pollPDU, a lower pollByte value triggers status reports more often. This is beneficial for applications with large data bursts, ensuring timely error detection and retransmissions, thus contributing to call stability.
t-PollRetransmit (ms) | RLC-Config -> am-Config -> t-PollRetransmit | Timer for retransmitting a POLL (status report request) if no corresponding STATUS PDU is received. | ms45, ms50, ms55, ..., ms500 (e.g., ms100) | ms80 to ms150 (Adjust based on latency requirements and radio conditions) | Direct. If a POLL is sent but no status report is received, this timer dictates how long the RLC entity waits before sending another POLL. A shorter timer leads to faster retransmission attempts, improving the chances of recovering lost RLC PDUs before RLF is triggered.
t-Reassembly (ms) | RLC-Config -> am-Config -> t-Reassembly | Timer used by the receiving RLC entity to reassemble an SDU from received RLC PDUs. If parts of an SDU are missing and this timer expires, the partial SDU is discarded. | ms35, ms40, ms45, ..., ms500 (e.g., ms100) | ms100 to ms200 (Slightly higher value for robustness in poor conditions) | Indirect. If this timer expires due to missing segments, the entire SDU is discarded, leading to data loss at the RLC layer. A slightly longer t-Reassembly gives more time for delayed or retransmitted segments to arrive, improving in-sequence delivery and reducing data loss that might contribute to higher layer failures.
t-StatusProhibit (ms) | RLC-Config -> am-Config -> t-StatusProhibit | Timer that prevents an RLC entity from sending too many STATUS PDUs (reports) in a short period. | ms0, ms5, ms10, ..., ms500 (e.g., ms10 or ms20) | ms10 to ms30 (Balance between rapid error reporting and resource consumption) | Indirect. While higher values can reduce signaling overhead (saving resources), excessively high values might delay the gNB/UE from receiving critical status information about lost PDUs, potentially slowing down recovery and contributing to RLF. A balanced value ensures timely reporting without overwhelming the control channels.
RLC Parameters (Acknowledged Mode - AM, most relevant for call drops):

## Slide 76
Call Drop Rate Improvement Plan
Parameter Name | 3GPP Reference (Relevant Context) | Explanation | Default/Typical Setting | Recommended Setting | How it Helps Improve Call Drop KPI
I. Radio Link Failure (RLF) Detection & Recovery |  |  |  |  | 
T310 (ms) | RRCReconfiguration / RRCSetup -> radioLinkMonitoringConfig -> T310 | Timer started by the UE when it detects "out-of-sync" conditions (e.g., too many consecutive negative physical layer indications from lower layers like PHY/MAC). | ms0, ms200, ms500, ms1000, ms2000 (e.g., ms500) | ms1000 or ms2000 (Higher for robustness) | Critical. A higher T310 allows the UE to tolerate longer periods of poor radio conditions (e.g., temporary fading or interference) before declaring an RLF, thus preventing premature call drops.
N310 | RRCReconfiguration / RRCSetup -> radioLinkMonitoringConfig -> N310 | Number of consecutive "out-of-sync" indications from the physical layer required for the UE to start T310. | n1, n2, n3, n4, n6, n8, n10, n20 (e.g., n10) | n10 or n20 (Higher for robustness) | Critical. A higher N310 makes the RLF detection more robust to sporadic physical layer issues, preventing the premature start of T310 and declaration of RLF.
T311 (ms) | RRCReconfiguration / RRCSetup -> radioLinkMonitoringConfig -> T311 | Timer started by the UE upon declaring an RLF. During this time, the UE attempts RRC re-establishment. If re-establishment fails, the connection is dropped. | ms1000, ms3000, ms5000, ms10000, ms30000 (e.g., ms5000) | ms5000 or ms10000 (Higher for more recovery time) | Critical. A longer T311 gives the UE more time to successfully re-establish an RRC connection (e.g., by performing a handover to a better cell) after an RLF, thereby salvaging the call.
N311 | RRCReconfiguration / RRCSetup -> radioLinkMonitoringConfig -> N311 | Number of consecutive "in-sync" indications from the physical layer required to stop T310. | n1, n2, n3, n4, n5, n6, n8, n10 (e.g., n1) | n1 or n2 (Lower for faster recovery from T310 start) | Important. A lower N311 allows the UE to quickly stop T310 if radio conditions improve rapidly, preventing unnecessary RLF declarations.
II. Mobility and Handover Optimization |  |  |  |  | 
A3-Offset (dB) | MeasObjectNR -> reportConfigNR -> reportConfigA3 -> a3-Offset | Defines the offset for the A3 event, which triggers inter-frequency/inter-RAT handovers when neighbor cell RSRP becomes serving cell RSRP + offset. | 0 to 6 dB (e.g., 2 dB) | 1 dB to 3 dB (Lower for quicker handover, higher for stickiness) | Crucial. An optimized A3-Offset ensures timely handovers to stronger target cells, preventing the serving cell's signal from degrading to a point where RLF is triggered. Too high a value can delay HO, too low can cause ping-pong.
Hysteresis (dB) | MeasObjectNR -> reportConfigNR -> reportConfigA3 -> hysteresis | Margin applied to measurement events to prevent frequent triggering (ping-pong effect). | 0 to 4 dB (e.g., 0 dB or 1 dB) | 0 dB to 2 dB (Lower for faster HO, higher for stability) | Important. Prevents unnecessary handovers back and forth between cells, which can consume resources and lead to instability, reducing the chance of mobility-related drops.
TimeToTrigger (ms) | MeasObjectNR -> reportConfigNR -> reportConfigA3 -> timeToTrigger | Duration for which a measurement event condition must be continuously met before the UE sends a measurement report. | ms0, ms40, ms64, ms100, ..., ms5120 (e.g., ms256) | ms128 to ms512 (Balance between fast reaction and avoiding spurious triggers) | Crucial. A well-tuned TimeToTrigger ensures the UE only initiates handover when the target cell's signal is consistently better, preventing drops from "bad" handovers to temporarily strong but unstable cells.
drx-Config (drx-onDurationTimer, drx-inactivityTimer, etc.) | DRX-Config (part of MAC-CellGroupConfig) | Defines the Discontinuous Reception (DRX) cycle, balancing power saving vs. latency. | Varies greatly (e.g., onDurationTimer=psf16, inactivityTimer=psf256) | Tune based on traffic profile: Shorter timers/cycles for active users, longer for inactive. | Indirect. While primarily for power saving, an overly aggressive DRX configuration (too long drx-inactivityTimer, too short drx-onDurationTimer) can cause delays in receiving DL assignments, leading to data buffering issues at gNB/UE, potentially triggering RLC/PDCP failures that contribute to RLF.

## Slide 77
The Three Key Parameters
Parameter | Layer | Description
t-PollRetransmit | RLC (Radio Link Control) | Determines how long the RLC entity waits for a Status Report from its peer after sending a PDU with a "POLL" bit. A POLL is a request for the receiver to report what it has successfully received.
maxRetxThreshold | RLC (Radio Link Control) | The maximum number of times a single RLC SDU (Service Data Unit) or a segment of it can be retransmitted. It's a failure counter, not a timer.
t310 | RRC (Radio Resource Control) | The "Radio Link Failure" timer. It starts when the UE's physical layer detects a serious problem (N310 consecutive "out-of-sync" indications). If the link doesn't recover before t310 expires, the UE declares a Radio Link Failure (RLF) and drops the connection.

## Slide 79
Scenario | maxRetxThreshold Setting | t-PollRetransmit (ms) Setting | t310 (ms) Setting | Rationale & Goal | Pros | Cons
Excellent Coverage / Stable RF (e.g., Indoor Small Cell, FWA) | Low (e.g., 4, 8) | Short (e.g., 45-80 ms) | Short (e.g., 500-1000 ms) | Goal: High Performance. Failures are rare and likely permanent. Detect and act on them quickly for low latency. | Fast Failure Detection: Quickly identifies non-recoverable links. ,Low Latency: Reduces delays caused by waiting for retransmissions. | Low Resilience: Can be too sensitive to brief, transient interference, leading to unnecessary connection drops.
Cell Edge / Poor RF (e.g., Rural, Indoor Fringe) | High (e.g., 16, 32) | Long (e.g., 120-200 ms) | Long (e.g., 2000-4000 ms) | Goal: High Stability. Packet loss is expected. Tolerate temporary link degradation to maintain the connection. | High Connection Stability: Prevents drops during temporary fades. ,Improved User Experience: The user perceives a slow but connected session rather than a dropped one. | Slow Failure Detection: Masks underlying permanent issues. ,Increased Latency: High buffer delay as the system waits longer to retransmit and recover.
High Mobility (e.g., Vehicle, High-Speed Train) | Medium (e.g., 8, 16) | Medium (e.g., 80-120 ms) | Medium-Long (e.g., 1000-2000 ms) | Goal: Balance. Tolerate handover-related interruptions but don't wait indefinitely if the handover fails or the UE loses coverage. | Robust Handover Performance: t310 is long enough to allow a handover to complete. ,Good compromise: Balances stability with responsiveness. | Can be a sub-optimal "one-size-fits-all" setting if the user stops or enters a very poor coverage zone.
Massive IoT (mMTC) (e.g., Smart Meters, Sensors) | High (e.g., 16, 32, or higher) | Long (e.g., 200-500 ms) | Very Long (e.g., 4000-6000 ms) | Goal: Maximize Battery & Connection. Latency is not a concern. Avoid RRC state transitions (Idle <-> Connected) which drain power. | Excellent Connection Retention: Keeps devices connected even in deep indoor locations with fluctuating links. ,Power Savings: Avoids costly re-establishment procedures. | Extremely Slow Reaction: Unsuitable for any application needing timely data. ,Can tie up network resources for devices that are permanently out of reach.
Call Drop Rate Improvement Plan

## Slide 82
t-PollRetransmit Timer - 5G RLC Acknowledged Mode Error Recovery
5G Protocol Stack
PDCP
RLC AM
t-PollRetransmit
MAC
gNB
RLC Sender
t-PollRetransmit
Timer
UE
RLC Receiver
STATUS PDU
Generator
t-PollRetransmit Process Flow & Timeline
Time →
T0
T1
T2
T3
T4
Step 1
Send Data + POLL
Start t-PollRetransmit
RLC PDU + POLL
Normal Case
STATUS PDU Received
Stop Timer
STATUS PDU (ACK)
Lost STATUS
STATUS PDU Lost
Timer Continues
STATUS PDU (LOST)
✗
Step 4
t-PollRetransmit
EXPIRES
Re-POLL + Retx Data
Restart Timer
RE-POLL + Data
t-PollRetransmit Timer Duration
Timer Stopped (STATUS received)
Timer Expires → Retransmission Triggered
≤ 100ms (Good)
≥ 200ms (Slow Recovery)
RLC AM Algorithm Summary
1. Send RLC PDU(s) → Set POLL bit → Start t-PollRetransmit
2. If STATUS PDU received → Stop timer | If timer expires → Re-POLL + Retransmit unACKed data
Configuration Guide
Timer Values:
❌ Too High (≥200ms):
• Slow error recovery
• Higher layer timeouts
✅ Optimal (80-150ms):
• Fast error detection
• Balanced signaling overhead
⚠️ Too Low (≤50ms):
• Excessive control signaling
• Network congestion
KPI Impact:
✓ Reduces Call Drop Rate
✓ Faster Data Recovery
✓ Better Throughput
Scenario Analysis
High Timer (200ms)
• STATUS PDU lost
• Wait 200ms for retry
• Data stall → RLF risk
Result: Call Drop ✗
Optimal Timer (100ms)
• STATUS PDU lost
• Quick retry in 100ms
• Fast data recovery
Result: Call Continues ✓
Performance:
• Recovery Time: 50% faster
• Call Drop: 20-30% reduction
• Throughput: 15% improvement
3GPP Technical Implementation Details
3GPP Reference:
• TS 38.322 (RLC Protocol Specification)
• RLC-Config → am-Config → t-PollRetransmit
• Timer values: ms5, ms10, ms15, ms20, ms25, ms30, ms35, ms40, ms45, ms50,
ms55, ms60, ms65, ms70, ms75, ms80, ms85, ms90, ms95, ms100, ms105, ms110,
ms115, ms120, ms125, ms130, ms135, ms140, ms145, ms150, ms155, ms160...
• Configured per RLC bearer during RRC connection setup
Implementation Notes:
• Works in conjunction with pollPDU and pollByte parameters
• Sender maintains VT(S), VT(A), VT(MS) state variables
• STATUS PDU contains ACK_SN and NACK_SN information
• Retransmission triggered for SN < VT(A) + AM Window Size
• maxRetxThreshold limits total retransmission attempts
• RLC failure indication sent to upper layers if threshold exceeded

## Slide 84
5G RLC t-Reassembly Timer Mechanism
Preventing Premature SDU Discard in Acknowledged Mode
Legend:
Successfully Received PDU
Missing/Lost PDU
Retransmitted PDU
Timer Active
RLC SDU Reassembly Process Timeline
Time
T0
T1
T2
T3
T4
Transmitter (gNB/UE)
RLC SDU Segmentation
PDU#1
PDU#2
LOST
PDU#3
PDU#2
Retx
Receiver (UE/gNB)
PDU#1
✓ Received
Gap Detected!
PDU#3
Out of Order
t-Reassembly Timer Active (100ms)
75% elapsed
PDU#2
✓ Gap Filled
Timer Stopped
Complete SDU Delivered
Problem: Short Timer (50ms)
• Timer expires before retransmission
• Incomplete SDU discarded prematurely
• Higher layer must request full retransmission
• Increased call drop probability
• Poor user experience in high-loss areas
Solution: Optimal Timer (100-200ms)
• More time for retransmissions to arrive
• Reduced premature SDU discards
• Better RLC layer reliability
• Improved call success rate
• Enhanced user experience
Key Parameters
3GPP Reference:
RLC-Config → am-Config → t-Reassembly
Default Setting:
ms100 to ms150
Recommended Setting:
ms100 to ms200

## Slide 86
Mobility Optimization

## Slide 87
FR1: 3.5 GHz (n78)
FR1 : 2.6 GHz
Source Cell (gNB-1)
PCI: 237
BW: 100 MHz
RSRP: -95 dBm
Target Cell (gNB-2)
PCI: 428
BW: 100 MHz
RSRP: -80 dBm
5G Core Network
AMF | SMF | UPF | PCF | NSSF
SA Architecture
UE
IMSI: 311480012345678
Velocity: 60 km/h
Xn Interface
1
Measurement Reports
Event A3 Triggered
2
Handover Decision
TTT: 160 ms
3
HO Preparation
Xn Signaling
4
HO Execution
RRC Reconfig
5
HO Completion
Path Switch Req
5G NR Handover Process
3GPP TS 38.300 | Release 17 | SA Architecture
SINR: 10 dB
SINR: 22 dB
Technical Parameters
• HO Margin: 3 dB
• A3 Offset: 2 dB
• HO Type: Intra-frequency
• MIMO: 4x4
Connection Status
Active Data Connection
Xn/X2 Interface

## Slide 88
Types of Handover in 5G NR
Intra-frequency Handover
Cell A (3.5 GHz)
Cell B (3.5 GHz)
Same Frequency Band
Inter-frequency Handover
Cell A (3.5 GHz)
Cell B (2.1 GHz)
Different Frequency Bands
Inter-RAT Handover
5G NR Cell
LTE Cell
Different Radio Technologies
Handover Complexity
Complexity Level
Intra-frequency
Inter-frequency
Inter-RAT
Key Considerations
Signal Measurement: UE measures RSRP, RSRQ, and SINR of serving and neighboring cells
Handover Margin: Controls handover trigger point (typically 2-3 dB)
Time-to-Trigger (TTT): Prevents ping-pong effect (range: 0-5120ms)

## Slide 89
5G NR Measurement Configuration & Reporting
UE
Serving gNB
PCI: 254
Neighbor gNB 1
PCI: 368
Neighbor gNB 2
PCI: 472
1. Measurement Configuration
3. Measurement Reports
Serving Cell
RSRP: -85 dBm
RSRQ: -9 dB
SINR: 18 dB
Neighbor Cell 1
RSRP: -92 dBm
RSRQ: -11 dB
SINR: 12 dB
2. Measurement Configuration Parameters
Measurement Objects
• NR Intra-freq: SSB Freq 640000
• NR Inter-freq: SSB Freq 643000
• Inter-RAT: ARFCN 2850 (LTE)
• FR1 Band: n78 (3.5 GHz)
Reporting Configuration
• Event A3: Neighbor > Serving+Offset
• Offset: 3 dB
• Time-To-Trigger (TTT): 320 ms
• Report Interval: 240 ms
• Report Amount: Infinity
Measurement Attributes
• Quantity: RSRP, RSRQ, SINR
• Max Cells: 8
• Filter Coefficient: fc4
• Cell-Individual Offset: 0 dB
• Measurement IDs: 1, 2, 3
Signal Measurements
• RSRP: Reference Signal Received Power
• RSRQ: Reference Signal Received Quality
• SINR: Signal to Interference plus Noise Ratio
• SSB: Synchronization Signal Block

## Slide 90
5G NR Measurement Types
Key metrics for handover decisions in next-generation networks
RSRP
Reference Signal Received Power
UE
-80
-120 dBm
-100 dBm
-80 dBm
What it measures:
• Linear average power of
Cell-specific Reference Signals
Indicates:
• Pure signal strength
• Higher = stronger signal
RSRQ
Reference Signal Received Quality
UE
-12
-20 dB
-15 dB
-5 dB
What it measures:
• Ratio of RSRP to total
received power (RSSI)
Indicates:
• Signal quality relative to
interference and noise
SINR
Signal-to-Interference-plus-Noise Ratio
Signal
I+N
15 dB
15
0 dB
10 dB
20+ dB
What it measures:
• Ratio of desired signal power
to interference plus noise
Indicates:
• Direct signal quality
• Higher potential data rates
Handover Decision Framework
1
RSRP
Trigger Point
Target > Serving + Margin
2
RSRQ
Quality Verification
Ensures target cell quality
3
SINR
QoS Prediction
Expected throughput

## Slide 91
5G NR Handover Decision
Source gNB
Serving Cell
Target gNB
Neighboring Cell
UE
Measurement Reports
Handover Decision Analysis
Measurement Comparison:
Source: RSRP -102 dBm | Target: RSRP -88 dBm
Hysteresis
Threshold: 3 dB
Status: Satisfied
Time-to-Trigger
Value: 320 ms
Signal Trends
Source Cell
Target Cell
Crossover
Decision Result
✓
Handover
Initiate to Target gNB
Abbreviations
• RSRP: Reference Signal Received Power
• RSRQ: Reference Signal Received Quality
• SINR: Signal-to-Interference-plus-Noise Ratio

## Slide 92
5G NR Idle Mode: Cell Reselection Process
UE
Serving Cell
Rs = Qmeas,s + QHyst
Neighbor Cell
Rn = Qmeas,n - Qoffset
System Information
Parameters in SIB1:
• s-NonIntraSearchP/Q
• q-Hyst, q-OffsetFreq
• t-ReselectionNR
Measures
RSRP/RSRQ
Measures
RSRP/RSRQ
Network Parameters
Reselection Criteria
1. S-Criteria met
2. Rn > Rs
3. For t-Reselection time
UE-Autonomous Decision
Rs = Qmeas,s + QHyst
Rn = Qmeas,n - Qoffset
If Rn > Rs for t-Reselection → Reselect
Key Parameters
RSRP: Reference Signal Received Power
RSRQ: Reference Signal Received Quality
SIB: System Information Block

## Slide 93
Event A1: Serving Cell Becomes Better Than Threshold
Time (ms)
0
200
400
600
800
RSRP (dBm)
-90
-100
-110
-120
-130
-140
Threshold_A1
(-100 dBm)
Hysteresis (2dB)
Serving Cell RSRP
TTT = 320ms
-134 dBm
-120 dBm
-107 dBm
-100 dBm
Event A1 Triggered
-94 dBm
5G NR Event A1 Parameters (Example):
• Threshold_A1 = -100 dBm (RSRP)
• Hysteresis = 2 dB
• Time-to-Trigger (TTT) = 320 ms
• Frequency = 3.5 GHz (n78)
Event A1 Condition:
Mp + Hys > Threshold_A1
RRC Signaling:
MeasConfig→MeasIdList→MeasId→MeasObjectId:1, ReportConfigId:A1

## Slide 94
Event A2: Serving Cell Below Threshold
Condition: Ms < Threshold_A2 (Serving cell quality becomes worse than configured threshold)
-110 dBm
-100 dBm
-90 dBm
-80 dBm
0s
2s
4s
6s
8s
10s
12s
14s
Time (seconds)
Signal Strength (RSRP)
Threshold_A2 = -90 dBm
Hysteresis: 2 dB
-80 dBm
-82 dBm
-92 dBm
-104 dBm
Threshold Crossing
Event A2 Triggered
After Time-to-Trigger: 1.2s
1.2 sec
Serving gNB
UE
Initial Strong Signal (-80 dBm)
Degraded Signal (-92 dBm)
gNB configures Event A2
Threshold: -90 dBm
UE monitors RSRP
Initial value: -80 dBm
RSRP < Threshold
-92 dBm < -90 dBm
Event A2 Triggered
After TTT: 1.2 seconds
UE sends Report
Measurement Report
Example Values:
• Threshold_A2: -90 dBm
• Hysteresis: 2 dB
• Time-to-Trigger: 1.2s
• Serving Cell RSRP: -92 dBm
Purpose of Event A2:
• Early warning for degrading
signal quality
• Triggers intensified neighbor
cell measurements

## Slide 95
Event A3: Neighbor Cell Better Than Serving Cell
Condition: Mn + Offset_A3 > Ms (Neighbor cell becomes better than serving cell by an offset)
-110 dBm
-100 dBm
-95 dBm
-90 dBm
-85 dBm
0s
2s
4s
6s
8s
10s
12s
14s
Time (seconds)
Signal Strength (RSRP)
-90 dBm
-92 dBm
-105 dBm
-100 dBm
-93 dBm
-85 dBm
Offset_A3 = +3 dB
Mn + Offset_A3 > Ms
TTT: 1s
Event A3 Triggered
Serving Cell
RSRP: -92 dBm
Neighbor Cell
RSRP: -89 dBm
UE
Evaluation:
-89 dBm + 3 dB (-86 dBm) > -92 dBm
Configure Event A3
Offset_A3: +3 dB, TTT: 1s
UE Measures Cells
Serving: -92 dBm, Neighbor: -89 dBm
A3 Condition Met
-89 dBm + 3 dB > -92 dBm
Event A3 Triggered
After Time-to-Trigger (1s)
UE Reports to gNB
Measurement Report (A3)
Event A3 Parameters:
• Offset_A3: +3 dB
• Time-to-Trigger: 1 second
• Hysteresis: 1 dB
• reportAmount: infinity
• triggerQuantity: RSRP
• reportQuantity: RSRP,RSRQ
Technical Notes:
• Primary handover event
• Used for both intra and inter
• Relative comparison
• Network can tune offset to
control handover aggressiveness
• Prevents ping-pong effects

## Slide 96
Event A4: Neighbor Cell Better Than Threshold
Condition: Mn > Threshold_A4 (Neighbor cell becomes better than absolute threshold)
-110 dBm
-100 dBm
-95 dBm
-90 dBm
-85 dBm
0s
2s
4s
6s
8s
10s
12s
14s
Time (seconds)
Signal Strength (RSRP)
Threshold_A4 = -90 dBm
-92 dBm
-94 dBm
-95 dBm
-100 dBm
-91.5 dBm
-88 dBm
-103 dBm
-97 dBm
Mn > Threshold_A4
TTT: 1.5s
Event A4 Triggered
Serving Cell
RSRP: -94 dBm
(Acceptable quality)
Neighbor Cell 1
RSRP: -88 dBm
(Above threshold)
Neighbor Cell 2
RSRP: -97 dBm
(Below threshold)
UE
Meets Threshold_A4 = -90 dBm
Configure Event A4
Threshold_A4: -90 dBm
UE Measures Neighbors
Multiple neighbor cells
Neighbor 1 > Threshold
-88 dBm > -90 dBm
Event A4 Triggered
After Time-to-Trigger
UE Reports to gNB
Measurement Report (A4)
Event A4 Use Cases:
• Proactive handover before
serving cell degradation
• Load balancing to good
quality neighbor cells
• Anticipating serving cell
failure or maintenance
A4 Parameters:
• Threshold_A4: -90 dBm
• Time-to-Trigger: 1.5s
Key Distinction:
• Absolute neighbor threshold
• Independent of serving cell

## Slide 97
Event A5: Dual Threshold Handover Trigger
Condition: Ms < Threshold_A5_1 AND Mn > Threshold_A5_2
-110 dBm
-100 dBm
-95 dBm
-90 dBm
-85 dBm
0s
2s
4s
6s
8s
10s
12s
14s
Time (seconds)
Signal Strength (RSRP)
Threshold_A5_1 = -92 dBm
Threshold_A5_2 = -88 dBm
-88 dBm
-91 dBm
-92 dBm
-96 dBm
-95 dBm
-91.5 dBm
-90 dBm
-88.5 dBm
-85 dBm
Ms < Threshold_A5_1
Mn > Threshold_A5_2
Event A5
Dual Condition Met
TTT: 1s
Event A5 Triggered
AND
Serving Cell
RSRP: -96 dBm
< Threshold_A5_1
Neighbor Cell
RSRP: -85 dBm
> Threshold_A5_2
UE
Event A5 Condition:
(-96 dBm < -92 dBm) AND (-85 dBm > -88 dBm)
Configure Event A5
Threshold_A5_1: -92 dBm
Threshold_A5_2: -88 dBm
UE Monitors Cells
Serving: -92 dBm → -96 dBm
Neighbor: -95 dBm → -85 dBm
Condition 1 Met
Ms < Threshold_A5_1
-96 dBm < -92 dBm
Condition 2 Met
Mn > Threshold_A5_2
-85 dBm > -88 dBm
Event A5 Triggered
Both conditions met
UE sends Measurement Report
A5 Use Cases:
• Reliable handover triggering
• Preventing unnecessary
handovers
• Ensuring suitable target
cell is available
Key Feature:
• Combined condition approach
• "Serving cell bad AND
neighbor cell good"
Compared to:
• A2: Only checks serving cell
• A3: Relative comparison
• A4: Only checks neighbor cell

## Slide 98
Event A6: Neighbor Cell Better Than Secondary Cell
Carrier Aggregation Scenario in 5G NR
Time (ms)
0
200
400
600
800
RSRP (dBm)
-90
-100
-110
-120
-130
-140
PCell (Primary)
SCell (Secondary)
Neighbor Cell
Offset_A6 = 3dB
Mn + Offset_A6
Event A6 Trigger Point
TTT = 160ms
-110 dBm
-113 dBm
Event A6 Parameters:
• Measurement: RSRP
• Offset_A6 = 3 dB
• Time-to-Trigger (TTT) = 160 ms
• Frequencies: PCell 2.5 GHz, SCell 3.7 GHz
Event A6 Condition:
Mn + Offset_A6 > Ms2 (Neighbor better than SCell by offset)
P
S
N
CA Active
UE
Action After Event A6:
SCell change from current SCell to better Neighbor Cell

## Slide 99
Event B1: Inter-RAT Neighbor Better Than Threshold
Condition: Mn_RAT > Threshold_B1 (Inter-RAT neighbor cell becomes better than threshold)
-110 dBm
-100 dBm
-95 dBm
-90 dBm
-85 dBm
0s
2s
4s
6s
8s
10s
12s
14s
Time (seconds)
Signal Strength (RSRP)
Threshold_B1 = -90 dBm
5G NR Serving Cell
LTE (Inter-RAT) Neighbor Cell
-85 dBm
-93 dBm
-102 dBm
-98 dBm
-93 dBm
-87 dBm
Mn_RAT > Threshold_B1
TTT: 1s
Event B1 Triggered
Inter-RAT Handover
5G NR Cell
RSRP: -102 dBm
(Degrading coverage)
LTE Cell
RSRP: -87 dBm
> Threshold_B1 (-90 dBm)
UE
Inter-RAT Handover
Configure Event B1
Threshold_B1: -90 dBm
Inter-RAT Measurement
UE measures LTE cells
LTE > Threshold
-87 dBm > -90 dBm
Event B1 Triggered
UE sends Measurement Report
Inter-RAT Handover
5G NR → LTE
Event B1 Use Cases:
• Coverage extension via LTE
• Fallback when exiting 5G
• Inter-RAT load balancing
• Energy efficiency (switching
to LTE to save battery)
B1 Parameters:
• Threshold_B1: -90 dBm
• Time-to-Trigger: 1s
• measurementType: RSRP
5G NR vs. LTE:
• 5G NR: Higher capacity, speed
• LTE: Wider coverage, lower freq.
• Different frequency bands
• Different cell IDs and PCIs
Inter-RAT Handover Components:
• S1/X2 or N2/Xn interfaces
• RAT-specific measurement objects

## Slide 100
Event B2: Serving Cell Becomes Worse Than Threshold 1 AND
Inter-RAT Neighbor Becomes Better Than Threshold 2
-110 dBm
-100 dBm
-90 dBm
-80 dBm
Time
RSRP
Threshold_B2_1 = -90 dBm
Threshold_B2_2 = -85 dBm
5G NR Serving Cell
LTE Cell
5G Below Threshold
LTE Above Threshold
Event B2 Triggered
AND
5G NR Cell
-100 dBm
LTE Cell
-80 dBm
UE
Inter-RAT Handover
Configure B2
5G Below Threshold
LTE Above Threshold
B2 Triggered
Handover to LTE

## Slide 101
Traffic Profile Collection Framework
Weekly Traffic Profile Collection
Monday
Tuesday
Wednesday
Thursday
Friday
Saturday
Sunday
Business Hours
Peak: 9-11 AM
Peak: 2-5 PM
24h Collection
Business Hours
Peak: 9-11 AM
Peak: 2-5 PM
24h Collection
Business Hours
Peak: 9-11 AM
Peak: 2-5 PM
24h Collection
Business Hours
Peak: 9-11 AM
Peak: 2-5 PM
24h Collection
Business Hours
Peak: 9-11 AM
Evening Peak
24h Collection
Shopping Hours
Peak: 11-4 PM
Evening: 6-9 PM
24h Collection
Leisure Hours
Peak: 10-6 PM
Evening: 7-10 PM
24h Collection
Hourly Collection Parameters
Collection Interval:
Hourly (00:00-23:00, 24 datapoints/day)
Aggregation:
15-minute samples averaged per hour
Duration:
Minimum 1 full week for baseline
Critical Hours:
Busy Hour per cell identified separately
Per-Cell Traffic Collection
Coverage Type:
Urban, Suburban, Rural (separate baselines)
Cell Types:
Macro, Micro, Small Cell, Indoor
Sectors:
All sectors in each site collected separately
Focus Areas:
Cells with high handover rates prioritized
Traffic Metrics Collected
• RRC Connected Users (average, peak)
• Throughput (DL/UL in Mbps)
• PRB Utilization (%, DL/UL)
• SINR Distribution (% of samples in each range)
Traffic Profile Analysis
• Hour-by-hour traffic variation pattern
• Day-of-week variation pattern
• Busy Hour determination per cell/area
• Correlation with mobility events (handovers)

## Slide 102
5G Handover Failure Analysis & Optimization
Handover Failures
Too Many Attempts
Preparation Failures
Execution Failures
CAUSES:
• Aggressive handover triggering
• Small cell sizes, high user density
• Fast-moving users
OPTIMIZATION:
• Increase a3-offset
• Increase a3-hysteresis
• Increase a3-time-to-trigger
• Consider cell size and overlap
*_PrepFail_TimeOut
*_PrepFail_Fail
*_PrepFail_CpFail
CAUSES:
• Network congestion
• Interface issues
• Slow gNB response
OPTIMIZATION:
• Increase TimeOut
• Optimize interface
• Load balancing
• Address root cause
CAUSES:
• Target gNB
rejecting requests
• Config mismatch
OPTIMIZATION:
• Check target gNB
logs for reasons
• Correct configs
• Adjust admission
CAUSES:
• Source gNB
internal issues
• Resource exhaustion
OPTIMIZATION:
• Check source gNB
resource usage
• Adjust call
admission control
Execution Failure Types
*_Fail_
RrcTimeOut
*_Fail_
TimeOut
*_Fail_
CpFail
*_Handover
Cancel
*_RRE
RrcTimeOut
Cause: UE loses
connection before
receiving message
Optimization:
• Trigger HO earlier
• Increase t304 timer
• Improve coverage
• Reduce interference
TimeOut
Cause: Network
congestion, slow
interface response
Optimization:
• Increase TimeOut
parameters
• Investigate
root cause
HandoverCancel/RRE
Cause: Source
cell cancels HO or
severe radio link
problems
Optimization:
• Adjust A3/A5 events
• Check coverage
• Investigate interf.
Key Configuration Parameters
A3 Event Parameters
Timers
Interface Parameters
Other
a3-offset: 2-4 dB
a3-hysteresis: 1-2 dB
a3-time-to-trigger: 320-640 ms
a3-MaxReportCells: 4-8
reportInterval: 240-480 ms
t304: 500-2000 ms
InterXnOut_PrepFail_XnTimeOut:
5000-10000 ms
PreparationTimer: 10000 ms
t311: 10000-30000 ms
Xn_AdmissionControl_MaxCalls
Xn_Interface_BufferSize
E1_MaxLoadPercentage
NG_InterfaceTimeout
F1_MaxConnections
max-call-count
max-drb-count
loadBalancing
interference
rsrpThreshold
Always test parameters in controlled environment first!

## Slide 103
5G NR Intra-Handover Optimization Framework
Key Performance Indicators (KPIs)
HOSR
Handover Success Rate
Target: >99.5%
HIT
Handover Interruption Time
Target: <20ms
Ping-Pong Rate
Back-and-forth HOs
Minimize
Too Late HO Rate
RLF due to late HO
Minimize
Too Early HO Rate
Unnecessary HOs
Minimize
Group 1: Measurement Configuration
L3 Filter Coefficient
fc2-fc3
High Speed
UEs
fc4
Default
fc6-fc8
Low Speed
UEs
F_new = (1-α) × F_old + α × M_new
More smoothing → More stable, Less responsive
Less smoothing → More responsive, Less stable
Group 2: Handover Triggering (Event A3)
A3 Event: M_n + O_cn - Hys > M_s + O_cs + A3_Offset
A3 Offset
Default: 3dB
↓ Reduces Too Late
Hysteresis
Default: 1-2dB
↑ Reduces Ping-Pong
Time to Trigger
Default: 320ms
↓ Fast UEs
↑ Ping-Pong
Ping-Pong ← → Too Late HO
Optimization Balance
Group 3: Mobility Robustness
t310 Timer
Default: 1000ms
↑ for urban
n310 Counter
Default: n1
↑ for glitches
n311 Counter
Default: n1
Keep low
RLF Detection Process
Out-of-Sync
n310 × ?
t310 Start
n311 consecutive In-Sync → Stop t310
t310 expires → RLF Declaration
Optimization Strategies by UE Mobility
High-Speed UEs (Vehicles)
• Filter Coefficient: fc2-fc3
• Time to Trigger: 80-160ms
• A3 Offset: 2-2.5dB
• Hysteresis: 1-2dB
• Priority: Reduce Too Late HO
Medium-Speed UEs
• Filter Coefficient: fc4
• Time to Trigger: 320ms
• A3 Offset: 3dB
• Hysteresis: 2dB
• Priority: Balanced approach
Low-Speed UEs (Pedestrians)
• Filter Coefficient: fc6-fc8
• Time to Trigger: 480-640ms
• A3 Offset: 4-5dB
• Hysteresis: 3dB
• Priority: Reduce Ping-Pong
Advanced: MSE-Based
• Mobility State Estimation
• Dynamic parameter adaptation
• Speed-based profile switching
• ML-assisted optimization
• Real-time KPI monitoring
Key Optimization Principles
Trade-off Management
Balance Ping-Pong vs Too Late HO
Holistic parameter tuning approach
UE Mobility Segmentation
Speed-based parameter sets
Adaptive optimization strategies
Continuous Monitoring
Real-time KPI tracking
Data-driven adjustments
Network-Specific Tuning
Environment-aware settings
Vendor-specific optimizations
Quick Reference: Parameter Impact Summary
Reduce Ping-pong
↑ Hysteresis
↑ Time To Trigger
↑ A3 Offset
↑ Filter Coefficient
Reduce Too Late HO
↓ Time To Trigger
↓ A3 Offset
↓ Filter Coefficient
↑ T310 Timer
Improve HOSR
Optimize A3 Params
↑ T310 Timer
Tune N310/N311
Prevent RLF
Reduce HIT
Prevent RLF
Fast HO Execution
Network Optimization
Vendor-specific
Environment-based
Urban: ↑ T310, ↑ N310
Highway: ↓ TTT, ↓ FC
Indoor: ↑ Hysteresis
Dense: ↑ A3 Offset
Monitoring Kpis
Hosr > 99.5%
HIT < 20ms
Ping-pong < 2%
RLF Rate < 0.5%

## Slide 104
Handover Scenario A: n78 (3500 MHz) → n2600 (n7) Coverage-Triggered
n78 Cell
3500 MHz
Source
Signal Weakening
n2600 Cell
n7 Band
Target
Strong Signal
📱
UE
HANDOVER
Event A5 Triggered
MeasConfig Parameters Design (n78 → n2600)
3GPP Parameter
Value/Description
Purpose
MeasObjectNR
arfcn-ValueNR: 531000
ssb-SubcarrierSpacing: kHz30
Defines n2600 layer
measurement target
ReportConfigNR
reportType: eventTriggered, eventId: eventA5
Event A5 trigger definition
eventA5.a5-Threshold1
rsrp: 30 (Actual: -140 + 30 = -110 dBm)
Serving n78 RSRP threshold
eventA5.a5-Threshold2
rsrp: 35 (Actual: -140 + 35 = -105 dBm)
Neighbor n2600 RSRP threshold
reportConfigNR.hysteresis
dB3 (3 dB)
Prevents ping-pong
reportConfigNR.timeToTrigger
ms320 (320 milliseconds)
Stability duration
reportConfigNR.reportQuantityCell
rsrp
Report RSRP values
reportConfigNR.maxReportCells
3
Best 3 n2600 cells
MeasGapConfig
gapPattern: gp0 (MGRP 40ms, MGL 6ms)
TDD UE measurement gaps
MeasIdToAddMod
measId: 1, measObjectId: (n2600 object)
reportConfigId: (Event A5 config)
Links measurement & reporting
Event A5 Trigger Logic
PRIMARY TRIGGER:
Serving n78 RSRP < -110 dBm (threshold1)
AND
SECONDARY CONDITION:
Neighbor n2600 RSRP > -105 dBm (threshold2)
HYSTERESIS: 3 dB margin prevents ping-pong
TIME TO TRIGGER: Conditions must persist for 320ms
RESULT: Measurement Report Sent
→ Handover Decision Triggered
🚨 CRITICAL DESIGN CONSIDERATIONS
• Creates 6ms gap every 40ms for TDD UE FDD frequency measurement
• Event A5 ensures dual condition: weak serving + strong target
• 320ms stability prevents unnecessary handovers on temporary fading
• 3 dB hysteresis prevents ping-pong between cells
• Reports best 3 n2600 cells for optimal target selection
Legend
n78 (3500 MHz) - Source Cell
n2600 (n7) - Target Cell
User Equipment (UE)
Handover Direction
Objective: Coverage-triggered handover before signal loss

## Slide 105
MeasConfig Parameters Design: n78 (3500 MHz) → n2600 Inter-Frequency Handover
Event A5 Coverage-Triggered Handover with Measurement Gap Configuration
n78 gNB
ARFCN: 647232
3500 MHz
Serving Cell
n2600 gNB
ARFCN: 531000
2655 MHz (n7)
Target Cell
UE
Measuring
HANDOVER EXECUTION
RSRP Measurement
RSRP Measurement
Handover Decision Zone
MeasConfig Parameters Design (n78 → n2600)
3GPP Parameter (within RRC IE)
Example Value / Description
Purpose in this Scenario
MeasObjectNR
arfcn-ValueNR: 531000 (example for n7 @ 2655 MHz)
ssb-SubcarrierSpacing: kHz30
referenceSignalConfig: Defines SSB measurement timing
Tells the UE what to measure:
specific frequency and parameters
of the n2600 layer
ReportConfigNR
reportType: eventTriggered
eventId: eventA5
Defines the trigger for sending a
MeasurementReport
eventA5.a5-Threshold1
rsrp: 30 (Actual value: -140 + 30 =
-110 dBm
)
Primary Trigger:
If the serving n78 cell's RSRP drops
below this critical threshold...
eventA5.a5-Threshold2
rsrp: 35 (Actual value: -140 + 35 =
-105 dBm
)
...AND
the neighbor n2600 cell's RSRP is above
this minimum acceptable threshold, the
event is triggered. Ensures we don't jump
to another bad cell.
reportConfigNR.hysteresis
dB3 (3 dB)
Prevents ping-pong.
The trigger condition must be met by this margin.
reportConfigNR.timeToTrigger
ms320 (320 milliseconds)
The trigger condition must be
continuously met for this duration before
a report is sent. Prevents reporting on
transient signal fluctuations.
reportConfigNR.reportQuantityCell
rsrp
The UE should report RSRP values.
reportConfigNR.maxReportCells
3
Report the best 3 cells found on the n2600 frequency.
MeasGapConfig
gapPattern: gp0 (MGRP 40ms, MGL 6ms)
Measurement Gap Repetition Period: 40ms
Measurement Gap Length: 6ms
CRITICAL.
Creates a 6ms gap every 40ms for
the TDD UE to measure the FDD
frequency, preventing call drops.
MeasIdToAddMod
measId: 1
measObjectId: (points to n2600 object)
reportConfigId: (points to Event A5 config)
Links the n2600 measurement object
with the Event A5 reporting configuration.
Event A5 Trigger Logic Flow
CONDITION 1: Serving Cell Check
n78 RSRP < -110 dBm (Threshold1)
⬇ AND ⬇
CONDITION 2: Target Cell Check
n2600 RSRP > -105 dBm (Threshold2)
HYSTERESIS: ±3 dB margin applied
TIME TO TRIGGER: 320ms stability check
MEASUREMENT GAP: 6ms every 40ms
RESULT: MeasurementReport Sent
→ Handover Command Initiated
⚡ ENGINEERING CONSIDERATIONS
🔸 ARFCN 531000 corresponds to n7 band center frequency calculation
🔸 TDD-FDD measurement requires dedicated gaps to avoid interference
🔸 320ms TTT balances mobility robustness vs. handover delay
🔸 Dual threshold (A5) prevents handover to weak cells
🔸 3 dB hysteresis compensates for measurement uncertainty
🔸 Max 3 cells reported for optimal target selection algorithm
Frequency Allocation & Measurement Timing
n78: 3500 MHz
ARFCN: 647232
Serving (TDD)
GAP
6ms/40ms
Pattern gp0
n2600 (n7): 2655 MHz
ARFCN: 531000
Target (FDD)
t = 0ms: Start measurement
t = 320ms: TTT expires
t = 325ms: Report sent
t = 350ms: HO command

## Slide 106
Throughput Optimization

## Slide 107
5G NR Signal Quality Parameters and Throughput Impact
gNB
5G Base Station
UE Device
RSRP
Reference Signal Received Power
-120 dBm
-100 dBm
-80 dBm
Weak Signal
Strong Signal
!
RSRQ
Reference Signal Received Quality
-20 dB
-15 dB
-10 dB
High Interference
Low Interference
!
SINR (CRITICAL)
Signal-to-Interference-plus-Noise Ratio
0 dB
15 dB
30 dB
Poor Quality
Excellent Quality
!
Low SINR forces Lower MCS which Reduces Throughput
MCS vs Throughput Impact
High
Medium
Low
Throughput
Poor SINR
Good SINR
Excellent SINR
Signal Quality
MCS 0-9
MCS 10-16
MCS 17-28
How to Monitor and Check
Drive Test Tools
• TEMS Investigation
• Nemo Handy/Outdoor
• Real-time RF measurements
UE Traces and Logs
• Device engineering mode
• Network signaling traces
• Layer 1/2/3 measurements
gNB Performance Counters
• Average cell RSRP/SINR
• SINR distribution stats
• MCS usage statistics
KEY INSIGHT: SINR is the most critical parameter for 5G throughput!

## Slide 108
5G NR: MCS and CQI Impact on Throughput Performance
Channel Quality
Signal Strength (RSRP)
Signal Quality (SINR)
Interference Level
Fading Conditions
Reports
CQI Reporting
UE to gNB
CQI Index: 0-15
Periodic/Aperiodic
Wideband/Subband
Selects
MCS Selection
gNB Decision
MCS Index: 0-28
DL and UL
Adaptive
Determines
Throughput Impact
Bits per Symbol
Spectral Efficiency
Data Rate
User Experience
MCS Index vs Modulation Scheme vs Throughput Impact
MCS Index
Modulation
Bits/Symbol
Code Rate
Channel Condition
Relative Throughput
Performance
0-9
QPSK
2
Low (0.15-0.6)
Poor SINR
25-50%
Low Throughput
10-16
16QAM
4
Medium (0.4-0.7)
Moderate SINR
60-80%
Medium Throughput
17-22
64QAM
6
High (0.6-0.8)
Good SINR
85-95%
High Throughput
23-28
256QAM
8
Very High (0.8-0.95)
Excellent SINR
95-100%
Peak Throughput
Key Performance Monitoring Parameters
gNB Counters to Monitor
DL/UL MCS Index Distribution
Average CQI per Cell/UE
UE Traces to Check
CQI Reporting Frequency
SINR/RSRP Measurements
Optimization Actions
Antenna Tilt Adjustment
Power Control Optimization
Expected Outcomes
Higher MCS Usage
Improved User Throughput
Poor
Excellent
Channel Quality Impact on Performance

## Slide 109
5G NR Block Error Rate (BLER) Impact on Throughput
gNB
(Base Station)
UE
(User Equipment)
Air Interface
Interference and Noise
Low BLER (1-5%)
Most blocks decoded successfully
Minimal retransmissions
High Effective Throughput
High BLER (>10%)
Many blocks with errors
Frequent retransmissions
Low Effective Throughput
HARQ Retransmission Process
Initial TX
NACK
ReTX
ACK
Resources consumed for retransmission
instead of new data transmission
BLER Impact Analysis
Effective Throughput
95% (Low BLER)
Peak: 1 Gbps → Effective: 950 Mbps
60% (High BLER)
Peak: 1 Gbps → Effective: 600 Mbps
Resource Utilization
Low BLER
90% New Data
10% Retrans
High BLER
60% New Data
40% Retrans
Key Factors Affecting BLER in 5G NR
Signal Quality (SINR/SNR)
Poor RF conditions increase BLER
Interference
Co-channel, adjacent channel interference
MCS Selection
Higher MCS = Higher BLER risk
Mobility/Doppler
Fast movement affects channel estimation
Network Load
High load increases interference
Channel Estimation
Inaccurate estimation increases errors
BLER Targets:
PDSCH: 1-10% (first transmission)
PUSCH: 1-10% (first transmission)
PUCCH: 1-5%
After HARQ: <1%
Legend
Successfully decoded block
Block with error (NACK)
Retransmission

## Slide 110
5G MIMO Rank and Spatial Multiplexing
5G gNB
Base Station
Multiple Antennas
UE
Device
Stream 1
Stream 2
Stream 3
Stream 4
Spatial Multiplexing
Multiple data streams on same time-frequency resources
MIMO Rank Indicator RI
Rank 1
Single Layer
Rank 2
2 Spatial Layers
Rank 4
4 Spatial Layers
What to Monitor
1
gNB Counters:
Average DL MIMO Rank
Rank Distribution Percentages
Spatial Multiplexing Efficiency
2
UE Traces:
RI Reports from UE
Channel Quality Indicators
PMI Precoding Matrix Index
3
Performance Impact:
Throughput per spatial layer
Spectral efficiency gains
4
Channel Conditions:
SINR per antenna port
Correlation between antennas
Throughput Impact Analysis
Good Channel Conditions
High MIMO Rank 4-8
Multiple spatial streams
Throughput multiplied by rank
Poor Channel Conditions
Low MIMO Rank 1-2
Limited spatial multiplexing
Reduced throughput gain
Optimization Strategies:
1. Antenna Diversity: Use spatially separated antennas
2. Beamforming: Optimize precoding matrices
3. Adaptive Rank: Adjust based on conditions
4. Interference Management: Coordinate cells
5. UE Positioning: Consider mobility patterns
Key Formula:
Throughput = Base Rate × MIMO Rank × Coding Rate × Modulation Efficiency
Key Performance Indicators KPIs
Average MIMO Rank
Target: Greater than 2.5
Good: Greater than 3.0
Rank 4+ Usage
Target: Greater than 30%
Excellent: Greater than 50%
Rank 1 Usage
Target: Less than 20%
Alert: Greater than 40%
Spectral Efficiency
Target: Greater than 4 bps/Hz
Excellent: Greater than 6 bps/Hz

## Slide 111
Throughput Check and Diagnosis (What to Check)
Parameter Name | Layer | Primary KPI Impact | 3GPP Reference (IE Path in SIB/RRC) | Default/Typical Setting | Recommended Setting
I. Modulation & Coding Scheme (MCS) / Signal Quality |  |  |  |  | 
mcs-Table (for PDSCH) | L1/L3 | DL Throughput | pdsch-ConfigCommon -> mcs-Table | qam64 | qam256 (if channel quality and UE support allow)
ssb-transmittedPower (dBm) | L1 | DL Throughput, Coverage | servingCellConfigCommon -> ssb-transmittedPower | Varies (e.g., 20-24 dBm) | Adjust to optimize SINR, balancing coverage and inter-cell interference.
reportQuantity (for CSI-RS measurements) | L3 | DL Throughput | MeasObjectNR -> reportConfigNR -> reportConfigType -> csi-RS-RLM -> reportQuantity (e.g., ssb-rsrp, ssb-rsrq, csi-rs-rsrp) | ssb-rsrp or csi-rs-rsrp | Ensure UE reports accurate CSI-RS based RSRP/RSRQ/SINR for optimal scheduling.
periodicityAndOffset (for CSI-RS reporting) | L3 | DL Throughput | MeasObjectNR -> reportConfigNR -> reportConfigType -> csi-RS-RLM -> periodicityAndOffset | Varies (e.g., sl160) | Shorter periodicities (e.g., sl20, sl40) for faster channel adaptation in high-mobility/dynamic channels.
II. Bandwidth & Resource Allocation |  |  |  |  | 
scellConfig (for Carrier Aggregation) | L3 | DL Throughput | RRCReconfiguration -> scellConfig (configured per SCell) | N/A (requires explicit configuration) | Configure max supported component carriers (CCs) and frequency bands based on spectrum availability and UE capabilities.

## Slide 112
Throughput Check and Diagnosis (What to Check)
Parameter Name | Layer | Primary KPI Impact | 3GPP Reference (IE Path in SIB/RRC) | Default/Typical Setting | Recommended Setting
scellConfig (for Carrier Aggregation) | L3 | DL Throughput | RRCReconfiguration -> scellConfig (configured per SCell) | N/A (requires explicit configuration) | Configure max supported component carriers (CCs) and frequency bands based on spectrum availability and UE capabilities.
initialDownlinkBWP (and subsequent BWP-Downlink) | L1/L3 | DL Throughput | sib1 -> initialDownlinkBWP (and RRCReconfiguration for BWP-Downlink) | Varies (e.g., initial BWP matching full carrier BW, SCS 30kHz) | Configure wider BWPs with higher SCS (e.g., 60kHz, 120kHz for FR2) and enable BWP switching for data-hungry users.
subcarrierSpacing (within BWP configuration) | L1 | DL Throughput | BWP-Downlink -> subcarrierSpacing | Varies (e.g., 30kHz for FR1, 120kHz for FR2) | Use higher SCS for wider bandwidths to achieve higher peak throughput (e.g., 60kHz in FR1, 120kHz in FR2).
controlResourceSetZero (PDCCH configuration) | L1/L3 | DL Throughput | sib1 -> controlResourceSetZero | Varies by vendor/PCI | Ensure sufficient CCE capacity and robust PDCCH transmission power for efficient scheduling.
searchSpaceZero (PDCCH configuration) | L1/L3 | DL Throughput | sib1 -> searchSpaceZero | Varies by vendor/PCI | Ensure sufficient candidates and monitoring occasions for timely DL grants.
III. MIMO & Beamforming |  |  |  |  | 
dmrs-TypeA-Position (PDSCH) | L1 | DL Throughput | pdsch-ConfigCommon -> dmrs-TypeA-Position | pos2 (Symbol 2) | Depends on channel characteristics; pos2 generally efficient. Ensure consistency.

## Slide 113
Throughput Check and Diagnosis (What to Check)
Parameter Name | Layer | Primary KPI Impact | 3GPP Reference (IE Path in SIB/RRC) | Default/Typical Setting | Recommended Setting
tci-State (TCI-State IE) | L1/L3 | DL Throughput | PDSCH-Config -> tci-StatePDCCH-r16 (and other TCI-related IEs) | Dynamically configured/Vendor-specific | Configure sufficient TCI states and enable efficient beam management (especially for FR2) to maximize spatial multiplexing and beamforming gain.
csi-RS-Resource (CSI-RS configuration) | L1/L3 | DL Throughput | CSI-RS-ResourceMapping | Varies by deployment | Optimize CSI-RS density and periodicity to provide accurate channel state information for beamforming and precoding.
reportConfigNR (PMI/RI reporting) | L3 | DL Throughput | MeasObjectNR -> reportConfigNR -> reportConfigType -> semiPersistentOnPUSCH or periodic CSI-RS reporting | Varies (e.g., periodic CSI-RS with moderate periodicity) | Ensure UEs provide necessary PMI (Precoding Matrix Indicator) and RI (Rank Indicator) feedback for optimal MIMO layer selection and precoding.
IV. Efficiency & Reliability (DL) |  |  |  |  | 
maxRetxThreshold (for DL RLC) | L2 (RLC) | DL Throughput, Call Drop | RLC-Config -> am-Config | t16 (16 retransmissions) | t16 or t32 (Higher for more robustness, lower for faster error reporting)
t-PollRetransmit (for DL RLC) | L2 (RLC) | DL Throughput, Call Drop | RLC-Config -> am-Config | ms100 to ms200 | ms80 to ms150 (Faster re-polling for quick error recovery)
pollPDU / pollByte (for DL RLC) | L2 (RLC) | DL Throughput, Call Drop | RLC-Config -> am-Config | p8/kB4 | p4/kB2 (More frequent polling for faster error detection)
headerCompression (for DRBs) | L2 (PDCP) | DL Throughput (Effective) | pdcp-Config for Data Radio Bearers (DRBs) | Enabled/Disabled by default | Enabled (e.g., ROHC - Robust Header Compression)

## Slide 114
PDCCH Parameters for Downlink Throughput Optimization
Parameter Name | Layer | Primary KPI Impact | 3GPP Reference (IE Path in SIB/RRC) | Default/Typical Setting | Recommended Setting | How it Helps Improve Downlink Throughput
I. CORESET Configuration (Capacity & Diversity) |  |  |  |  |  | 
frequencyDomainResources (bitmask) | L1/L3 | DL Throughput, PDCCH Capacity | controlResourceSetZero (in SIB1) / ControlResourceSet (in PDCCH-Config) | Varies (e.g., typically a high % of BW for CORESET0) | Increase the number of Resource Blocks (RBs) allocated for CORESETs (especially for CORESETs used for dedicated scheduling). | Direct. More RBs in a CORESET directly translate to more available CCEs, thus increasing the PDCCH capacity. Higher capacity means more DL/UL scheduling grants can be sent simultaneously, enabling higher throughput for more UEs.
duration (OFDM symbols) | L1/L3 | DL Throughput, PDCCH Capacity | controlResourceSetZero (in SIB1) / ControlResourceSet (in PDCCH-Config) | 1 or 2 symbols | 2 or 3 symbols | Direct. Longer CORESET duration (more OFDM symbols) also increases PDCCH capacity (more CCEs available per slot). This allows for scheduling of more users or larger grants, boosting throughput. (Trade-off: consumes more data symbols).
cce-REG-MappingType | L1/L3 | DL Throughput, PDCCH Reliability | controlResourceSetZero (in SIB1) / ControlResourceSet (in PDCCH-Config) | interleaved | interleaved (for diversity), non-interleaved (for beamforming) | Indirect. interleaved provides frequency diversity, improving PDCCH reliability in channels with frequency-selective fading. non-interleaved is better for dedicated beamforming, allowing targeted PDCCH for higher SINR. Choose based on scenario.
precoderGranularity | L1/L3 | DL Throughput, PDCCH Reliability | ControlResourceSet (in PDCCH-Config) | sameAsREG-bundle | sameAsREG-bundle (default); allContiguousRBs (for wider beams/less precise precoding) | Indirect. Impacts how precisely beamforming can be applied to PDCCH. Optimal setting ensures PDCCH is reliably received by the UE's specific beam, increasing its decodability and speeding up scheduling.

## Slide 115
Parameter Name | Layer | Primary KPI Impact | 3GPP Reference (IE Path in SIB/RRC) | Default/Typical Setting | Recommended Setting | How it Helps Improve Downlink Throughput
II. Search Space Configuration (Timeliness & Reliability) |  |  |  |  |  | 
monitoringSlotPeriodicityAndOffset | L1/L3 | DL Throughput, Scheduling Latency | searchSpaceZero (in SIB1) / SearchSpace (in PDCCH-Config) | Varies (e.g., n1, n2 - every 1st or 2nd slot) | n1 or n2 (more frequent monitoring) | Direct. Defines how often the UE monitors for PDCCH. More frequent monitoring (n1) means the gNB can send scheduling grants more quickly, reducing latency and allowing for faster data transfer, thus boosting throughput.
monitoringSymbolsWithinSlot | L1/L3 | DL Throughput, Scheduling Latency | searchSpaceZero (in SIB1) / SearchSpace (in PDCCH-Config) | Varies (e.g., s0Ands1 - symbols 0 and 1) | Ensure symbols align with CORESET duration (e.g., s0Ands1Ands2Ands3 if CORESET duration is 4 symbols). | Direct. Defines which OFDM symbols within a slot the UE monitors. More monitoring symbols (aligned with CORESET duration) provide more opportunities for PDCCH detection, especially in dynamic channels.
aggregationLevel (AL) & numCandidates | L1/L3 | DL Throughput, PDCCH Capacity/Reliability | searchSpaceZero (in SIB1) / SearchSpace (in PDCCH-Config) | ALs: al4, al8, al16 for common SS; ALs: al1, al2, al4, al8, al16 for dedicated SS. numCandidates typically 1, 2, 4. | Balance. For common search spaces (SIB1), use higher ALs (e.g., al8, al16) for robustness in wider coverage. For dedicated search spaces, allow lower ALs (e.g., al1, al2) for UEs in good conditions to save CCEs, and higher ALs for UEs at cell edge. | 
dci-Formats (e.g., dci-0-1, dci-1-1) | L1/L3 | DL Throughput (Efficiency) | searchSpaceZero (in SIB1) / SearchSpace (in PDCCH-Config) | dci-0-1, dci-1-1 are common. | Ensure the scheduler primarily uses efficient DCI formats (e.g., dci-1-1 for DL, dci-0-1 for UL) that are optimized for common traffic patterns to minimize overhead. | 
PDCCH Parameters for Downlink Throughput Optimization

## Slide 116
5G NR Carrier Aggregation (CA) Throughput Optimization Parameters
Parameter Name | 3GPP Reference | Default/Typical Value | Recommended Setting for CA Throughput | Optimization Tips
1. UE Capabilities (Implicit) | TS 38.306, 38.331 | Varies per UE model | Maximize (Utilize highest supported capabilities) | - maxNumberServingCells: Configure as many SCells as the UE supports.<br>- supportedBandCombination: Prioritize UEs supporting wider and higher-order band combinations (e.g., 2FR1+FR2, 3+CA).<br>- maxNumberMIMO-Layers: Utilize the maximum supported MIMO layers per CC.
2. SCell Activation Timer (sCellActivationTimer) | TS 38.331 (RRC), 38.321 (MAC) | Typically 200-500 ms | Shorter (e.g., 50-200 ms) | - Faster SCell activation reduces latency when new data arrives, quickly bringing additional capacity online.<br>- Too short can lead to frequent, unnecessary activations and increased control overhead/power consumption. Balance with sCellDeactivationTimer.
3. SCell Deactivation Timer (sCellDeactivationTimer) | TS 38.331 (RRC), 38.321 (MAC) | Typically 1000-5000 ms | Longer (e.g., 3000-5000 ms) | - Keeps SCells active for longer periods, reducing the need for re-activation for bursty traffic, thus lowering latency and signaling overhead for subsequent data.<br>- Too long can lead to wasted power consumption at the UE if SCells remain active without data.
4. Bandwidth Part (BWP) Configuration | TS 38.331 (RRC) | Active BWP covers full CC bandwidth | Ensure Active BWP utilizes the full configured bandwidth of the Component Carrier. | - For throughput, the active BWP should encompass the widest possible contiguous frequency range within the CC.<br>- BWP switching introduces latency; minimize unnecessary switches by keeping a wide BWP active during high-throughput sessions.
5. MCS Table Selection (mcs-Table) | TS 38.214 (PDSCH) | qam64 (default in many cases) | qam256 for good channel conditions, qam64 for moderate, qam16 for poor. | - Higher order modulation (e.g., 256QAM) allows more bits per symbol, directly increasing spectral efficiency and throughput.<br>- Requires good SINR. Monitor BLER; if high, revert to a lower modulation order.<br>- Dynamic MCS adaptation is key.
6. HARQ Processes (harq-NumProcess) | TS 38.321 (MAC) | 16 (DL), 16 (UL) | Maximize (16 for NR) | - More HARQ processes allow for more parallel transmissions and retransmissions, improving the effective data rate by reducing the impact of errors.<br>- NR supports up to 16 processes, which is generally used.
7. DMRS Configuration (dmrs-Type, dmrs-AdditionalPos, nrofDMRS-Symbol) | TS 38.211, 38.214 (PDSCH/PUSCH) | Type1 (2 ports) | Type2 if supporting 8+ layers MIMO, Type1 otherwise. Use more DMRS symbols for challenging channels. | - dmrs-Type2 offers more DMRS ports (up to 12), enabling higher rank MIMO (more spatial layers), which directly increases throughput.<br>- dmrs-AdditionalPos: Can add more DMRS symbols for improved channel estimation in challenging scenarios, but increases overhead.

## Slide 117
EN_DC 3GPP Parameter Design for Throughput
Parameter Name (3GPP IE) | Belongs To | RRC Message Container | Function / Impact | Default / Typical | Recommended Setting for High Throughput
ul-DataSplitThreshold | DRB-ToAddMod | secondaryCellGroupConfig | CRITICAL: Threshold to start sending data to the SN (gNB). Lower value = more data over NR. | infinity (off) | b0 (0 Bytes). Send all data to NR immediately.
maxNumberMIMO-LayersPDSCH | PDSCH-Config | spCellConfig -> physicalCellGroupConfig | Sets the max number of DL MIMO spatial layers. Directly multiplies throughput. | two | four or eight, matching gNB/UE capability.
mcs-Table | PDSCH-Config | spCellConfig -> physicalCellGroupConfig | Selects the MCS table. qam256 table is essential for high spectral efficiency. | qam64 | qam256. Enable the 256QAM table.
sCellToAddModListNR | NR-Config | secondaryCellGroupConfig | Configures NR Secondary Cells (SCs) for Carrier Aggregation. | Not present | Add all supported NR carriers for the band combination.
channelBandwidth | SCS-SpecificCarrier in FrequencyInfoDL | spCellConfig -> reconfigurationWithSync | Sets the carrier bandwidth. The single biggest factor for throughput. | Vendor specific | Use the maximum supported BW (e.g., fr1 -> mhz100).
BWP-Downlink | ServingCellConfig | spCellConfig -> reconfigurationWithSync | Defines the active DL Bandwidth Part. | Vendor specific | Configure a single, wide BWP covering the entire channel bandwidth.
dmrs-TypeA-Position | PDSCH-Config | spCellConfig -> physicalCellGroupConfig | Position of DMRS symbols. pos2 is standard. | pos2 | pos2.
maxLength | DMRS-DownlinkConfig | PDSCH-Config | DMRS length. len2 adds overhead but improves channel estimation for high mobility. | len1 | len1 for low/medium mobility to reduce overhead.
crossCarrierSchedulingConfig | ServingCellConfig | spCellConfig | Enables scheduling of an SCell from the PSCell's PDCCH. | Disabled | Enable if multiple NR carriers are aggregated.

## Slide 118
EN_DC UL 3GPP Parameter Design for Throughput
Parameter Name (3GPP IE) | Belongs To | RRC Message Container | Function / Impact | Default / Typical | Recommended Setting for High Throughput
maxNumberMIMO-LayersPUSCH | PUSCH-Config | spCellConfig -> physicalCellGroupConfig | Sets max UL MIMO layers. Major UL throughput booster. | Not present (SISO) | two or four if UE/gNB supports UL MIMO.
mcs-Table | PUSCH-Config | spCellConfig -> physicalCellGroupConfig | Selects the UL MCS table. Essential for high UL rates. | qam64 | qam256. Enable UL 256QAM.
transformPrecoder | PUSCH-Config | spCellConfig -> physicalCellGroupConfig | Toggles between CP-OFDM (higher throughput) and DFT-S-OFDM (better for cell edge). | enabled (DFT-S-OFDM) | disabled. Allow gNB to dynamically schedule CP-OFDM for high throughput UEs.
BWP-Uplink | ServingCellConfig | spCellConfig -> reconfigurationWithSync | Defines the active UL Bandwidth Part. | Vendor specific | Configure a single, wide BWP covering the entire UL channel bandwidth.
p0-NominalWithGrant | PUSCH-PowerControl | spCellConfig -> physicalCellGroupConfig | Baseline PUSCH power. Tune to ensure UEs can reach high MCS targets. | Vendor specific | Tune based on RF analysis. Increase slightly if UEs are power-limited for 256QAM.
periodicBSR-Timer | BSR-Config | MAC-CellGroupConfig | How often the UE sends a BSR. A shorter timer means faster response to new UL data. | sf20 (20 slots) | sf5 or sf10. Make it more aggressive.
sr-ProhibitTimer | SchedulingRequestConfig | physicalCellGroupConfig | Prevents UE from sending SRs too frequently. | Vendor specific | Set to a low value (e.g., 1-4ms) to allow rapid requests.

## Slide 119: Baseline Parameter
5G Baseline Parameter Overview
MCG Carrier Management
  NSA DC Vs Anchoring Priority
  SgNB Addition
  Flexible Anchoring
  Anchoring Policy
  NSA MLB
NSA Default QCI Bearer
Throughput
Baseline Parameter Checking
  Anchoring Side
  NR Side

## Slide 120: 5G Baseline Parameter Overview
Tech | Category | MO
LTE Anchor Cell | Anchoring | NRSCGFREQCONFIG
 |  | NSADCMGMTCONFIG
 |  | PCCFREQCFG
 | LTE-NR Relation | NREXTERNALCELL
 |  | NRNFREQ
 |  | NRNRELATIONSHIP
 | NSA QCI Bearer | CellQciPara
 |  | RlcPdcpParaGroup
 | WBB Strategy | Cell
 |  | CellAlgoSwitch
 |  | SPIDCFG
 | X2 | GlobalProcSwitch
NR | LLD | GNBTRACKINGAREA
 |  | NRDUCELL
 |  | NRDUCELLTRP
 | Coverage | NRDUCELLTRPBEAM
 | NSA Bearer | GNBPDCPPARAMGROUP
 |  | GNBRLCPARAMGROUP
 |  | NRDUCELLCSIRS
 |  | NRDUCellQciBearer
 | NSA DC | NRCELLALGOSWITCH
 |  | NRCellNsaDcConfig
 | Throughput | NRDUCELLALGOSWITCH
 |  | NRDUCELLPDCCH
 |  | NRDUCELLPDSCH
 |  | NRDUCELLPUCCH
 |  | NRDUCELLPUSCH
 | NR-NR Relation | NRCELLRELATION
 |  | NREXTERNALNCELL
 | X2 | gNBX2SonConfig

## Slide 121: 5G Baseline Parameter : MCG Carrier Management
To become an Anchor Cell , the LTE cell have to define :
Frequency at PCC Configurations (DLARFCN@PccFreqCfg)
Activate the NSA DC Capability Switch
Activate the NSA PCC Anchoring Switch
Set the NSA Anchoring Priority accordingly
Define LTE to NR Neighbor Relation
Tech | Band | NSA_DC_CAPABILITY_SWITCH |  | NSA_PCC_ANCHORING_SWITCH |  | NsaPccAnchoringPriority | 
 |  | Default Value | G Baseline | Default Value | G Baseline | Default Value | G Baseline
FDD | L1800 F1 | OFF | ON | OFF | ON | 1 | 7
FDD | L2100 F1 | OFF | ON | OFF | ON | 1 | 7
FDD | L700 F1 | OFF | ON | OFF | ON | 1 | 6
TDD | L2600 F1 | OFF | ON | OFF | ON | 1 | 0
TDD | L2600 F2 | OFF | ON | OFF | ON | 1 | 0
TDD | L2600 F4 | OFF | ON | OFF | ON | 1 | 0
TDD | L2600 F5 | OFF | ON | OFF | ON | 1 | 0
TDD | L2300 F1 | OFF | ON | OFF | ON | 1 | 0
TDD | L2300 F2 | OFF | ON | OFF | ON | 1 | 0
**G Project End State Anchoring Strategy is Full Anchoring for FDD and TDD, is just that preferable using FDD as Anchor Cell with set High Priority since the coverage is continuous . For TDD Cell , is set to 0 is just that this cell is unlikely to consider as an Anchoring Target Cell , doesn’t mean this cell is unable to setup NSA Service

## Slide 122: 5G Baseline Parameter : MCG Carrier Management
NE | MML Object | Parameter ID | Default Value | G Baseline | Remarks
LTE | NsaDcMgmtConfig | NSA_BLIND_SCG_ADDITION_ SWITCH@ NsaDcAlgoSwitch | Off | Off | When is OFF , Measurement-based PSCell configuration is performed with Event B1 Measurement
LTE | NrScgFreqConfig | NsaDcB1ThldRsrp | -105 | -120 | Set lower value for faster trigger Event B1 to measure NR Neighbor, more chances to latch on 5G
LTE | NrScgFreqConfig | NrB1TimeToTrigger | 40MS | 40MS | 
NR | NRCellNsaDcConfig | PscellA2RsrpThld | -121 | -125 | Event A2 to release PSCell of the NSA User ; Set 5dBm gap with SgNB Addition to prevent ping pong
UE
eNodeB
gNodeB
MME
RRC CONN REQ
RRC CONN SETUP
RRC CONN SETUP CMP
UL NAS TRANS
INIT UE MESSAGE
INIT UE CONTEXT SETUP REQ
UE CAP ENQUIRE
UE CAP
SEC CMD
SEC CMP
RANDOM ACCESS
RRC RECFG
RRC RECFG CMP
INIT UE CONTEXT SETUP RSP
RRC RECFG(5G Cell Measure by B1 )
RRC RECFG CMP B1 MEAS RPRT
SgNB Addition Rsp
RRC RECFG
（5g Scell Add）
RRC RECFG CMP
SgNB RECFG CMP
ERAB MOD IND
ERAB MOD CNF
EPC
LTE
NR
Option 3x
EPC
LTE
NR
Option 3x
EPC
LTE
NR
Option 3x
EPC
LTE
NR
Option 3x
UE CAP IND
5G neigbour
Measure
5G SCG ADD
Path Update
（Opt 3x）
SgNB Addition Req
UE Initial Access
Data Forwarding
S-GW
Data Forwarding
Bear Modication
X2 SetUp Req
X2 Setup Rsp
The SCG is added blindly and
the B1 is not delivered.
For Blind Pscell Configuration Scenario
:
4G measure 5G neighbor by Event B1
SgNB Addition with Event B1 Measurement based if NR Neighbor is >-120dBm

## Slide 123: 5G Baseline Parameter : SCG Carrier Management
During SgNB Addition or PCC Anchoring Selection would also need to consider traffic volume
As to consider to balance between SCG Addition and UE Power Consume , below is the proposed setting .
MML Object | Parameter ID | Default Value | G Baseline | Remarks
NsaDcMgmtConfig | VOLUME_BASED_PERIODIC_TRIG_SW | On | On | 
NsaDcMgmtConfig | ScgAdditionBufferDelayThld | 5ms | 10ms | NR SCG can be added or PCC anchoring can be triggered for an NSA DC UE only when the data for the UE has been buffered on the eNodeB for a period of time longer than this threshold
NsaDcMgmtConfig | ScgAdditionBufferLenThld | 0 | 50kB | NR SCG can be added or PCC anchoring can be triggered for an NSA DC UE only when the traffic volume buffered on the eNodeB for the UE exceeds this threshold
NsaDcMgmtConfig | ScgAdditionInterval | 60s | 10s | 

## Slide 124: 5G Baseline Parameter : MCG Carrier Management
F1 Non Anchor
F2 NSA Anchor
F1 Non Anchor
2
1
3
MML Object | Parameter ID | Default Value | G Baseline | Remarks
NsaDcMgmtConfig | PERIODIC_PCC_ANCHORING_SW | Off | On | ON=Enable Periodic NSA DC PCC anchoring
NsaDcMgmtConfig | NSA_DC_STATE_PCC_ANCHORING_SW | On | On | ON =NSA DC PCC anchoring can be triggered for UEs in the NSA DC state
NsaDcMgmtConfig | ScgAdditionInterval | 60s | 10s | 10s=Shorten the Interval Time for scenarios : Anchor Cell attempting to add NR SCG Trigger PCC Anchoring for an NSA UE If NR SCG addition failed, eNodeB will retry again after this period **Drawback: Smaller Value, will have more measurements
Flexible Anchoring with more chances for SgNB Addition
With the Periodic PCC Anchoring Switch, ScgAdditionInterval configured,
After NSA UE moves from Point 1 to 2 (Anchor Area), NSA UE will be able to handover to Point 3 and proceed SgNB Addition
Before that, without Periodic Switch, After NSA UE moves from Point 1 to 2 (Anchor Area) , NSA UE will not trigger handover to Anchor Cell.
5G

## Slide 125: 5G Baseline Parameter : MCG Carrier Management
Anchoring Handover Policy with consider if there is any NR Coverage
During initial 5G rollout, the NR Coverage might not be continuous , therefore there will have scenario that after NSA UE has handover to the Anchor Cell , UE might unable to perform SgNB Addition,
MML Object | Parameter ID | Default Value | G Baseline | Remarks
NsaDcMgmtConfig | NsaDcPccAnchoringPolicy | DEFAULT | BASED_ON_NR_COVERAGE | BASED_ON_NR_COVERAGE= During Anchoring Cell Selection, would also need to consider NR Coverage Condition To fulfil A5 (Anchor Cell)+ B1 (NR Cell), then only will handover to Anchor Cell • DEFAULT=To fulfil A1 (Current Serving Cell)+A5 (Anchor Cell), then only will handover to Anchor Cell
F1 with 20M
Non Anchor Cell
NSA Priority 0
PCC Priority 7
5G
F2 with 5M
Anchor Cell
NSA Priority 5
PCC Priority 5
2
If NSA UE is at the location with NR Coverage, then NSA PCC Anchoring handover will be triggered from Point 1 to 2
Otherwise, If NSA UE is at the location without NR Coverage, then NSA UE will
based on LTE CA PCC Priority to perform Anchoring Selection
This Policy will involves in Initial Access, Coverage Handover, Re establish, PCC Periodic Anchoring , SCG Release
1

## Slide 126: 5G Baseline Parameter : MCG Carrier Management
Page 9
MML Object | Parameter ID | Default Value | Remarks
CellMlbUeSel | NsaDcUeSelectionStrategy | LTE_NSA_DC_FAIR | Random Select either NSA UE or LTE Only UE to MLB
 |  | LTE_UE_PREFERRED | 1.LTE Only UE --> 2. UE has NSA Capability but yet to add SgNB --> 3.NSA UE
 |  | NSA_DC_UE_PREFERRED | 1. UE has NSA Capability --> LTE Only UE
MLB Options for NSA UE
NSA UE will only MLB within NSA PCC Anchoring Layer , will not MLB to Non Anchoring Layer
L26 F1/F2/F3
L23 F1/F2
SPID 256
Anchor Cell
Anchor Cell
Anchor Cell
SPID 4 SPID 256 SPID 1/2/3
P0
P0
P7 P7 P6
NSA UE
MLB Area
LTE UE
MLB Area
L21 F1
L18 F1
L7 F1

## Slide 127: 5G Baseline Parameter :
ge 10
Pa
LTE Side
MOD CELLQCIPARA: LocalCellId=1, Qci=7, NsaDcDefaultBearerMode=SCG_SPLIT_BEARER; MOD QCIPARA: Qci=7, NsaDcRlcPdcpParamGroupId=221;
MOD RLCPDCPPARAGROUP: RlcPdcpParaGroupId=221, RlcMode=RlcMode_AM, AmPdcpSnSize=AmPdcpSnsize_18bits;
NR Side
MOD NRCELLQCIBEARER: NrCellId=351, Qci=7, RlcMode=AM;
MOD GNBRLCPARAMGROUP: RlcParamGroupId=3, RlcMode=AM;
MOD GNBPDCPPARAMGROUP: PdcpParamGroupId=5, DlDataPdcpSplitMode=SCG_ONLY, DlPdcpSnSize=BITS18, UlPdcpSnSize=BITS18, UlDataSplitPrimaryPath=SCG,
UlDataSplitThreshold=INFINITY;
5G Project NSA Default QCI Bearer is 7
Parameter related to NSA Default Bearer would need to align at both LTE and NR Side, otherwise will unable to setup Data on NR.
** Alignment is done along with all the Data QCI that is currently use at G Project, which is 6,7,8,9 to prevent sudden QCI Bearer change on Core Side

## Slide 128: 5G Baseline Parameter : NR Single User and Multiple User MIMO
Page 11
MML Object | Parameter ID | Default Value | G Baseline
NRDUCELLALGOSWITCH | Dl256QamSwitch | OFF | ON
 | Ul256QamSwitch | UL_256QAM_OFF | UL_256QAM_FIXED *Version 19B is not recommended to ON
 | DL_SU_MULTI_LAYER_SW@SuMimoMultipleLayerSw | ON | ON
 | UL_SU_MULTI_LAYER_SW@SuMimoMultipleLayerSw | ON | ON
 | DL_MU_MIMO_SW@MuMimoSwitch | OFF | ON
 | UL_MU_MIMO_SW@MuMimoSwitch | OFF | ON
 | PDCCH_MU_SW@MuMimoSwitch | OFF | ON
NRDUCellPdsch | MaxMimoLayerNum | LAYER_DEFAULT | LAYER_16 (DL)
NRDUCELLPUSCH | MaxMimoLayerCnt | LAYER_2(2 Layers) | LAYER_8 (UL)
NRDUCELLPDCCH | MaxPairLayerNum | LAYER_2 | LAYER_2
** Ensure the related MIMO license are available
Key Parameters related to MIMO and for Throughput improvement

## Slide 129: NSA Baseline Parameter Checking
Type | Detail | Remarks | Parameter
 | LTE Anchor Performance Baseline Parameters | Checked the configuration parameters on the Anchor Side. | NsaDcAlgoSwitch @ NSA_DC_CAPABILITY_SWITCH-1&NSA_PCC_ANCHORING_SWITCH-1 PCCFREQCFG: PccDlEarfcn=1650, NsaPccAnchoringPriority=7; According to the strategy NSADCMGMTCONFIG: LocalCellId=111, NsaDcAlgoSwitch=NSA_DC_CAPABILITY_SWITCH- 1&NSA_PCC_ANCHORING_SWITCH-1&DlDataMcgSplitBearerMode=SCG_ONLY, NsaDcDefaultBearerMode=SCG_SPLIT_BEARER, UlDataSplitThreshold=INFINITY 4.CELLQCIPARA: LocalCellId=111, Qci=7, NsaDcDefaultBearerMode=SCG_SPLIT_BEARER; 5.RLCPDCPPARAGROUP: RlcPdcpParaGroupId=221, RlcMode=RlcMode_AM, AmPdcpSnSize=AmPdcpSnsize_18bits; 9.NRCELLQCIBEARER: NrCellId=351, Qci=6/7/8/9, RlcMode=AM;
Performance Baseline Parameters |  |  | NRDUCELLTRP: NrDuCellTrpId=401, TxRxMode=64T64R, MaxTransmitPower=295; NRDUCELL: NrDuCellId=401, DuplexMode=CELL_TDD, FrequencyBand=N78, SlotAssignment=8_2_DDDSUUDDDD, SlotStructure=SS818 GNODEBPARAM: FrameOffset=0 NRDUCELLALGOSWITCH: NrDuCellId=401, MuMimoSwitch=UL_MU_MIMO_SW-1&PDCCH_MU_SW- 1&DL_MU_MIMO_SW-1, Ul256QamSwitch=UL_256QAM_FIXED, (* UL 256 QAM for Version 19B is not recommended) SuMimoMultipleLayerSw=DL_SU_MULTI_LAYER_SW-1&UL_SU_MULTI_LAYER_SW-1, Dl256QamSwitch=ON; 5.NRCELLALGOSWITCH: NrCellId=401, NsaDcSwitch=ON, InterFreqHoSwitch=COVERAGE_BASED_HO-1; 6.NRDUCELLPDSCH: NrDuCellId=401, MaxMimoLayerNum=LAYER_16 7.NRDUCELLPUSCH: NrDuCellId=401, UlAdditionalDmrsPos=POS1, MaxMimoLayerCnt=LAYER_8 8.GNBPDCPPARAMGROUP: PdcpParamGroupId=5, DlDataPdcpSplitMode=SCG_ONLY, DlPdcpSnSize=BITS18, UlPdcpSnSize=BITS18, UlDataSplitPrimaryPath=SCG, UlDataSplitThreshold=INFINITY;
NR Performance Baseline Parameters |  | Checked the configuration parameters on the NR Side. | 
NSA 4G->5G Neighboring Cell & X2 |  | Check whether the NSA 4G->5G unidirectional neighboring cell is missing and whether the external cell consistency check is performed based on the topology. X2 interface configuration parameter check | PCC frequency configuration PCCFREQCFG: PccDlEarfcn=1650, NsaPccAnchoringPriority=7; According to the strategy NR neighboring frequency configuration NRNFREQ: LocalCellId=183, DlArfcn=638000; NR DC frequency configuration NRSCGFREQCONFIG: PccDlEarfcn=1650, ScgDlArfcn=638000; External cell configuration NREXTERNALCELL: Mcc="515", Mnc="02", GnodebId=834747, CellId=353, DlArfcn=638000, UlArfcnConfigInd=NOT_CFG, PhyCellId=290, Tac=50028; NR neighboring cell configuration NRNRELATIONSHIP: LOCALCELLID=183, Mcc="515", Mnc="02", GnodebId=834747, CellId=353; GLOBALPROCSWITCH: InterfaceSetupPolicySw=LTE_NR_X2_SON_SETUP_SW-1;
Neighboring Cell & X2 |  |  | 
NSA 4G<->4G neighboring cell |  | Check the missing neighboring cell configuration, invalid neighboring cell check, and external parameter consistency of the NSA 4G<->4G neighboring cell. | ANR
NSA 5G<->5G neighboring cell |  | Check the missing neighboring cell configuration, invalid neighboring cell check, and external parameter consistency of the 5G<->5G neighboring cell. | NREXTERNALNCELL: Mcc="515", Mnc="02", gNBId=837551, CellId=352, PhysicalCellId=174, RanNotificationAreaId=65535, Tac=50010, SsbFreqPos=638000; Page 12 NRCELLRELATION: NrCellId=352, Mcc="515", Mnc="02", gNBId=837551, CellId=352;
For NSA Parameter Checking, would require to check on Performance Baseline Parameter and Neighoring for both Anchoring and NR Sides

## Slide 130: NSA DC SgNB Evaluation for Service Integrity and Traffic
Category | KPI Name | KPI Formula
Availability | NR Cell Unavailable Duration (s) | N.Cell.Unavail.Dur.System + N.Cell.Unavail.Dur.Manual
Service Integrity | NR User DL Average Throughput (Mbps) | ((N.ThpVol.DL - N.ThpVol.DL.LastSlot)/N.ThpTime.DL.RmvLastSlot)*1000
Service Integrity | NR User UL Average Throughput (Mbps) | ((N.ThpVol.UL- N.ThpVol.UE.UL.SmallPkt)/N.ThpTime.UE.UL.RmvSmallPkt)*1000
Service Integrity | NR Cell DL Average Throughput (Mbps) | (N.ThpVol.DL.Cell/N.ThpTime.DL.Cell)*1000
Service Integrity | NR Cell UL Average Throughput (Mbps) | (N.ThpVol.UL.Cell/N.ThpTime.UL.Cell)*1000
Traffic | N.User.NsaDc.PSCell.Avg | N.User.NsaDc.PSCell.Avg
Traffic | N.User.RRCConn.Max | N.User.RRCConn.Max
Traffic | N.User.RRCConn.Avg | N.User.RRCConn.Avg
Traffic | NR DL Traffic Volume (GB) | (N.ThpVol.DL)/8/1024/1024
Traffic | NR UL Traffic Volume (GB) | (N.ThpVol.UL)/8/1024/1024
Traffic | NR Avg RRC DL Active User Number | N.User.RRCConn.Active.DL.Avg
Traffic | NR Max RRC DL Active User Number | N.User.RRCConn.Active.DL.Max
Traffic | NR Avg RRC UL Active User Number | N.User.RRCConn.Active.UL.Avg
Traffic | NR Max RRC UL Active User Number | N.User.RRCConn.Active.UL.Max
Traffic Volume for Data Split | NR Total DL Data Volume Split over X2 (Mbit) | N.PDCP.Vol.DL.X2U.TrfPDU.Tx /1000
Traffic Volume for Data Split | NR Total UL Data Volume Split Over X2 (Mbit) | N.PDCP.Vol.UL.X2U.TrfPDU.Rx/1000

## Slide 131: NSA DC SgNB Evaluation for Capacity
Resource Type | Resource Monitoring Indicator | Resource Meaning | KPI Formula
Cell | PRB Usage | Physical channel bandwidth over the air interface | NR DL PRB Utilization (%) =(N.PRB.DL.Used.Avg/N.PRB.DL.Avail.Avg）× 100% NR UL PRB Utilization (%)=(N.PRB.UL.Used.Avg/N.PRB.UL.Avail.Avg）× 100%
 | User Capacity Usage | Number of users in RRC_CONNECTED mode | NSA N.User.NsaDc.PSCell.Avg
 | PDCCH Resource Usage | PDCCH resources | CCE usage = N.CCE.Used.Avg/N.CCE.Avail.Avg x 100%
gNodeB | Paging Resource Usage | Paging capability of a gNodeB | NSA Paging messages are delivered through the LTE network. Therefore, the paging resource usage of the LTE network is used.
 | Main Control Board CPU Usage | Processing capability of the main control board of a gNodeB | Average CPU usage: VS.BBUBoard.CPULoad.Mean
 | BBP CPU Usage | Processing capability of the BBP of a gNodeB | Control-plane CPU usage Average control-plane CPU usage: VS.BBUBoard.CPULoad.Mean Percentage of times the control-plane CPU usage exceeds a preconfigured threshold: VS.BBUBoard.CPULoad.Over User-plane CPU usage Average user-plane CPU usage: VS.NRBoard.UPlane.CPULoad.Avg

## Slide 132: Module 4: Alarms and Troubleshooting

## Slide 133
What 3GPP Does Standardize: The Alarm Model
KPI Category | Common 3GPP probableCause Values
Accessibility | resourceUnavailable, underlyingResourceUnavailable, lossOfSignal, softwareError, configurationOrCustomizationError
Retainability | lossOfSignal (Radio Link Failure), linkFailure (Transport), qoSUnattainable, thresholdCrossed (e.g., high interference)
Mobility | linkFailure (for Xn interface), handoverFailure, configurationOrCustomizationError (Missing neighbor)
Throughput | thresholdCrossed (High Interference, High PRB usage), qoSUnattainable, degradedSignal, transmitFailure

## Slide 134
Alarms Affecting 5G NR Accessibility KPI
Alarm Group / Type | Specific Alarms from Your List (Examples) | Key MO Class(es) | Impact Explanation
Cell/Carrier Unavailability | Service Unavailable,MO Configuration Exceeds Resources...,Resource Configuration Failure,Configuration Requires Feature Activation,ESS Service Unavailable | NRCellDU | Direct Impact: The cell is not operational and cannot broadcast system information or respond to access requests. This is the most severe cause of accessibility failure.
Transport & Interface Failure | F1C Link to GNBCUCP Failure,GNBCUCP Service Unavailable,Default AMF PLMN Service Unavailable,XnC Link to GNodeB Failure (Impacts NSA setup) | GNBDUFunction,GNBCUCPFunction | Direct Impact: The gNB-DU cannot communicate with the gNB-CU, or the gNB-CU cannot communicate with the AMF in the core network. No new user sessions can be authenticated or set up.
Synchronization Failure | Synchronization Lost,Sync PTP Time Availability Fault,Radio Clock Service in Time Holdover Mode,Calendar Clock Misaligned | FieldReplaceableUnit,RadioEquipmentClock...,NRSynchronization | Direct Impact: A cell without a stable timing reference cannot transmit correctly or at all. It is effectively offline, leading to total accessibility failure for that cell.
Admission Control / Licensing | Licensed Capacity Exceeded,License Key Not Available,MO Configuration Exceeds Resources Enabled by the Key | FeatureState,NRCellDU | Direct Impact: The gNB is operational but actively rejects new users because a software or hardware capacity license limit has been reached.
Hardware Fault | No Connection,HW Fault,Missing SXU | FieldReplaceableUnit,PlugInModule | Direct Impact: The physical hardware (baseband or radio unit) required to operate the cell has failed. The cell cannot be brought into service.

## Slide 135
Alarms Affecting 5G NR Retainability KPI
Alarm Group / Type | Specific Alarms from Your List (Examples) | Key MO Class(es) | Impact Explanation
RF Quality & Interference | VSWR Over Threshold,RF Reflected Power High,PIM Desense Over Threshold | RfPort | Direct Impact: High VSWR indicates a problem with the antenna line (cable, connector, antenna). PIM is a form of self-interference. Both degrade the SINR, leading to radio link failures and dropped calls.
Hardware & RF Path Failures | HW Fault,HW Partial Fault<brLinearization Disturbance Performance Degraded,Link Failure / Link Degraded | FieldReplaceableUnit,RiLink (CPRI/eCPRI) | Direct Impact: A fault in the radio unit, baseband, or the optical link (RiLink) connecting them will cause instability or failure, immediately dropping all active sessions on that hardware.
Cell Restart / "Sleeping Cell" | Suspected Sleeping Cell,SW Error,System Restart Alert,Radio Restart Alert | EUtranCellFDD/TDD,NRCellDU,ManagedElement | Direct Impact: A "sleeping cell" transmits a signal but doesn't process user traffic, causing drops. A software error forcing a cell or node restart will drop all active connections.
Unstable Transport | Ethernet Link Failure (if flapping),Aggregated Ethernet Link Failure,IKE Peer Not Reachable (for IPsec) | EthernetPort,LagPort,Ikev2Session | Indirect Impact: An unstable or "flapping" backhaul connection causes high packet loss and latency. This makes the gNB lose contact with the UPF, causing timers to expire and sessions to be dropped.

## Slide 136
Alarms Affecting 5G NR Mobility KPI
Alarm Group / Type | Specific Alarms from Your List (Examples) | Key MO Class(es) | Impact Explanation
Inter-gNB Link (Xn) Failure | XnC Link to GNodeB Failure | GNBCUCPFunction | Direct Impact: This is the most critical alarm for inter-gNB mobility. The Xn control plane link between two gNBs is down, making handovers between them impossible.
Target Cell Unavailability | Service Unavailable,Resource Allocation Failure,Licensed Capacity Exceeded | NRCellDU (on the target cell) | Direct Impact: The source gNB commands a UE to hand over to a target cell that is down, locked, or has no free resources. The handover preparation or execution will fail.
Feature Incompatibility | Inter Node Feature Incompatibility,Inconsistent Configuration | ExternalENodeBFunction,NRCellDU | Indirect Impact: The source and target cells have conflicting feature sets or parameters, preventing a successful handover.
Inter-Node CA/DC Failure | Inter Node Carrier Aggregation Service Unavailable | ExtGNBDUPartnerFunction | Direct Impact: This specifically affects Dual Connectivity (EN-DC, NE-DC) or Inter-Node Carrier Aggregation setup, which is a form of mobility procedure. Failure to add the secondary cell impacts this KPI.

## Slide 137
Alarms Affecting 5G NR Throughput KPI
Alarm Group / Type | Specific Alarms from Your List (Examples) | Key MO Class(es) | Impact Explanation
RF Quality & Performance | VSWR Over Threshold,PIM Desense Over Threshold,Antenna Calibration DL/UL Failure,ESS Service Degraded | RfPort,NRSectorCarrier | Direct Impact: Poor RF quality (high reflections, interference) lowers the SINR. The gNB is forced to use a more robust but less efficient Modulation and Coding Scheme (MCS), which directly reduces data throughput. Failed calibration leads to suboptimal beamforming.
Resource & Feature Limitations | Carrier Control All Resources Allocated to Other RAT,Power Saving Capacity Limit Exceeded,Resource Allocation Failure Service Degraded | NRSectorCarrier,SectorCarrier | Direct Impact: Fewer resources (PRBs) are available for 5G users, either because they are shared with LTE or limited by power-saving features. This reduces the total cell throughput and the average user throughput.
Hardware Degradation | HW Partial Fault,Linearization Disturbance Performance Degraded,RX Diversity Lost | FieldReplaceableUnit,AntennaUnitGroup | Direct Impact: The hardware is not fully failed but is operating in a degraded state (e.g., reduced power, one of two RX paths failed). This shrinks the high-SINR, high-throughput coverage area of the cell. Loss of diversity is particularly harmful to UL throughput.
Transport Bottleneck | Ethernet Link Failure,Aggregated Ethernet Link Failure | EthernetPort,LagPort | Indirect Impact: If a gNB with multiple backhaul links loses one, the remaining link may become a bottleneck. The radio link may be capable of 2 Gbps, but if the backhaul is congested at 500 Mbps, user throughput will be capped.

## Slide 138: Thanks